## Slide 1
FULL FINDINGS · COMPREHENSIVE REFERENCE DECK
ArduPilot PNT (Positioning, Navigation, Timing) Reference Audit
Read-only static-analysis audit — every snippet reproduced verbatim from the cited path:line range
HEAD 5b67e27b0a · 43 pages · Read-only static-analysis catalog
Every catalogued finding, ordered by the audit’s own severity and category axes.

## Slide 2
TWO AXES, BOTH THE AUDIT’S OWN
How to read this deck
This deck is a communication layer over a finished audit: it selects nothing, scores nothing and omits nothing.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Axis | What orders it | Where the axis comes from
Severity | The audit’s five Audit-Discipline Flags, presented with the audit’s own stated occurrence counts, followed by the two touch-points the audit itself singles out in superlative risk language. | Audit-Discipline Flags, transcribed with its own footnote.
Category | The catalog’s own structure: GROUP 1 core references and GROUP 2 indirect / relational references across Positioning, Navigation and Timing, each main table followed by its paired Layer 1 and Layer 2 dependency map, then the instance mapping and the coverage register. | The audit’s own table numbering, unchanged.
THE FIDELITY RULE THIS DECK FOLLOWS
Every figure on every slide is a figure the audit itself states. Nothing is recomputed, re-scored or re-worded.
Every row keeps its own number, file path, line range, classification and the audit’s own Notes text, including its flag tokens and its [FIX F*] and AAP cross-references, exactly as printed.
Cited path:line ranges are transcribed, never re-derived: they are stated as of the audited HEAD 5b67e27b0a, the pre-refactor baseline.
Every column of every source table is carried, Code Snippet (5-10 lines) included: each cell’s source lines are set one paragraph per line, in the audit’s own order, with their indentation and their blank lines intact.

## Slide 3
EVERY FIGURE AS THE AUDIT STATES IT
The audit at a glance
The audit prints these totals on its own face; they reconcile against the rows that follow.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
THE AUDIT’S OWN FRONT-MATTER LINE
“Audited HEAD 5b67e27b0a · Core references: 63 · Indirect references: 31 · Total references: 94 · Evidence rows: 282 (main + Layer 1 + Layer 2)”
63
core references (Tables 1–3)
31
indirect references (Tables 4–6)
94
main rows catalogued
282
evidence rows in total
18
data objects
12
catalog tables in 6 groups
12
current → new mapping rows
109
coverage register entries

## Slide 4
LEGEND · THE AUDIT’S OWN CLASSIFICATION VOCABULARY
Legend
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Term | Meaning, as the audit defines it
Role (Group 1) | Source = produces/writes PNT state from a measurement ¦ Transform = fuses/derives/converts PNT state (EKF fusion, GPS blending, geodetic↔NED) ¦ Sink = only reads PNT state to drive control/behavior.
Group 2 columns | Trigger Condition (what invokes the code) ¦ PNT State Observed (the exact accessor/value read, e.g. gps.status(), ahrs.have_inertial_nav(), EKF variance) — the discriminator from Group 1 ¦ Behavior Change Description (how behavior changes).
Dependency Type (Layer 1) | Data dependency (shared data value/struct field) ¦ Function call (direct call) ¦ Inheritance / Interface (backend overrides a virtual frontend interface) ¦ Shared global / singleton (access via an AP:: accessor — AP::gps(), AP::ahrs(), AP::scheduler(), AP::rtc()).
Notes flags | [CIRCULAR] circular dependency (e.g. AHRS↔EKF) ¦ [SHARED-STRUCT] PNT fields packed with non-PNT fields (extraction risk) ¦ [DUPLICATED] copy-pasted PNT logic across locations ¦ [MULTI-CATEGORY] spans >1 PNT category (emitted once per table) ¦ [ABSENT] expected PNT element not found where checked.
Cross-reference | Each main table owns a monotonic, per-table # space (1,2,3…). Its dependency sub-table (the matching Xa table) reuses those exact numbers as Ref #. Each Xa table contains a Layer 1 block (direct edges) followed by a Layer 2 block (full transitive chain + final consumer + Chain Depth = the number of → hops explicitly listed in that chain).
Chain Depth follows the same convention throughout: the number of → hops explicitly listed in that chain.

## Slide 5
SCOPE AND LINE-NUMBER BASIS, VERBATIM
Scope of the catalog
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
SCOPE
Scope. This document is an audit-grade, read-only static-analysis catalog of every location in the ArduPilot firmware codebase (repository root containing ArduCopter/, ArduPlane/, Rover/, ArduSub/, AntennaTracker/, Blimp/, libraries/, modules/) where Positioning, Navigation, and Timing (PNT) data is handled, together with a two-layer dependency map for every catalogued reference. GROUP 1 catalogs core references — code that directly implements, reads, writes, or processes PNT data. GROUP 2 catalogs indirect / relational references — code that does not directly read or write PNT data but whose behavior changes as a result of PNT state. All file paths are repository-root-relative; every code snippet is reproduced VERBATIM from the cited path and line range so each row is independently verifiable. No source file is modified by this audit.
LINE-NUMBER BASIS, AS PRINTED ON THE AUDIT’S FIRST PAGE
“Line-number basis: every cited path:line range in this document is stated as of the audited HEAD 5b67e27b0a (the pre-refactor baseline). The reusable-service extraction adds one additive, default-off set_update_dt timing seam to AP_L1_Control.cpp / .h after that commit; that seam relocates no behavior and only shifts those two files' line numbers, so the numbers here are intentionally not post-seam current-source lines.”

## Slide 6
THE SURVEYED SURFACE
Footprint Summary
The surface swept to make the catalog exhaustive, in the audit’s own words and figures.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Footprint surveyed: libraries/ = 151 subsystems; libraries/AP_GPS/*.{cpp,h} = 44 files (14 receiver backends each catalogued individually + AP_GPS_Blended + GPS_Backend base); EKF families AP_NavEKF/AP_NavEKF2/AP_NavEKF3 with AP_NavEKF3 split across 13 fusion modules (all catalogued); flight/drive-mode files = 81 (ArduCopter 29 + ArduPlane 26 + Rover 14 + ArduSub 12), enumerated in the Coverage & Explicit-Absence Register. PNT state is produced under libraries/ and consumed/acted-upon in vehicle glue code (failsafe, ekf_check, fence, flight-mode gating).
151
subsystems in libraries/
44
AP_GPS files
14
receiver backends
13
EKF3 fusion modules
81
flight / drive-mode files

## Slide 7
EXECUTIVE SUMMARY · AS THE AUDIT OPENS
Project overview and the core problem addressed
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
“This Executive Summary opens the audit and states up front what the catalog behind it establishes: where every Positioning, Navigation and Timing behavior in the ArduPilot firmware lives today, what depends on it, and — for the L1 lateral-navigation slice — which member of the reusable AfsimL1Behavior service each behavior is refactored into. It is a reading aid: the numbered tables, the instance mapping and the registers that follow remain the authoritative record.”
PROJECT OVERVIEW
This deliverable is an audit-grade, read-only static-analysis catalog of every location in the ArduPilot firmware codebase where Positioning, Navigation and Timing (PNT) data is handled, taken at audited HEAD 5b67e27b0a. Every catalogued reference reproduces the code at its cited path:line range verbatim and carries a two-layer dependency map: Layer 1 records the direct callers, callees and typed data edges around the reference, and Layer 2 records the full transitive chain through to the final consumer that acts on the value.
The catalog is extended with a current-location → new-service-location mapping. For every PNT touch-point inside the wrapped L1 guidance controller it names the member of the reusable AfsimL1Behavior service that the behavior is refactored into: the AHRS state shim that supplies injected position, velocity and attitude, the injected-dt timing seam that replaces the internal hardware clock, and the extern "C" command surface that returns the roll and lateral-acceleration commands. No source file is modified by this audit.

## Slide 8
EXECUTIVE SUMMARY · AS THE AUDIT OPENS
Project overview and the core problem addressed (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
CORE PROBLEM ADDRESSED
PNT behavior in ArduPilot is not a library that a host can call — it is embedded in the vehicle flight loop and duplicated across vehicles. Position, velocity, attitude and the control-step timebase are pulled implicitly from shared AHRS/EKF state and the hardware clock; PNT values arrive packed into structures alongside non-PNT fields; and the same derivation is repeated across the vehicle glue code. The catalog records that coupling directly: [SHARED-STRUCT] marks the packed structures, [DUPLICATED] marks the repeated derivations, and [CIRCULAR] marks the state that depends on itself.
The consequence is that an external host cannot reuse a PNT behavior without first knowing every place that behavior lives, what it reads, and what breaks if it moves. This audit establishes exactly that ground truth — an enumerated, independently verifiable inventory of every PNT touch-point together with its dependency neighbourhood — and, for the L1-navigation slice, names the service member each behavior moves to, so the extraction can be reviewed as a mapping between named locations rather than as a rewrite.

## Slide 9
STAKEHOLDER ROUTING · THE AUDIT’S OWN AUDIENCES
Key Stakeholders and Users
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Integration and host engineers embedding the extracted guidance service use the current → new service location mapping as the wiring contract: it names, accessor by accessor, the value the host must inject and the service member that now supplies it. Flight-controls reviewers signing off the guidance seam use the Core Navigation and Core Timing tables, with their paired dependency sub-tables, to confirm that nothing outside the audited seam observes the values being injected.
Firmware maintainers auditing PNT coupling use the audit-discipline flags to locate circular state, shared structures and duplicated derivations before touching shared state, and the Coverage & Explicit-Absence Register to see which surfaces were swept and found clear. Reviewers and auditors rely on the read-only guarantee and on the verbatim path:line citations, which make every row independently checkable against the tree at the audited HEAD rather than something that has to be taken on trust.

## Slide 10
STAKEHOLDER ROUTING · WHICH PART CARRIES WHAT
Which part of this deck each audience needs
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Audience the audit names | What they use | Where it is in this deck
Integration and host engineers | The current → new service location mapping, as the wiring contract: accessor by accessor, the value the host must inject and the service member that now supplies it. | Part 11 · PNT Instance Audit
Flight-controls reviewers | Core Navigation and Core Timing with their paired dependency sub-tables, to confirm that nothing outside the audited seam observes the values being injected. | Parts 5 and 6 · Core Navigation, Core Timing
Firmware maintainers | The audit-discipline flags, to locate circular state, shared structures and duplicated derivations before touching shared state, and the Coverage & Explicit-Absence Register to see which surfaces were swept and found clear. | Part 3 · severity axis; Part 12 · coverage register
Reviewers and auditors | The read-only guarantee and the verbatim path:line citations, which make every row independently checkable against the tree at the audited HEAD rather than something that has to be taken on trust. | Part 13 · provenance and reconciliation

## Slide 11
KEY FINDINGS AT A GLANCE · EVERY FIGURE AS STATED
Key Findings at a Glance
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Every figure below is a reconciled total of the catalog itself, carried forward unchanged from the tables, the instance mapping and the registers that follow.
Dimension | Value | What the Catalog Establishes | Where It Is Catalogued
Core PNT references | 63 | Code that directly implements, reads, writes or processes PNT data. | GROUP 1 — CORE PNT REFERENCES: Table 1 Core Positioning, Table 2 Core Navigation, Table 3 Core Timing, each with its 1a / 2a / 3a dependency map.
Indirect / relational PNT references | 31 | Code that reads no PNT data itself but whose behavior changes as a result of PNT state. | GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES: Table 4 Indirect Positioning, Table 5 Indirect Navigation, Table 6 Indirect Timing, each with its 4a / 5a / 6a dependency map.
Total catalogued touch-points | 94 | Core plus indirect — the complete PNT surface enumerated by this audit. | All GROUP 1 and GROUP 2 main tables.
Evidence rows | 282 | 94 touch-points × 3 layers: the main row, its Layer 1 direct edges and its Layer 2 transitive chain. | Each main table together with its matching Xa dependency sub-table.
Data objects | 18 | Catalogued table objects: 6 main tables plus their 6 Layer 1 and 6 Layer 2 blocks. | Tables 1 / 1a through 6 / 6a.
Catalog structure | 12 | Tables in 6 numbered groups: 6 main tables, each paired with an Xa sub-table holding its Layer 1 and Layer 2 blocks. | Tables 1 / 1a through 6 / 6a, rendered in that order.

## Slide 12
KEY FINDINGS AT A GLANCE · EVERY FIGURE AS STATED
Key Findings at a Glance (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Dimension | Value | What the Catalog Establishes | Where It Is Catalogued
Audit-discipline flags | 5 | Flag kinds, with occurrences [CIRCULAR] 8 · [SHARED-STRUCT] 19 · [DUPLICATED] 36 · [MULTI-CATEGORY] 7 · [ABSENT] 30. They mark extraction risk and enforce non-inference discipline inline in the Notes columns. | Notes columns throughout; taxonomy and occurrence counts in Audit-Discipline Flags.
Coverage and explicit absences | 109 | Register entries across 10 sub-registers, including 27 checked, explicitly documented absences — evidence that the sweep was exhaustive rather than opportunistic. | Coverage & Explicit-Absence Register.
Current → new service mapping | 12 | L1-navigation touch-points mapped onto the AfsimL1Behavior member each is refactored into, spanning position, velocity, attitude, airspeed scaling, timing, geometry and the command outputs. | PNT Instance Audit — Current Location → New Service Location.

## Slide 13
EXECUTIVE SUMMARY · WHAT THE CATALOG IS FOR
Expected Impact and Value Proposition
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
The audit converts an implicit understanding of ArduPilot PNT coupling into a verifiable extraction baseline. Because every row cites a path:line range and reproduces the code at that range verbatim, the inventory can be re-checked against the tree at audited HEAD 5b67e27b0a rather than taken on trust, and the totals above reconcile against the catalog they summarise.
The audit-discipline flags turn extraction risk into explicit, addressable markers — where state is circular, where PNT fields are packed with non-PNT fields, where a derivation is duplicated, and, through the checked absences, where an expected PNT element was looked for and genuinely is not present. For the L1-navigation slice the current → new mapping supplies a documented wiring contract for the reusable service, so the guidance seam can be reviewed and signed off against named locations on both sides of the extraction.

## Slide 14
DOCUMENT ROADMAP · THE AUDIT’S OWN READING ORDER
Document Roadmap / How to Read This Document
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
The sections below appear in this order. Section names, table numbers and row numbering are exactly as catalogued.
Section, as catalogued | What it contains
Legend | The classification vocabularies — Role for Group 1, the Trigger Condition / PNT State Observed / Behavior Change discriminators for Group 2, Dependency Type for Layer 1 — plus the Notes-flag meanings and the cross-reference rule that ties each Xa table back to its main table numbering. Read this first.
Footprint Summary | The surveyed surface: the subsystems, receiver backends, EKF families and flight-mode files swept to make the catalog exhaustive.
GROUP 1 — CORE PNT REFERENCES | Tables 1 / 1a Core Positioning, 2 / 2a Core Navigation and 3 / 3a Core Timing: code that directly implements, reads, writes or processes PNT data. Table 2 also carries the New Service Location column.
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES | Tables 4 / 4a Indirect Positioning, 5 / 5a Indirect Navigation and 6 / 6a Indirect Timing: code whose behavior changes as a result of PNT state.
PNT Instance Audit — Current Location → New Service Location | The consolidated mapping of every PNT touch-point inside the wrapped L1 controller onto its AfsimL1Behavior member, with the line-number basis stated alongside it.
Audit-Discipline Flags | The flag taxonomy with its occurrence counts, reconciled against the catalog.
Coverage & Explicit-Absence Register | The directory-wide token sweeps and checked absences that establish exhaustiveness across libraries/, the vehicle directories and the submodule boundary edges.

## Slide 15
Severity axis
The audit’s own Audit-Discipline Flags, with its own stated occurrence counts. No new scale is introduced.

## Slide 16
AUDIT-DISCIPLINE FLAGS · 5 KINDS, CATALOG-WIDE
Audit-Discipline Flags
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Extraction-risk and non-inference discipline markers applied inline in the Notes columns throughout the catalog. Each occurrence figure is the audit’s own count of that token across its whole annotation corpus: the Notes of every main row and every Layer 2 chain, the Legend entry that defines the flag and, for [ABSENT], the Coverage register’s checked absences.
Flag | Occurrences | Meaning
[CIRCULAR] | 8 | Circular dependency (e.g. AHRS ↔ EKF).
[SHARED-STRUCT] | 19 | PNT fields packed with non-PNT fields (extraction risk).
[DUPLICATED] | 36 | Same PNT value read/derived in multiple places.
[MULTI-CATEGORY] | 7 | Touch-point spans more than one PNT pillar.
[ABSENT] | 30 | A checked, explicitly-documented absence (non-inference discipline).
Explicitly-documented absences catalogued in the Coverage register: 27.

## Slide 17
SEVERITY AXIS · [SHARED-STRUCT]
Flag [SHARED-STRUCT] – where it is applied
PNT fields packed with non-PNT fields (extraction risk).
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Occurrences catalog-wide, as the audit states them: 19 · [SHARED-STRUCT] marks the packed structures
Catalogued at | File Path | Line(s) | Function / Class | Notes flags on the row
Table 1 #1 | libraries/AP_GPS/AP_GPS_UBLOX.cpp | 1510-1518 | AP_GPS_UBLOX::_parse_gps()(NAV-POSLLH) | [SHARED-STRUCT]
Table 1 #2 | libraries/AP_GPS/AP_GPS_NMEA.cpp | 333-340 | AP_GPS_NMEA::_term_complete() | [SHARED-STRUCT]
Table 1 #3 | libraries/AP_GPS/AP_GPS_SBF.cpp | 484-491 | AP_GPS_SBF::process_message() | [SHARED-STRUCT]
Table 1 #4 | libraries/AP_GPS/AP_GPS_NOVA.cpp | 209-216 | AP_GPS_NOVA::process_message() | [SHARED-STRUCT]
Table 1 #5 | libraries/AP_GPS/AP_GPS_SBP.cpp | 276-283 | AP_GPS_SBP::_attempt_state_update() | [SHARED-STRUCT]
Table 1 #6 | libraries/AP_GPS/AP_GPS_SBP2.cpp | 328-335 | AP_GPS_SBP2::_attempt_state_update() | [SHARED-STRUCT]
Table 1 #7 | libraries/AP_GPS/AP_GPS_SIRF.cpp | 178-185 | AP_GPS_SIRF::_parse_gps() | [SHARED-STRUCT]
Table 1 #8 | libraries/AP_GPS/AP_GPS_ERB.cpp | 150-157 | AP_GPS_ERB::_parse_gps() | [SHARED-STRUCT]
Table 1 #9 | libraries/AP_GPS/AP_GPS_MAV.cpp | 67-75 | AP_GPS_MAV::handle_msg() | [SHARED-STRUCT]
Every main-table row the flag is applied to, in catalog order. Each row’s full Notes text is carried at the row itself, in the category part for its table. The catalog-wide figure above counts the token across the whole annotation corpus stated with the taxonomy, not the rows listed here.

## Slide 18
SEVERITY AXIS · [SHARED-STRUCT]
Flag [SHARED-STRUCT] (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Catalogued at | File Path | Line(s) | Function / Class | Notes flags on the row
Table 1 #10 | libraries/AP_GPS/AP_GPS_MSP.cpp | 44-51 | AP_GPS_MSP::handle_msp() | [SHARED-STRUCT]
Table 1 #11 | libraries/AP_GPS/AP_GPS_GSOF.cpp | 231-238 | AP_GPS_GSOF::pack_state_data() | [SHARED-STRUCT]
Table 1 #12 | libraries/AP_GPS/AP_GPS_DroneCAN.cpp | 388-396 | AP_GPS_DroneCAN::handle_fix2_msg() | [SHARED-STRUCT]
Table 1 #13 | libraries/AP_GPS/AP_GPS_ExternalAHRS.cpp | 49-56 | AP_GPS_ExternalAHRS::handle_external() | [SHARED-STRUCT]
Table 1 #14 | libraries/AP_GPS/AP_GPS_SITL.cpp | 86-93 | AP_GPS_SITL::read() | [SHARED-STRUCT]
Table 1 #18 | libraries/AP_GPS/AP_GPS.h | 192-201 | structAP_GPS::GPS_State | [SHARED-STRUCT] [MULTI-CATEGORY]
Table 1 #20 | libraries/AP_Common/Location.h | 11-20 | classLocation | [SHARED-STRUCT]
Every main-table row the flag is applied to, in catalog order. Each row’s full Notes text is carried at the row itself, in the category part for its table. The catalog-wide figure above counts the token across the whole annotation corpus stated with the taxonomy, not the rows listed here.

## Slide 19
SEVERITY AXIS · [SHARED-STRUCT]
Flag [SHARED-STRUCT] in the Layer 2 chains
Layer 2 chain rows the flag is applied to, with the audit’s own Chain Depth.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Catalogued at | PNT Origin | Final Consumer | Chain Depth | Notes flags on the row
Table 1a #18 | GPS_State (struct) | AP_Motors and AP_RTC | 4 | [SHARED-STRUCT] [MULTI-CATEGORY]
Table 1a #20 | class Location (geodetic value type) | AP_Motors | 5 | [SHARED-STRUCT]

## Slide 20
SEVERITY AXIS · [DUPLICATED]
Flag [DUPLICATED] – where it is applied
Same PNT value read/derived in multiple places.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Occurrences catalog-wide, as the audit states them: 36 · [DUPLICATED] marks the repeated derivations
Catalogued at | File Path | Line(s) | Function / Class | Notes flags on the row
Table 2 #20 | libraries/AP_NavEKF2/AP_NavEKF2_core.cpp | 528-536 | NavEKF2_core::UpdateFilter() | [CIRCULAR] [DUPLICATED]
Table 2 #21 | libraries/AP_NavEKF2/AP_NavEKF2_PosVelFusion.cpp | 560-568 | NavEKF2_core::FuseVelPosNED() | [DUPLICATED]
Table 4 #3 | ArduCopter/fence.cpp | 20-28 | Copter::fence_checks_async() | [DUPLICATED]
Table 4 #9 | Rover/fence.cpp | 17-25 | Rover::fence_checks_async() | [DUPLICATED]
Table 4 #10 | ArduPlane/takeoff.cpp | 58-62 | Plane::auto_takeoff_check() | [DUPLICATED]
Table 5 #1 | ArduCopter/ekf_check.cpp | 117-125 | Copter::ekf_over_threshold() | [DUPLICATED]
Table 5 #2 | ArduPlane/ekf_check.cpp | 56-65 | Plane::ekf_check() | [DUPLICATED]
Table 5 #3 | Rover/ekf_check.cpp | 93-102 | Rover::ekf_over_threshold() | [DUPLICATED]
Every main-table row the flag is applied to, in catalog order. Each row’s full Notes text is carried at the row itself, in the category part for its table. The catalog-wide figure above counts the token across the whole annotation corpus stated with the taxonomy, not the rows listed here.

## Slide 21
SEVERITY AXIS · [DUPLICATED]
Flag [DUPLICATED] (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Catalogued at | File Path | Line(s) | Function / Class | Notes flags on the row
Table 5 #4 | ArduSub/failsafe.cpp | 112-121 | Sub::failsafe_ekf_check() | [DUPLICATED]
Table 6 #1 | ArduCopter/failsafe.cpp | 37-45 | Copter::failsafe_check() | [DUPLICATED]
Table 6 #2 | ArduPlane/failsafe.cpp | 22-30 | Plane::failsafe_check() | [DUPLICATED]
Table 6 #3 | Rover/failsafe.cpp | 22-30 | Rover::failsafe_check() | [DUPLICATED]
Table 6 #4 | ArduSub/failsafe.cpp | 31-39 | Sub::mainloop_failsafe_check() | [DUPLICATED]
Table 6 #5 | Blimp/failsafe.cpp | 37-45 | Blimp::failsafe_check() | [DUPLICATED]
Table 6 #6 | ArduCopter/ekf_check.cpp | 84-88 | Copter::ekf_check() — GCS warn throttle | [DUPLICATED]
Table 6 #7 | ArduPlane/ekf_check.cpp | 78-82 | Plane::ekf_check() — GCS warn throttle | [DUPLICATED]
Table 6 #10 | ArduCopter/fence.cpp | 8-16 | Copter::fence_checks_async() | [DUPLICATED]
Table 6 #11 | Rover/fence.cpp | 6-14 | Rover::fence_checks_async() | [DUPLICATED]
Every main-table row the flag is applied to, in catalog order. Each row’s full Notes text is carried at the row itself, in the category part for its table. The catalog-wide figure above counts the token across the whole annotation corpus stated with the taxonomy, not the rows listed here.

## Slide 22
SEVERITY AXIS · [DUPLICATED]
Flag [DUPLICATED] in the Layer 2 chains
Layer 2 chain rows the flag is applied to, with the audit’s own Chain Depth.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Catalogued at | PNT Origin | Final Consumer | Chain Depth | Notes flags on the row
Table 2a #20 | NavEKF2_core::UpdateFilter() | AP_Motors | 3 | [CIRCULAR] [DUPLICATED]
Table 2a #21 | NavEKF2_core::FuseVelPosNED() | AP_AHRS | 3 | [DUPLICATED]
Table 4a #3 | AP_AHRS vehicle position (via AC_Fence) | Copter fence failsafe (RTL/LAND) | 4 | [DUPLICATED]
Table 4a #9 | AP_AHRS vehicle position (via AC_Fence) | Rover fence failsafe | 4 | [DUPLICATED]
Table 5a #1 | EKF variances (via AP_AHRS) | EKF failsafe action (LAND) | 5 | [DUPLICATED]
Table 5a #2 | EKF variances (Plane) | Plane EKF failsafe | 4 | [DUPLICATED]
Table 5a #3 | EKF variances (Rover) | Rover EKF failsafe | 3 | [DUPLICATED]
Table 5a #4 | EKF variances (Sub) | Sub EKF failsafe flag | 3 | [DUPLICATED]
Table 6a #1 | AP_HAL::micros() + AP_Scheduler tick counter | AP_Motors (motor min / disarm) | 3 | [DUPLICATED]
Table 6a #2 | AP_HAL::micros() + AP_Scheduler tick counter | SRV_Channels (RC passthrough) | 4 | [DUPLICATED]
Table 6a #3 | AP_HAL::micros() + AP_Scheduler tick counter | AP_Arming (disarm) | 3 | [DUPLICATED]
Table 6a #4 | AP_HAL::micros() + AP_Scheduler tick counter | AP_Motors (motor min) | 3 | [DUPLICATED]

## Slide 23
SEVERITY AXIS · [DUPLICATED]
Flag [DUPLICATED] in the Layer 2 chains (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Catalogued at | PNT Origin | Final Consumer | Chain Depth | Notes flags on the row
Table 6a #5 | AP_HAL::micros() + AP_Scheduler tick counter | AP_Motors (motor min) | 3 | [DUPLICATED]
Table 6a #6 | AP_HAL::millis() wall clock | GCS_MAVLINK (telemetry text) | 3 | [DUPLICATED]
Table 6a #7 | AP_HAL::millis() wall clock | GCS_MAVLINK (telemetry text) | 3 | [DUPLICATED]
Table 6a #10 | AP_HAL::millis() wall clock | AC_Fence / fence failsafe | 5 | [DUPLICATED]
Table 6a #11 | AP_HAL::millis() wall clock | AC_Fence / fence failsafe | 4 | [DUPLICATED]

## Slide 24
SEVERITY AXIS · [CIRCULAR]
Flag [CIRCULAR] – where it is applied
Circular dependency (e.g. AHRS ↔ EKF).
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Occurrences catalog-wide, as the audit states them: 8 · [CIRCULAR] marks the state that depends on itself
Catalogued at | File Path | Line(s) | Function / Class | Notes flags on the row
Table 2 #1 | libraries/AP_AHRS/AP_AHRS.cpp | 3600-3604 | AP_AHRS::get_location() | [CIRCULAR]
Table 2 #6 | libraries/AP_NavEKF3/AP_NavEKF3_core.cpp | 627-636 | NavEKF3_core::UpdateFilter() | [CIRCULAR]
Table 2 #7 | libraries/AP_NavEKF3/AP_NavEKF3_PosVelFusion.cpp | 502-511 | NavEKF3_core::SelectVelPosFusion() | [CIRCULAR]
Table 2 #9 | libraries/AP_NavEKF3/AP_NavEKF3_Measurements.cpp | 559-567 | NavEKF3_core::readGpsData() | [CIRCULAR]
Table 2 #20 | libraries/AP_NavEKF2/AP_NavEKF2_core.cpp | 528-536 | NavEKF2_core::UpdateFilter() | [CIRCULAR] [DUPLICATED]
Every main-table row the flag is applied to, in catalog order. Each row’s full Notes text is carried at the row itself, in the category part for its table. The catalog-wide figure above counts the token across the whole annotation corpus stated with the taxonomy, not the rows listed here.

## Slide 25
SEVERITY AXIS · [CIRCULAR]
Flag [CIRCULAR] in the Layer 2 chains
Layer 2 chain rows the flag is applied to, with the audit’s own Chain Depth.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Catalogued at | PNT Origin | Final Consumer | Chain Depth | Notes flags on the row
Table 2a #6 | NavEKF3_core::UpdateFilter() | AP_Motors | 3 | [CIRCULAR]
Table 2a #20 | NavEKF2_core::UpdateFilter() | AP_Motors | 3 | [CIRCULAR] [DUPLICATED]

## Slide 26
SEVERITY AXIS · [MULTI-CATEGORY]
Flag [MULTI-CATEGORY] – where it is applied
Touch-point spans more than one PNT pillar.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Occurrences catalog-wide, as the audit states them: 7 · Touch-point spans more than one PNT pillar.
Catalogued at | File Path | Line(s) | Function / Class | Notes flags on the row
Table 1 #17 | libraries/AP_GPS/AP_GPS.h | 360-365 | AP_GPS::velocity() | [MULTI-CATEGORY]
Table 1 #18 | libraries/AP_GPS/AP_GPS.h | 192-201 | structAP_GPS::GPS_State | [SHARED-STRUCT] [MULTI-CATEGORY]
Table 3 #8 | libraries/AP_GPS/AP_GPS.h | 409-418 | AP_GPS::time_week_ms()/time_week() | [MULTI-CATEGORY]
Every main-table row the flag is applied to, in catalog order. Each row’s full Notes text is carried at the row itself, in the category part for its table. The catalog-wide figure above counts the token across the whole annotation corpus stated with the taxonomy, not the rows listed here.

## Slide 27
SEVERITY AXIS · [MULTI-CATEGORY]
Flag [MULTI-CATEGORY] in the Layer 2 chains
Layer 2 chain rows the flag is applied to, with the audit’s own Chain Depth.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Catalogued at | PNT Origin | Final Consumer | Chain Depth | Notes flags on the row
Table 1a #15 | GPS velocity (fill_3d_velocity) | AP_Motors | 6 | [MULTI-CATEGORY]
Table 1a #18 | GPS_State (struct) | AP_Motors and AP_RTC | 4 | [SHARED-STRUCT] [MULTI-CATEGORY]
Table 3a #8 | GPS receiver (time-of-week) | EKF GPS-time / UTC conversion | 4 | [MULTI-CATEGORY]

## Slide 28
SEVERITY AXIS · [ABSENT]
Flag [ABSENT] – where it is applied
A checked, explicitly-documented absence (non-inference discipline).
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Occurrences catalog-wide, as the audit states them: 30 · where an expected PNT element was looked for and genuinely is not present
Catalogued at | File Path | Line(s) | Function / Class | Notes flags on the row
Table 1 #23 | libraries/AC_AttitudeControl/AC_PosControl.cpp | 363-372 | AC_PosControl::input_pos_NEU_cm() | [ABSENT]
Every main-table row the flag is applied to, in catalog order. Each row’s full Notes text is carried at the row itself, in the category part for its table. The catalog-wide figure above counts the token across the whole annotation corpus stated with the taxonomy, not the rows listed here.

## Slide 29
SEVERITY AXIS · [ABSENT]
Flag [ABSENT] in the Layer 2 chains
Layer 2 chain rows the flag is applied to, with the audit’s own Chain Depth.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Catalogued at | PNT Origin | Final Consumer | Chain Depth | Notes flags on the row
Table 4a #8 | (no PNT — GPS-independent) | AP_Motors | 3 | [ABSENT]

## Slide 30
SEVERITY AXIS · [ABSENT]
Flag [ABSENT] – the checked absences
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
THE AUDIT’S OWN FOOTNOTE TO THE FLAGS TABLE
“Explicitly-documented absences catalogued in the Coverage register: 27.”
WHERE THEY ARE CATALOGUED
The checked absences are catalogued entry by entry in the Coverage & Explicit-Absence Register, which is carried in full in Part 12 of this deck: each one names the surface that was swept, what was looked for, and the evidence that it is not present.
THE DISCIPLINE THE FLAG ENFORCES
“A checked, explicitly-documented absence (non-inference discipline).”

## Slide 31
SEVERITY AXIS · THE TWO NAMED TOP RISKS
The two touch-points the audit itself singles out
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
The audit applies superlative risk language to exactly two catalogued touch-points. Both are quoted here in full, as printed.
Table 1 #18 · libraries/AP_GPS/AP_GPS.h 192-201 structAP_GPS::GPS_State
“[SHARED-STRUCT] [MULTI-CATEGORY] One struct mixes Positioning (location), Navigation (velocity, ground_speed, ground_course) and Timing (time_week_ms, time_week) — see Table 3 #8. Primary extraction-risk struct for a PNT split.”
Table 1 #20 · libraries/AP_Common/Location.h 11-20 classLocation
“[SHARED-STRUCT] Geodetic PNT fields lat/lng (1E7 deg) and alt (cm) packed with NON-PNT bitfields relative_alt, loiter_ccw, terrain_alt, origin_alt, loiter_xtrack. Ubiquitous value type; top extraction risk.”

## Slide 32
Table 1 — Core Positioning
Where PNT is born: receiver backends, the shared state struct and the location value type.

## Slide 33
GROUP 1 — CORE PNT REFERENCES · CORE POSITIONING
Table 1 — Core Positioning
All 26 catalogued rows, with every Notes annotation, flag token and cited path:line range exactly as printed.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | File Path | Line(s) | Function/Class | Role | Notes
1 | libraries/AP_GPS/AP_GPS_UBLOX.cpp | 1510-1518 | AP_GPS_UBLOX::_parse_gps()(NAV-POSLLH) | Source | [SHARED-STRUCT] Receiver backend writes GPS_State.location/status from the u-blox UBX binary NAV-POSLLH. One of 14 receiver backends, each catalogued individually. target GPS_State.
2 | libraries/AP_GPS/AP_GPS_NMEA.cpp | 333-340 | AP_GPS_NMEA::_term_complete() | Source | [SHARED-STRUCT] Receiver backend writes GPS_State.location/status from the NMEA-0183 ASCII (GGA/RMC) sentence. One of 14 receiver backends, each catalogued individually. target GPS_State.
3 | libraries/AP_GPS/AP_GPS_SBF.cpp | 484-491 | AP_GPS_SBF::process_message() | Source | [SHARED-STRUCT] Receiver backend writes GPS_State.location/status from the Septentrio SBF binary PVTGeodetic. One of 14 receiver backends, each catalogued individually. target GPS_State.
4 | libraries/AP_GPS/AP_GPS_NOVA.cpp | 209-216 | AP_GPS_NOVA::process_message() | Source | [SHARED-STRUCT] Receiver backend writes GPS_State.location/status from the NovAtel OEM BESTPOS. One of 14 receiver backends, each catalogued individually. target GPS_State.
5 | libraries/AP_GPS/AP_GPS_SBP.cpp | 276-283 | AP_GPS_SBP::_attempt_state_update() | Source | [SHARED-STRUCT] Receiver backend writes GPS_State.location/status from the Swift Navigation SBP v1 POS_LLH. One of 14 receiver backends, each catalogued individually. target GPS_State.
# 1–5

## Slide 34
GROUP 1 — CORE PNT REFERENCES · CORE POSITIONING
Table 1 — Core Positioning (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | File Path | Line(s) | Function/Class | Role | Notes
6 | libraries/AP_GPS/AP_GPS_SBP2.cpp | 328-335 | AP_GPS_SBP2::_attempt_state_update() | Source | [SHARED-STRUCT] Receiver backend writes GPS_State.location/status from the Swift Navigation SBP v2 POS_LLH. One of 14 receiver backends, each catalogued individually. target GPS_State.
7 | libraries/AP_GPS/AP_GPS_SIRF.cpp | 178-185 | AP_GPS_SIRF::_parse_gps() | Source | [SHARED-STRUCT] Receiver backend writes GPS_State.location/status from the SiRF binary geodetic navigation. One of 14 receiver backends, each catalogued individually. target GPS_State.
8 | libraries/AP_GPS/AP_GPS_ERB.cpp | 150-157 | AP_GPS_ERB::_parse_gps() | Source | [SHARED-STRUCT] Receiver backend writes GPS_State.location/status from the Emlid Reach ERB protocol. One of 14 receiver backends, each catalogued individually. target GPS_State.
9 | libraries/AP_GPS/AP_GPS_MAV.cpp | 67-75 | AP_GPS_MAV::handle_msg() | Source | [SHARED-STRUCT] Receiver backend writes GPS_State.location/status from the MAVLink GPS_INPUT message. One of 14 receiver backends, each catalogued individually. target GPS_State.
10 | libraries/AP_GPS/AP_GPS_MSP.cpp | 44-51 | AP_GPS_MSP::handle_msp() | Source | [SHARED-STRUCT] Receiver backend writes GPS_State.location/status from the MSP protocol GPS data. One of 14 receiver backends, each catalogued individually. target GPS_State.
11 | libraries/AP_GPS/AP_GPS_GSOF.cpp | 231-238 | AP_GPS_GSOF::pack_state_data() | Source | [SHARED-STRUCT] Receiver backend writes GPS_State.location/status from the Trimble GSOF binary. One of 14 receiver backends, each catalogued individually. target GPS_State.
# 6–11

## Slide 35
GROUP 1 — CORE PNT REFERENCES · CORE POSITIONING
Table 1 — Core Positioning (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | File Path | Line(s) | Function/Class | Role | Notes
12 | libraries/AP_GPS/AP_GPS_DroneCAN.cpp | 388-396 | AP_GPS_DroneCAN::handle_fix2_msg() | Source | [SHARED-STRUCT] Receiver backend writes GPS_State.location/status from the DroneCAN/UAVCAN Fix2 (external boundary modules/DroneCAN). One of 14 receiver backends, each catalogued individually. target GPS_State.
13 | libraries/AP_GPS/AP_GPS_ExternalAHRS.cpp | 49-56 | AP_GPS_ExternalAHRS::handle_external() | Source | [SHARED-STRUCT] Receiver backend writes GPS_State.location/status from the External AHRS/INS GPS feed. One of 14 receiver backends, each catalogued individually. target GPS_State.
14 | libraries/AP_GPS/AP_GPS_SITL.cpp | 86-93 | AP_GPS_SITL::read() | Source | [SHARED-STRUCT] Receiver backend writes GPS_State.location/status from the Software-in-the-loop simulated GPS. One of 14 receiver backends, each catalogued individually. target GPS_State.
15 | libraries/AP_GPS/GPS_Backend.cpp | 101-109 | AP_GPS_Backend::fill_3d_velocity() | Transform | Backend base class; derives state.velocity (NED) from ground_speed + ground_course for receivers that do not report 3D velocity. Shared by all backends.
16 | libraries/AP_GPS/AP_GPS.h | 324-329 | AP_GPS::location() | Source | Frontend accessor exposing backend-measured GPS_State.location; dispatches to primary_instance. Reached vehicle-side via the AP::gps() singleton.
17 | libraries/AP_GPS/AP_GPS.h | 360-365 | AP_GPS::velocity() | Source | [MULTI-CATEGORY] 3D NED velocity accessor of measured GPS_State.velocity. velocity also drives Navigation fusion (Table 2).
# 12–17

## Slide 36
GROUP 1 — CORE PNT REFERENCES · CORE POSITIONING
Table 1 — Core Positioning (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | File Path | Line(s) | Function/Class | Role | Notes
18 | libraries/AP_GPS/AP_GPS.h | 192-201 | structAP_GPS::GPS_State | Source | [SHARED-STRUCT] [MULTI-CATEGORY] One struct mixes Positioning (location), Navigation (velocity, ground_speed, ground_course) and Timing (time_week_ms, time_week) — see Table 3 #8. Primary extraction-risk struct for a PNT split.
19 | libraries/AP_GPS/AP_GPS_Blended.cpp | 17-25 | AP_GPS_Blended::_calc_weights() | Transform | Multi-receiver blending of location/velocity (GPS_MAX_RECEIVERS==2). Reads gps.state[].status (Data dependency) to weight receivers.
20 | libraries/AP_Common/Location.h | 11-20 | classLocation | Source | [SHARED-STRUCT] Geodetic PNT fields lat/lng (1E7 deg) and alt (cm) packed with NON-PNT bitfields relative_alt, loiter_ccw, terrain_alt, origin_alt, loiter_xtrack. Ubiquitous value type; top extraction risk.
21 | libraries/AP_Common/Location.cpp | 259-268 | Location::get_vector_from_origin_NEU_cm() | Transform | Geodetic (lat/lng/alt) → NEU centimetre vector relative to the EKF origin (geodetic↔NED duality).
22 | libraries/AP_InertialNav/AP_InertialNav.cpp | 14-23 | AP_InertialNav::update() | Transform | Pulls EKF origin-relative NE/D position into _relpos_cm (cm). get_position_neu_cm() exposes it to vehicle code.
23 | libraries/AC_AttitudeControl/AC_PosControl.cpp | 363-372 | AC_PosControl::input_pos_NEU_cm() | Sink | [ABSENT] 3D position/velocity controller consuming the position target. there is no standalone AC_PosControl library — it physically resides under libraries/AC_AttitudeControl/ (snapshot-fidelity note).
24 | libraries/APM_Control/AR_PosControl.cpp | 114-123 | AR_PosControl::update() | Sink | Rover position controller; reads AP::ahrs().get_relative_position_NED_origin() and get_velocity_NED() (Shared global/singleton). Separate controller from Copter's AC_PosControl.
# 18–24

## Slide 37
GROUP 1 — CORE PNT REFERENCES · CORE POSITIONING
Table 1 — Core Positioning (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | File Path | Line(s) | Function/Class | Role | Notes
25 | libraries/AP_Beacon/AP_Beacon.cpp | 175-184 | AP_Beacon::get_vehicle_position_ned() | Source | Non-GPS (GPS-denied) positioning source; returns vehicle NED position with a staleness timeout.
26 | libraries/AP_VisualOdom/AP_VisualOdom.cpp | 201-210 | AP_VisualOdom::handle_pose_estimate() | Source | Non-GPS visual-odometry position/attitude source feeding EKF external-nav fusion.
# 25–26

## Slide 38
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 1 — Code Snippet (5-10 lines)
Every row’s Code Snippet (5-10 lines), reproduced verbatim from the cited path:line range: one paragraph per source line, in the audit’s own order, with its indentation and its blank lines intact and nothing abbreviated.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
1 | libraries/AP_GPS/AP_GPS_UBLOX.cpp · 1510-1518 · AP_GPS_UBLOX::_parse_gps()(NAV-POSLLH) _last_pos_time = _buffer.posllh.itow; state.location.lng = _buffer.posllh.longitude; state.location.lat = _buffer.posllh.latitude; state.have_undulation = true; state.undulation = (_buffer.posllh.altitude_msl - _buffer.posllh.altitude_ellipsoid) * 0.001; set_alt_amsl_cm(state, _buffer.posllh.altitude_msl / 10); state.status = next_fix; _new_position = true;
# 1

## Slide 39
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 1 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
2 | libraries/AP_GPS/AP_GPS_NMEA.cpp · 333-340 · AP_GPS_NMEA::_term_complete() state.location.lat = _new_latitude; state.location.lng = _new_longitude; } state.num_sats = _new_satellite_count; state.hdop = _new_hdop; switch(_new_quality_indicator) { case 0: // Fix not available or invalid state.status = AP_GPS::NO_FIX;
3 | libraries/AP_GPS/AP_GPS_SBF.cpp · 484-491 · AP_GPS_SBF::process_message() state.location.lat = (int32_t)(temp.Latitude * RAD_TO_DEG_DOUBLE * (double)1e7); state.location.lng = (int32_t)(temp.Longitude * RAD_TO_DEG_DOUBLE * (double)1e7); state.have_undulation = !is_DNU(temp.Undulation); double height = temp.Height; // in metres if (state.have_undulation) { height -= temp.Undulation; state.undulation = -temp.Undulation; }
# 2–3

## Slide 40
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 1 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
4 | libraries/AP_GPS/AP_GPS_NOVA.cpp · 209-216 · AP_GPS_NOVA::process_message() state.last_gps_time_ms = AP_HAL::millis(); state.location.lat = (int32_t) (bestposu.lat * (double)1e7); state.location.lng = (int32_t) (bestposu.lng * (double)1e7); state.have_undulation = true; state.undulation = -bestposu.undulation; set_alt_amsl_cm(state, bestposu.hgt * 100);
5 | libraries/AP_GPS/AP_GPS_SBP.cpp · 276-283 · AP_GPS_SBP::_attempt_state_update() state.location.lat = (int32_t) (pos_llh->lat * (double)1e7); state.location.lng = (int32_t) (pos_llh->lon * (double)1e7); state.location.alt = (int32_t) (pos_llh->height * 100); state.num_sats = pos_llh->n_sats; if (pos_llh->flags == 0) { state.status = AP_GPS::GPS_OK_FIX_3D;
# 4–5

## Slide 41
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 1 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
6 | libraries/AP_GPS/AP_GPS_SBP2.cpp · 328-335 · AP_GPS_SBP2::_attempt_state_update() // state.location.lat = (int32_t) (last_pos_llh.lat * (double)1e7); state.location.lng = (int32_t) (last_pos_llh.lon * (double)1e7); state.location.alt = (int32_t) (last_pos_llh.height * 100); state.num_sats = last_pos_llh.n_sats; switch (last_pos_llh.flags.fix_mode) { case 1:
7 | libraries/AP_GPS/AP_GPS_SIRF.cpp · 178-185 · AP_GPS_SIRF::_parse_gps() state.status = AP_GPS::NO_FIX; }else if ((_buffer.nav.fix_type & FIX_MASK) == FIX_3D) { state.status = AP_GPS::GPS_OK_FIX_3D; }else{ state.status = AP_GPS::GPS_OK_FIX_2D; } state.location.lat = int32_t(be32toh(_buffer.nav.latitude)); state.location.lng = int32_t(be32toh(_buffer.nav.longitude));
# 6–7

## Slide 42
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 1 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
8 | libraries/AP_GPS/AP_GPS_ERB.cpp · 150-157 · AP_GPS_ERB::_parse_gps() _last_pos_time = _buffer.pos.time; state.location.lng = (int32_t)(_buffer.pos.longitude * (double)1e7); state.location.lat = (int32_t)(_buffer.pos.latitude * (double)1e7); state.have_undulation = true; state.undulation = _buffer.pos.altitude_msl - _buffer.pos.altitude_ellipsoid; set_alt_amsl_cm(state, _buffer.pos.altitude_msl * 100); state.status = next_fix; _new_position = true;
9 | libraries/AP_GPS/AP_GPS_MAV.cpp · 67-75 · AP_GPS_MAV::handle_msg() state.status = (AP_GPS::GPS_Status)packet.fix_type; Location loc = {}; loc.lat = packet.lat; loc.lng = packet.lon; if (have_alt) { loc.alt = packet.alt * 100; // convert to centimeters } state.location = loc;
# 8–9

## Slide 43
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 1 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
10 | libraries/AP_GPS/AP_GPS_MSP.cpp · 44-51 · AP_GPS_MSP::handle_msp() state.status = (AP_GPS::GPS_Status)pkt.fix_type; state.num_sats = pkt.satellites_in_view; state.location = { pkt.latitude, pkt.longitude, pkt.msl_altitude, Location::AltFrame::ABSOLUTE };
11 | libraries/AP_GPS/AP_GPS_GSOF.cpp · 231-238 · AP_GPS_GSOF::pack_state_data() state.location.lat = (int32_t)(RAD_TO_DEG_DOUBLE * position.latitude_rad * (double)1e7); state.location.lng = (int32_t)(RAD_TO_DEG_DOUBLE * position.longitude_rad * (double)1e7); state.location.alt = (int32_t)(position.altitude * 100); state.last_gps_time_ms = AP_HAL::millis(); if ((vel.velocity_flags & 1) == 1) { state.ground_speed = vel.horizontal_velocity; state.ground_course = wrap_360(degrees(vel.heading));
# 10–11

## Slide 44
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 1 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
12 | libraries/AP_GPS/AP_GPS_DroneCAN.cpp · 388-396 · AP_GPS_DroneCAN::handle_fix2_msg() if (msg.height_msl_mm != msg.height_ellipsoid_mm) { seen_valid_height_ellipsoid = true; } interim_state.have_undulation = seen_valid_height_ellipsoid; if (seen_valid_height_ellipsoid) { interim_state.undulation = (msg.height_msl_mm - msg.height_ellipsoid_mm) * 0.001; } interim_state.location = loc; set_alt_amsl_cm(interim_state, alt_amsl_cm);
13 | libraries/AP_GPS/AP_GPS_ExternalAHRS.cpp · 49-56 · AP_GPS_ExternalAHRS::handle_external() state.num_sats = pkt.satellites_in_view; const Location loc { pkt.latitude, pkt.longitude, pkt.msl_altitude, Location::AltFrame::ABSOLUTE };
# 12–13

## Slide 45
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 1 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
14 | libraries/AP_GPS/AP_GPS_SITL.cpp · 86-93 · AP_GPS_SITL::read() state.status = AP_GPS::GPS_OK_FIX_3D; state.num_sats = 15; state.location = Location{ int32_t(latitude*1e7), int32_t(longitude*1e7), int32_t(altitude*100), Location::AltFrame::ABSOLUTE
15 | libraries/AP_GPS/GPS_Backend.cpp · 101-109 · AP_GPS_Backend::fill_3d_velocity() void AP_GPS_Backend::fill_3d_velocity(void) { float gps_heading = radians(state.ground_course); state.velocity.x = state.ground_speed * cosf(gps_heading); state.velocity.y = state.ground_speed * sinf(gps_heading); state.velocity.z = 0; state.have_vertical_velocity = false; }
# 14–15

## Slide 46
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 1 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
16 | libraries/AP_GPS/AP_GPS.h · 324-329 · AP_GPS::location() const Location &location(uint8_t instance) const { return state[instance].location; } const Location &location() const { return location(primary_instance); }
17 | libraries/AP_GPS/AP_GPS.h · 360-365 · AP_GPS::velocity() const Vector3f &velocity(uint8_t instance) const { return state[instance].velocity; } const Vector3f &velocity() const { return velocity(primary_instance); }
# 16–17

## Slide 47
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 1 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
18 | libraries/AP_GPS/AP_GPS.h · 192-201 · structAP_GPS::GPS_State struct GPS_State { uint8_t instance; // the instance number of this GPS // all the following fields must all be filled by the backend driver GPS_Status status; ///< driver fix status uint32_t time_week_ms; ///< GPS time (milliseconds from start of GPS week) uint16_t time_week; ///< GPS week number Location location; ///< last fix location float ground_speed; ///< ground speed in m/s float ground_course; ///< ground course in degrees, wrapped 0-360
19 | libraries/AP_GPS/AP_GPS_Blended.cpp · 17-25 · AP_GPS_Blended::_calc_weights() bool AP_GPS_Blended::_calc_weights(void) { // zero the blend weights memset(&_blend_weights, 0, sizeof(_blend_weights)); static_assert(GPS_MAX_RECEIVERS == 2, "GPS blending only currently works with 2 receivers"); // Note that the early quit below relies upon exactly 2 instances // The time delta calculations below also rely upon every instance being currently detected and being parsed
# 18–19

## Slide 48
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 1 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
20 | libraries/AP_Common/Location.h · 11-20 · classLocation uint8_t relative_alt : 1; // 1 if altitude is relative to home uint8_t loiter_ccw : 1; // 0 if clockwise, 1 if counter clockwise uint8_t terrain_alt : 1; // this altitude is above terrain uint8_t origin_alt : 1; // this altitude is above ekf origin uint8_t loiter_xtrack : 1; // 0 to crosstrack from center of waypoint, 1 to crosstrack from tangent exit location // note that mission storage only stores 24 bits of altitude (~ +/- 83km) int32_t alt; // in cm int32_t lat; // in 1E7 degrees int32_t lng; // in 1E7 degrees
21 | libraries/AP_Common/Location.cpp · 259-268 · Location::get_vector_from_origin_NEU_cm() bool Location::get_vector_from_origin_NEU_cm(T &vec_neu) const { // convert altitude int32_t alt_above_origin_cm = 0; if (!get_alt_cm(AltFrame::ABOVE_ORIGIN, alt_above_origin_cm)) { return false; } // convert lat, lon if (!get_vector_xy_from_origin_NE_cm(vec_neu.xy())) {
# 20–21

## Slide 49
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 1 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
22 | libraries/AP_InertialNav/AP_InertialNav.cpp · 14-23 · AP_InertialNav::update() void AP_InertialNav::update(bool high_vibes) { // get the NE position relative to the local earth frame origin Vector2f posNE; if (_ahrs_ekf.get_relative_position_NE_origin_float(posNE)) { _relpos_cm.x = posNE.x * 100; // convert from m to cm _relpos_cm.y = posNE.y * 100; // convert from m to cm } // get the D position relative to the local earth frame origin
23 | libraries/AC_AttitudeControl/AC_PosControl.cpp · 363-372 · AC_PosControl::input_pos_NEU_cm() void AC_PosControl::input_pos_NEU_cm(const Vector3p& pos_neu_cm, float pos_terrain_target_u_cm, float terrain_buffer_cm) { input_pos_NEU_m(pos_neu_cm * 0.01, pos_terrain_target_u_cm * 0.01, terrain_buffer_cm * 0.01); } // Sets a new NEU position target in meters and computes a jerk-limited trajectory. // Updates internal acceleration commands using a smooth kinematic path constrained // by configured acceleration and jerk limits. Terrain margin is used to constrain // horizontal velocity to avoid vertical buffer violation. void AC_PosControl::input_pos_NEU_m(const Vector3p& pos_neu_m, float pos_terrain_target_u_m, float terrain_buffer_m)
# 22–23

## Slide 50
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 1 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
24 | libraries/APM_Control/AR_PosControl.cpp · 114-123 · AR_PosControl::update() void AR_PosControl::update(float dt) { // exit immediately if no current location, destination or disarmed Vector3p curr_pos_NED_m; Vector3f curr_vel_NED; if (!hal.util->get_soft_armed() ¦¦ !AP::ahrs().get_relative_position_NED_origin(curr_pos_NED_m) ¦¦ !AP::ahrs().get_velocity_NED(curr_vel_NED)) { _desired_speed = _atc.get_desired_speed_accel_limited(0.0f, dt); _desired_lat_accel = 0.0f; _desired_turn_rate_rads = 0.0f;
25 | libraries/AP_Beacon/AP_Beacon.cpp · 175-184 · AP_Beacon::get_vehicle_position_ned() bool AP_Beacon::get_vehicle_position_ned(Vector3f &position, float& accuracy_estimate) const { if (!device_ready()) { return false; } // check for timeout if (AP_HAL::millis() - veh_pos_update_ms > AP_BEACON_TIMEOUT_MS) { return false; }
# 24–25

## Slide 51
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 1 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
26 | libraries/AP_VisualOdom/AP_VisualOdom.cpp · 201-210 · AP_VisualOdom::handle_pose_estimate() void AP_VisualOdom::handle_pose_estimate(uint64_t remote_time_us, uint32_t time_ms, float x, float y, float z, float roll, float pitch, float yaw, float posErr, float angErr, uint8_t reset_counter, int8_t quality) { // exit immediately if not enabled if (!enabled()) { return; } // call backend if (_driver != nullptr) { // convert attitude to quaternion and call backend
# 26

## Slide 52
DEPENDENCY MAP · LAYER 1 · DIRECT EDGES
Table 1a — Layer 1 dependency map
Table 1a: Layer 1 — direct callers / callees with typed dependency
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Component/Function | Directly Calls | Directly Called By | Dependency Type
1 | AP_GPS_UBLOX backend | writes GPS_State.location/status; fill_3d_velocity() | AP_GPS::update() → backend read() | Inheritance/Interface
2 | AP_GPS_NMEA backend | writes GPS_State.location/status; fill_3d_velocity() | AP_GPS::update() → backend read() | Inheritance/Interface
3 | AP_GPS_SBF backend | writes GPS_State.location/status; fill_3d_velocity() | AP_GPS::update() → backend read() | Inheritance/Interface
4 | AP_GPS_NOVA backend | writes GPS_State.location/status; fill_3d_velocity() | AP_GPS::update() → backend read() | Inheritance/Interface
5 | AP_GPS_SBP backend | writes GPS_State.location/status; fill_3d_velocity() | AP_GPS::update() → backend read() | Inheritance/Interface
6 | AP_GPS_SBP2 backend | writes GPS_State.location/status; fill_3d_velocity() | AP_GPS::update() → backend read() | Inheritance/Interface
7 | AP_GPS_SIRF backend | writes GPS_State.location/status; fill_3d_velocity() | AP_GPS::update() → backend read() | Inheritance/Interface
8 | AP_GPS_ERB backend | writes GPS_State.location/status; fill_3d_velocity() | AP_GPS::update() → backend read() | Inheritance/Interface
9 | AP_GPS_MAV backend | writes GPS_State.location/status; fill_3d_velocity() | AP_GPS::update() → backend read() | Inheritance/Interface
# 1–9

## Slide 53
DEPENDENCY MAP · LAYER 1 · DIRECT EDGES
Table 1a — Layer 1 dependency map (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Component/Function | Directly Calls | Directly Called By | Dependency Type
10 | AP_GPS_MSP backend | writes GPS_State.location/status; fill_3d_velocity() | AP_GPS::update() → backend read() | Inheritance/Interface
11 | AP_GPS_GSOF backend | writes GPS_State.location/status; fill_3d_velocity() | AP_GPS::update() → backend read() | Inheritance/Interface
12 | AP_GPS_DroneCAN backend | writes GPS_State.location/status; fill_3d_velocity() | AP_GPS::update() → backend read() | Inheritance/Interface
13 | AP_GPS_ExternalAHRS backend | writes GPS_State.location/status; fill_3d_velocity() | AP_GPS::update() → backend read() | Inheritance/Interface
14 | AP_GPS_SITL backend | writes GPS_State.location/status; fill_3d_velocity() | AP_GPS::update() → backend read() | Inheritance/Interface
15 | AP_GPS_Backend::fill_3d_velocity() | cosf/sinf on state.ground_course; writes state.velocity | All receiver backends (UBLOX, NMEA, SIRF, ...) | Data dependency
16 | AP_GPS::location() | returns state[instance].location | NavEKF3_Measurements::readGpsData(); AP_AHRS; AC_WPNav | Function call
17 | AP_GPS::velocity() | returns state[instance].velocity | NavEKF3_Measurements::readGpsData() (PosVel fusion) | Function call
18 | AP_GPS::GPS_State (struct) | (data struct — no calls) | All GPS backends (write); frontend accessors (read) | Data dependency
19 | AP_GPS_Blended::_calc_weights() | gps.state[].status; time deltas | AP_GPS_Blended::calc_weights()/update (blended primary) | Data dependency
# 10–19

## Slide 54
DEPENDENCY MAP · LAYER 1 · DIRECT EDGES
Table 1a — Layer 1 dependency map (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Component/Function | Directly Calls | Directly Called By | Dependency Type
20 | class Location | get_alt_cm(); get_vector_xy_from_origin_NE_cm() | GPS_State; AP_AHRS; AC_WPNav; AP_Mission (ubiquitous) | Data dependency
21 | Location::get_vector_from_origin_NEU_cm() | get_alt_cm(); get_vector_xy_from_origin_NE_cm() | AC_WPNav::get_vector_NEU_cm() | Function call
22 | AP_InertialNav::update() | _ahrs_ekf.get_relative_position_NE_origin_float() | Copter::read_inertia() | Function call
23 | AC_PosControl::input_pos_NEU_cm() | input_pos_NEU_m() | ArduCopter mode_auto.cpp / mode.cpp | Function call
24 | AR_PosControl::update() | AP::ahrs().get_relative_position_NED_origin(); get_velocity_NED() | Rover mode controllers | Shared global/singleton
25 | AP_Beacon::get_vehicle_position_ned() | device_ready(); AP_HAL::millis() | NavEKF3 range-beacon fusion | Function call
26 | AP_VisualOdom::handle_pose_estimate() | _driver backend handle_pose_estimate() | GCS / AP_ExternalAHRS pose handlers | Inheritance/Interface
# 20–26

## Slide 55
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 1a — Layer 1 Code Snippet
Every row’s Code Snippet, reproduced verbatim from the cited path:line range: one paragraph per source line, in the audit’s own order, with its indentation and its blank lines intact and nothing abbreviated.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
1 | AP_GPS_UBLOX backend · Inheritance/Interface _last_pos_time = _buffer.posllh.itow; state.location.lng = _buffer.posllh.longitude; state.location.lat = _buffer.posllh.latitude; state.have_undulation = true; state.undulation = (_buffer.posllh.altitude_msl - _buffer. posllh.altitude_ellipsoid) * 0.001; set_alt_amsl_cm(state, _buffer.posllh.altitude_msl / 10); state.status = next_fix; _new_position = true;
2 | AP_GPS_NMEA backend · Inheritance/Interface state.location.lat = _new_latitude; state.location.lng = _new_longitude; } state.num_sats = _new_satellite_count; state.hdop = _new_hdop; switch(_new_quality_indicator) { case 0: // Fix not available or invalid state.status = AP_GPS::NO_FIX;
# 1–2

## Slide 56
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 1a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
3 | AP_GPS_SBF backend · Inheritance/Interface state.location.lat = (int32_t)(temp.Latitude * RAD_TO_DEG_DOUBLE * (double)1e7); state.location.lng = (int32_t)(temp.Longitude * RAD_TO_DEG_DOUBLE * (double)1e7); state.have_undulation = !is_DNU(temp.Undulation); double height = temp.Height; // in metres if (state.have_undulation) { height -= temp.Undulation; state.undulation = -temp.Undulation; }
4 | AP_GPS_NOVA backend · Inheritance/Interface state.last_gps_time_ms = AP_HAL::millis(); state.location.lat = (int32_t) (bestposu.lat * (double)1e7 ); state.location.lng = (int32_t) (bestposu.lng * (double)1e7 ); state.have_undulation = true; state.undulation = -bestposu.undulation; set_alt_amsl_cm(state, bestposu.hgt * 100);
# 3–4

## Slide 57
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 1a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
5 | AP_GPS_SBP backend · Inheritance/Interface state.location.lat = (int32_t) (pos_llh->lat * (double)1e7); state.location.lng = (int32_t) (pos_llh->lon * (double)1e7); state.location.alt = (int32_t) (pos_llh->height * 100 ); state.num_sats = pos_llh->n_sats; if (pos_llh->flags == 0) { state.status = AP_GPS::GPS_OK_FIX_3D;
6 | AP_GPS_SBP2 backend · Inheritance/Interface // state.location.lat = (int32_t) (last_pos_llh.lat * (double)1e7); state.location.lng = (int32_t) (last_pos_llh.lon * (double)1e7); state.location.alt = (int32_t) (last_pos_llh.height * 100); state.num_sats = last_pos_llh.n_sats; switch (last_pos_llh.flags.fix_mode) { case 1:
# 5–6

## Slide 58
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 1a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
7 | AP_GPS_SIRF backend · Inheritance/Interface state.status = AP_GPS::NO_FIX; }else if ((_buffer.nav.fix_type & FIX_MASK) == FIX_3D) { state.status = AP_GPS::GPS_OK_FIX_3D; }else{ state.status = AP_GPS::GPS_OK_FIX_2D; } state.location.lat = int32_t(be32toh(_buffer.nav.latitude)); state.location.lng = int32_t(be32toh(_buffer.nav.longitude));
8 | AP_GPS_ERB backend · Inheritance/Interface _last_pos_time = _buffer.pos.time; state.location.lng = (int32_t)(_buffer.pos.longitude * (double)1e7); state.location.lat = (int32_t)(_buffer.pos.latitude * ( double)1e7); state.have_undulation = true; state.undulation = _buffer.pos.altitude_msl - _buffer.pos. altitude_ellipsoid; set_alt_amsl_cm(state, _buffer.pos.altitude_msl * 100); state.status = next_fix; _new_position = true;
# 7–8

## Slide 59
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 1a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
9 | AP_GPS_MAV backend · Inheritance/Interface state.status = (AP_GPS::GPS_Status)packet.fix_type; Location loc = {}; loc.lat = packet.lat; loc.lng = packet.lon; if (have_alt) { loc.alt = packet.alt * 100; // convert to centimeters } state.location = loc;
10 | AP_GPS_MSP backend · Inheritance/Interface state.status = (AP_GPS::GPS_Status)pkt.fix_type; state.num_sats = pkt.satellites_in_view; state.location = { pkt.latitude, pkt.longitude, pkt.msl_altitude, Location::AltFrame::ABSOLUTE };
# 9–10

## Slide 60
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 1a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
11 | AP_GPS_GSOF backend · Inheritance/Interface state.location.lat = (int32_t)(RAD_TO_DEG_DOUBLE * position.latitude_rad * (double)1e7); state.location.lng = (int32_t)(RAD_TO_DEG_DOUBLE * position.longitude_rad * (double)1e7); state.location.alt = (int32_t)(position.altitude * 100); state.last_gps_time_ms = AP_HAL::millis(); if ((vel.velocity_flags & 1) == 1) { state.ground_speed = vel.horizontal_velocity; state.ground_course = wrap_360(degrees(vel.heading));
12 | AP_GPS_DroneCAN backend · Inheritance/Interface if (msg.height_msl_mm != msg.height_ellipsoid_mm) { seen_valid_height_ellipsoid = true; } interim_state.have_undulation = seen_valid_height_ellipsoid; if (seen_valid_height_ellipsoid) { interim_state.undulation = (msg.height_msl_mm - msg.height_ellipsoid_mm) * 0.001; } interim_state.location = loc; set_alt_amsl_cm(interim_state, alt_amsl_cm);
# 11–12

## Slide 61
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 1a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
13 | AP_GPS_ExternalAHRS backend · Inheritance/Interface state.num_sats = pkt.satellites_in_view; const Location loc { pkt.latitude, pkt.longitude, pkt.msl_altitude, Location::AltFrame::ABSOLUTE };
14 | AP_GPS_SITL backend · Inheritance/Interface state.status = AP_GPS::GPS_OK_FIX_3D; state.num_sats = 15; state.location = Location{ int32_t(latitude*1e7), int32_t(longitude*1e7), int32_t(altitude*100), Location::AltFrame::ABSOLUTE
# 13–14

## Slide 62
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 1a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
15 | AP_GPS_Backend::fill_3d_velocity() · Data dependency void AP_GPS_Backend::fill_3d_velocity(void) { float gps_heading = radians(state.ground_course); state.velocity.x = state.ground_speed * cosf(gps_heading); state.velocity.y = state.ground_speed * sinf(gps_heading); state.velocity.z = 0; state.have_vertical_velocity = false; }
16 | AP_GPS::location() · Function call const Location &location(uint8_t instance) const { return state[instance].location; } const Location &location() const { return location(primary_instance); }
17 | AP_GPS::velocity() · Function call const Vector3f &velocity(uint8_t instance) const { return state[instance].velocity; } const Vector3f &velocity() const { return velocity(primary_instance); }
# 15–17

## Slide 63
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 1a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
18 | AP_GPS::GPS_State (struct) · Data dependency struct GPS_State { uint8_t instance; // the instance number of this GPS // all the following fields must all be filled by the backend driver GPS_Status status; ///< driver fix status uint32_t time_week_ms; ///< GPS time (milliseconds from start of GPS week) uint16_t time_week; ///< GPS week number Location location; ///< last fix location float ground_speed; ///< ground speed in m /s float ground_course; ///< ground course in degrees, wrapped 0-360
19 | AP_GPS_Blended::_calc_weights() · Data dependency bool AP_GPS_Blended::_calc_weights(void) { // zero the blend weights memset(&_blend_weights, 0, sizeof(_blend_weights)); static_assert(GPS_MAX_RECEIVERS == 2, "GPS blending only currently works with 2 receivers"); // Note that the early quit below relies upon exactly 2 instances // The time delta calculations below also rely upon every instance being currently detected and being parsed
# 18–19

## Slide 64
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 1a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
20 | class Location · Data dependency uint8_t relative_alt : 1; // 1 if altitude is relative to home uint8_t loiter_ccw : 1; // 0 if clockwise, 1 if counter clockwise uint8_t terrain_alt : 1; // this altitude is above terrain uint8_t origin_alt : 1; // this altitude is above ekf origin uint8_t loiter_xtrack : 1; // 0 to crosstrack from center of waypoint, 1 to crosstrack from tangent exit location // note that mission storage only stores 24 bits of altitude ( ~ +/- 83km) int32_t alt; // in cm int32_t lat; // in 1E7 degrees int32_t lng; // in 1E7 degrees
21 | Location::get_vector_from_origin_NEU_cm() · Function call bool Location::get_vector_from_origin_NEU_cm(T &vec_neu) const { // convert altitude int32_t alt_above_origin_cm = 0; if (!get_alt_cm(AltFrame::ABOVE_ORIGIN, alt_above_origin_cm)) { return false; } // convert lat, lon if (!get_vector_xy_from_origin_NE_cm(vec_neu.xy())) {
# 20–21

## Slide 65
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 1a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
22 | AP_InertialNav::update() · Function call void AP_InertialNav::update(bool high_vibes) { // get the NE position relative to the local earth frame origin Vector2f posNE; if (_ahrs_ekf.get_relative_position_NE_origin_float(posNE)) { _relpos_cm.x = posNE.x * 100; // convert from m to cm _relpos_cm.y = posNE.y * 100; // convert from m to cm } // get the D position relative to the local earth frame origin
23 | AC_PosControl::input_pos_NEU_cm() · Function call void AC_PosControl::input_pos_NEU_cm(const Vector3p& pos_neu_cm, float pos_terrain_target_u_cm, float terrain_buffer_cm) { input_pos_NEU_m(pos_neu_cm * 0.01, pos_terrain_target_u_cm * 0 .01, terrain_buffer_cm * 0.01); } // Sets a new NEU position target in meters and computes a jerk-limited trajectory. // Updates internal acceleration commands using a smooth kinematic path constrained // by configured acceleration and jerk limits. Terrain margin is used to constrain // horizontal velocity to avoid vertical buffer violation. void AC_PosControl::input_pos_NEU_m(const Vector3p& pos_neu_m, float pos_terrain_target_u_m, float terrain_buffer_m)
# 22–23

## Slide 66
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 1a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
24 | AR_PosControl::update() · Shared global/singleton void AR_PosControl::update(float dt) { // exit immediately if no current location, destination or disarmed Vector3p curr_pos_NED_m; Vector3f curr_vel_NED; if (!hal.util->get_soft_armed() ¦¦ !AP::ahrs().get_relative_position_NED_origin(curr_pos_NED_m) ¦¦ !AP::ahrs().get_velocity_NED(curr_vel_NED)) { _desired_speed = _atc.get_desired_speed_accel_limited(0.0f , dt); _desired_lat_accel = 0.0f; _desired_turn_rate_rads = 0.0f;
25 | AP_Beacon::get_vehicle_position_ned() · Function call bool AP_Beacon::get_vehicle_position_ned(Vector3f &position, float & accuracy_estimate) const { if (!device_ready()) { return false; } // check for timeout if (AP_HAL::millis() - veh_pos_update_ms > AP_BEACON_TIMEOUT_MS) { return false; }
# 24–25

## Slide 67
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 1a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
26 | AP_VisualOdom::handle_pose_estimate() · Inheritance/Interface void AP_VisualOdom::handle_pose_estimate(uint64_t remote_time_us, uint32_t time_ms, float x, float y, float z, float roll, float pitch, float yaw, float posErr, float angErr, uint8_t reset_counter, int8_t quality) { // exit immediately if not enabled if (!enabled()) { return; } // call backend if (_driver != nullptr) { // convert attitude to quaternion and call backend
# 26

## Slide 68
DEPENDENCY MAP · LAYER 2 · DEPTHS 3, 4, 5, 6, 8
Table 1a — Layer 2 transitive chains
Table 1a: Layer 2 — full transitive chain, final consumer & hop depth
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
1 | AP_GPS_UBLOX (state.location) | AP_GPS_UBLOX → AP_GPS::location()/velocity() → NavEKF3_Measurements::readGpsData (gps.location/gps.velocity) → NavEKF3::FuseVelPosNED → AP_AHRS::get_location() → AC_WPNav → AC_PosControl → AC_AttitudeControl → AP_Motors | AP_Motors / SRV_Channel | 8 | Sensor source to actuator; GPS ingested in AP_NavEKF3_Measurements.cpp (readGpsData) before FuseVelPosNED.
2 | AP_GPS_NMEA (state.location) | AP_GPS_NMEA → AP_GPS::location()/velocity() → NavEKF3_Measurements::readGpsData (gps.location/gps.velocity) → NavEKF3::FuseVelPosNED → AP_AHRS::get_location() → AC_WPNav → AC_PosControl → AC_AttitudeControl → AP_Motors | AP_Motors / SRV_Channel | 8 | Sensor source to actuator; GPS ingested in AP_NavEKF3_Measurements.cpp (readGpsData) before FuseVelPosNED.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 1–2

## Slide 69
DEPENDENCY MAP · LAYER 2 · DEPTHS 3, 4, 5, 6, 8
Table 1a — Layer 2 transitive chains (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
3 | AP_GPS_SBF (state.location) | AP_GPS_SBF → AP_GPS::location()/velocity() → NavEKF3_Measurements::readGpsData (gps.location/gps.velocity) → NavEKF3::FuseVelPosNED → AP_AHRS::get_location() → AC_WPNav → AC_PosControl → AC_AttitudeControl → AP_Motors | AP_Motors / SRV_Channel | 8 | Sensor source to actuator; GPS ingested in AP_NavEKF3_Measurements.cpp (readGpsData) before FuseVelPosNED.
4 | AP_GPS_NOVA (state.location) | AP_GPS_NOVA → AP_GPS::location()/velocity() → NavEKF3_Measurements::readGpsData (gps.location/gps.velocity) → NavEKF3::FuseVelPosNED → AP_AHRS::get_location() → AC_WPNav → AC_PosControl → AC_AttitudeControl → AP_Motors | AP_Motors / SRV_Channel | 8 | Sensor source to actuator; GPS ingested in AP_NavEKF3_Measurements.cpp (readGpsData) before FuseVelPosNED.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 3–4

## Slide 70
DEPENDENCY MAP · LAYER 2 · DEPTHS 3, 4, 5, 6, 8
Table 1a — Layer 2 transitive chains (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
5 | AP_GPS_SBP (state.location) | AP_GPS_SBP → AP_GPS::location()/velocity() → NavEKF3_Measurements::readGpsData (gps.location/gps.velocity) → NavEKF3::FuseVelPosNED → AP_AHRS::get_location() → AC_WPNav → AC_PosControl → AC_AttitudeControl → AP_Motors | AP_Motors / SRV_Channel | 8 | Sensor source to actuator; GPS ingested in AP_NavEKF3_Measurements.cpp (readGpsData) before FuseVelPosNED.
6 | AP_GPS_SBP2 (state.location) | AP_GPS_SBP2 → AP_GPS::location()/velocity() → NavEKF3_Measurements::readGpsData (gps.location/gps.velocity) → NavEKF3::FuseVelPosNED → AP_AHRS::get_location() → AC_WPNav → AC_PosControl → AC_AttitudeControl → AP_Motors | AP_Motors / SRV_Channel | 8 | Sensor source to actuator; GPS ingested in AP_NavEKF3_Measurements.cpp (readGpsData) before FuseVelPosNED.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 5–6

## Slide 71
DEPENDENCY MAP · LAYER 2 · DEPTHS 3, 4, 5, 6, 8
Table 1a — Layer 2 transitive chains (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
7 | AP_GPS_SIRF (state.location) | AP_GPS_SIRF → AP_GPS::location()/velocity() → NavEKF3_Measurements::readGpsData (gps.location/gps.velocity) → NavEKF3::FuseVelPosNED → AP_AHRS::get_location() → AC_WPNav → AC_PosControl → AC_AttitudeControl → AP_Motors | AP_Motors / SRV_Channel | 8 | Sensor source to actuator; GPS ingested in AP_NavEKF3_Measurements.cpp (readGpsData) before FuseVelPosNED.
8 | AP_GPS_ERB (state.location) | AP_GPS_ERB → AP_GPS::location()/velocity() → NavEKF3_Measurements::readGpsData (gps.location/gps.velocity) → NavEKF3::FuseVelPosNED → AP_AHRS::get_location() → AC_WPNav → AC_PosControl → AC_AttitudeControl → AP_Motors | AP_Motors / SRV_Channel | 8 | Sensor source to actuator; GPS ingested in AP_NavEKF3_Measurements.cpp (readGpsData) before FuseVelPosNED.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 7–8

## Slide 72
DEPENDENCY MAP · LAYER 2 · DEPTHS 3, 4, 5, 6, 8
Table 1a — Layer 2 transitive chains (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
9 | AP_GPS_MAV (state.location) | AP_GPS_MAV → AP_GPS::location()/velocity() → NavEKF3_Measurements::readGpsData (gps.location/gps.velocity) → NavEKF3::FuseVelPosNED → AP_AHRS::get_location() → AC_WPNav → AC_PosControl → AC_AttitudeControl → AP_Motors | AP_Motors / SRV_Channel | 8 | Sensor source to actuator; GPS ingested in AP_NavEKF3_Measurements.cpp (readGpsData) before FuseVelPosNED.
10 | AP_GPS_MSP (state.location) | AP_GPS_MSP → AP_GPS::location()/velocity() → NavEKF3_Measurements::readGpsData (gps.location/gps.velocity) → NavEKF3::FuseVelPosNED → AP_AHRS::get_location() → AC_WPNav → AC_PosControl → AC_AttitudeControl → AP_Motors | AP_Motors / SRV_Channel | 8 | Sensor source to actuator; GPS ingested in AP_NavEKF3_Measurements.cpp (readGpsData) before FuseVelPosNED.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 9–10

## Slide 73
DEPENDENCY MAP · LAYER 2 · DEPTHS 3, 4, 5, 6, 8
Table 1a — Layer 2 transitive chains (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
11 | AP_GPS_GSOF (state.location) | AP_GPS_GSOF → AP_GPS::location()/velocity() → NavEKF3_Measurements::readGpsData (gps.location/gps.velocity) → NavEKF3::FuseVelPosNED → AP_AHRS::get_location() → AC_WPNav → AC_PosControl → AC_AttitudeControl → AP_Motors | AP_Motors / SRV_Channel | 8 | Sensor source to actuator; GPS ingested in AP_NavEKF3_Measurements.cpp (readGpsData) before FuseVelPosNED.
12 | AP_GPS_DroneCAN (state.location) | AP_GPS_DroneCAN → AP_GPS::location()/velocity() → NavEKF3_Measurements::readGpsData (gps.location/gps.velocity) → NavEKF3::FuseVelPosNED → AP_AHRS::get_location() → AC_WPNav → AC_PosControl → AC_AttitudeControl → AP_Motors | AP_Motors / SRV_Channel | 8 | Sensor source to actuator; GPS ingested in AP_NavEKF3_Measurements.cpp (readGpsData) before FuseVelPosNED.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 11–12

## Slide 74
DEPENDENCY MAP · LAYER 2 · DEPTHS 3, 4, 5, 6, 8
Table 1a — Layer 2 transitive chains (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
13 | AP_GPS_ExternalAHRS (state.location) | AP_GPS_ExternalAHRS → AP_GPS::location()/velocity() → NavEKF3_Measurements::readGpsData (gps.location/gps.velocity) → NavEKF3::FuseVelPosNED → AP_AHRS::get_location() → AC_WPNav → AC_PosControl → AC_AttitudeControl → AP_Motors | AP_Motors / SRV_Channel | 8 | Sensor source to actuator; GPS ingested in AP_NavEKF3_Measurements.cpp (readGpsData) before FuseVelPosNED.
14 | AP_GPS_SITL (state.location) | AP_GPS_SITL → AP_GPS::location()/velocity() → NavEKF3_Measurements::readGpsData (gps.location/gps.velocity) → NavEKF3::FuseVelPosNED → AP_AHRS::get_location() → AC_WPNav → AC_PosControl → AC_AttitudeControl → AP_Motors | AP_Motors / SRV_Channel | 8 | Sensor source to actuator; GPS ingested in AP_NavEKF3_Measurements.cpp (readGpsData) before FuseVelPosNED.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 13–14

## Slide 75
DEPENDENCY MAP · LAYER 2 · DEPTHS 3, 4, 5, 6, 8
Table 1a — Layer 2 transitive chains (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
15 | GPS velocity (fill_3d_velocity) | GPS_State.velocity → AP_GPS::velocity() → NavEKF3_Measurements::readGpsData → NavEKF3::FuseVelPosNED → AP_AHRS::get_velocity_NED() → AC_PosControl → AP_Motors | AP_Motors | 6 | [MULTI-CATEGORY] also Navigation.
16 | AP_GPS::location() | AP_GPS::location() → NavEKF3_Measurements::readGpsData (gps.location) → NavEKF3::FuseVelPosNED → AP_AHRS::get_location() → AC_WPNav::set_wp_destination_loc → AC_PosControl → AP_Motors | AP_Motors | 6 | Geodetic position path (ingestion hop explicit).
17 | AP_GPS::velocity() | AP_GPS::velocity() → NavEKF3_Measurements::readGpsData (gps.velocity) → NavEKF3::FuseVelPosNED → AP_AHRS::get_velocity_NED() → AC_PosControl → AP_Motors | AP_Motors | 5 | Velocity path (ingestion hop explicit).
18 | GPS_State (struct) | GPS_State → AP_GPS accessors {location¦velocity¦time_week} → NavEKF3_Measurements → EKF/AHRS + AP_RTC → controllers + clock | AP_Motors and AP_RTC | 4 | [SHARED-STRUCT] [MULTI-CATEGORY] branches into Table 3.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 15–18

## Slide 76
DEPENDENCY MAP · LAYER 2 · DEPTHS 3, 4, 5, 6, 8
Table 1a — Layer 2 transitive chains (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
19 | AP_GPS_Blended | Blended → AP_GPS primary (blended) location/velocity → NavEKF3_Measurements → NavEKF3::FuseVelPosNED → AP_AHRS → controllers → AP_Motors | AP_Motors | 6 | Transform upstream of EKF ingestion.
20 | class Location (geodetic value type) | Location → AC_WPNav::set_wp_destination_loc → get_vector_NEU_cm → AC_PosControl → AC_AttitudeControl → AP_Motors | AP_Motors | 5 | [SHARED-STRUCT] Pervasive value type; depth measured along its dominant waypoint-control consumer branch (the AC_WPNav→PosControl path).
21 | Location→NEU conversion | get_vector_from_origin_NEU_cm() → AC_WPNav::get_vector_NEU_cm → set_wp_destination_NEU_cm → AC_PosControl | AC_PosControl | 3 | Geodetic↔NED transform edge.
22 | AP_InertialNav | EKF origin-relative pos → AP_InertialNav::update → _relpos_cm → Copter logging/reporting | GCS / logger | 3 | Reporting branch.
23 | AC_PosControl (Sink) | AP_AHRS pos → AC_WPNav → AC_PosControl → AC_AttitudeControl → AP_Motors | AP_Motors | 4 | Inbound chain to a Sink endpoint.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 19–23

## Slide 77
DEPENDENCY MAP · LAYER 2 · DEPTHS 3, 4, 5, 6, 8
Table 1a — Layer 2 transitive chains (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
24 | AR_PosControl (Sink, Rover) | AP_AHRS pos/vel → AR_PosControl → AR_AttitudeControl → SRV_Channels | SRV_Channels | 3 | Rover actuation endpoint.
25 | AP_Beacon (Source) | AP_Beacon → get_vehicle_position_ned → NavEKF3 RngBcn fusion → AP_AHRS → AP_Motors | AP_Motors | 4 | GPS-denied source.
26 | AP_VisualOdom (Source) | AP_VisualOdom → NavEKF3 external-nav fusion → AP_AHRS → AP_Motors | AP_Motors | 3 | GPS-denied source.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 24–26

## Slide 78
Table 2 — Core Navigation
The navigation hub, the estimator stack and the guidance and mission layer.

## Slide 79
GROUP 1 — CORE PNT REFERENCES · CORE NAVIGATION
Table 2 — Core Navigation
All 28 catalogued rows, with every Notes annotation, flag token and cited path:line range exactly as printed.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | File Path | Line(s) | Function/Class | Role | New Service Location | Notes
1 | libraries/AP_AHRS/AP_AHRS.cpp | 3600-3604 | AP_AHRS::get_location() | Transform | — | [CIRCULAR] Central navigation hub returns the fused Location from the active EKF. Reached via AP::ahrs(). AHRS owns NavEKF2/NavEKF3 while the EKF core reads AHRS/sensor state back through AP_DAL — AHRS↔EKF mutual reference.
2 | libraries/AP_AHRS/AP_AHRS.h | 238-246 | AP_AHRS::groundspeed() | Sink | — | Read accessor returning the already-fused state.ground_speed (m/s). Performs no fusion and produces nothing from a measurement — classified Sink (read accessor), NOT Source.
3 | libraries/AP_AHRS/AP_AHRS.h | 269-277 | AP_AHRS::get_origin()/have_inertial_nav() | Sink | — | Availability/origin read accessors (have_inertial_nav() is a user-cited symbol, L273). They report EKF availability/origin — read accessors, NOT measurement Sources; classified Sink. EKF origin is WRITTEN by the EKF (see #15 calcGpsGoodToAlign / setOrigin).
4 | libraries/AP_AHRS/AP_AHRS.cpp | 1739-1748 | AP_AHRS::get_relative_position_NED_origin() | Transform | — | Geodetic↔NED: origin-relative NED position via active-EKF-type dispatch (DCM/EKF2/EKF3) — performs conversion on read.
5 | libraries/AP_AHRS/AP_AHRS.cpp | 3662-3666 | AP_AHRS::get_velocity_NED() | Transform | — | Exposes the fused NED velocity (nav-hub output of EKF fusion); consumed by crash detection and Rover position control.
# 1–5

## Slide 80
GROUP 1 — CORE PNT REFERENCES · CORE NAVIGATION
Table 2 — Core Navigation (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | File Path | Line(s) | Function/Class | Role | New Service Location | Notes
6 | libraries/AP_NavEKF3/AP_NavEKF3_core.cpp | 627-636 | NavEKF3_core::UpdateFilter() | Transform | — | [CIRCULAR] Extended Kalman Filter predict/fuse step (the core PNT transform). AHRS owns NavEKF2/NavEKF3 while the EKF core reads AHRS/sensor state back through AP_DAL — AHRS↔EKF mutual reference. One of 13 AP_NavEKF3 fusion modules, all catalogued.
7 | libraries/AP_NavEKF3/AP_NavEKF3_PosVelFusion.cpp | 502-511 | NavEKF3_core::SelectVelPosFusion() | Transform | — | [CIRCULAR] GPS position/velocity fusion scheduling; the dtIMUavg<0.005 gate couples EKF fusion cadence to the scheduler loop rate (timing coupling). AHRS owns NavEKF2/NavEKF3 while the EKF core reads AHRS/sensor state back through AP_DAL — AHRS↔EKF mutual reference. One of 13 AP_NavEKF3 fusion modules, all catalogued.
8 | libraries/AP_NavEKF3/AP_NavEKF3_PosVelFusion.cpp | 694-702 | NavEKF3_core::FuseVelPosNED() | Transform | — | Core position/velocity measurement-update (Kalman gain applied to GPS/baro NED innovations). One of 13 AP_NavEKF3 fusion modules, all catalogued.
# 6–8

## Slide 81
GROUP 1 — CORE PNT REFERENCES · CORE NAVIGATION
Table 2 — Core Navigation (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | File Path | Line(s) | Function/Class | Role | New Service Location | Notes
9 | libraries/AP_NavEKF3/AP_NavEKF3_Measurements.cpp | 559-567 | NavEKF3_core::readGpsData() | Transform | — | [CIRCULAR] GPS ingestion into the EKF delayed-time buffer (reads gps.location()/velocity()/status via AP_DAL). This is the GPS→EKF hop omitted earlier (cf. Table 1a chains). AHRS owns NavEKF2/NavEKF3 while the EKF core reads AHRS/sensor state back through AP_DAL — AHRS↔EKF mutual reference. One of 13 AP_NavEKF3 fusion modules, all catalogued.
10 | libraries/AP_NavEKF3/AP_NavEKF3_Control.cpp | 232-240 | NavEKF3_core::setAidingMode() | Transform | — | Navigation aiding-mode state machine (none/relative/absolute) driving which PNT measurements are fused. One of 13 AP_NavEKF3 fusion modules, all catalogued.
11 | libraries/AP_NavEKF3/AP_NavEKF3_MagFusion.cpp | 227-235 | NavEKF3_core::SelectMagFusion() | Transform | — | Magnetometer/yaw fusion scheduling feeding the heading component of the navigation solution. One of 13 AP_NavEKF3 fusion modules, all catalogued.
12 | libraries/AP_NavEKF3/AP_NavEKF3_AirDataFusion.cpp | 193-201 | NavEKF3_core::SelectTasFusion() | Transform | — | True-airspeed / synthetic-sideslip fusion (wind/velocity estimation for fixed-wing nav). One of 13 AP_NavEKF3 fusion modules, all catalogued.
13 | libraries/AP_NavEKF3/AP_NavEKF3_OptFlowFusion.cpp | 21-29 | NavEKF3_core::SelectFlowFusion() | Transform | — | Optical-flow fusion scheduling for GPS-denied velocity/position aiding. One of 13 AP_NavEKF3 fusion modules, all catalogued.
# 9–13

## Slide 82
GROUP 1 — CORE PNT REFERENCES · CORE NAVIGATION
Table 2 — Core Navigation (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | File Path | Line(s) | Function/Class | Role | New Service Location | Notes
14 | libraries/AP_NavEKF3/AP_NavEKF3_Outputs.cpp | 326-334 | NavEKF3_core::getLLH() | Transform | — | EKF position output: converts the filter state to a geodetic Location consumed by AP_AHRS. One of 13 AP_NavEKF3 fusion modules, all catalogued.
15 | libraries/AP_NavEKF3/AP_NavEKF3_VehicleStatus.cpp | 14-22 | NavEKF3_core::calcGpsGoodToAlign() | Transform | — | GPS-quality gate deciding whether the GPS is good enough to align/aid the navigation solution. One of 13 AP_NavEKF3 fusion modules, all catalogued.
16 | libraries/AP_NavEKF3/AP_NavEKF3_GyroBias.cpp | 6-13 | NavEKF3_core::resetGyroBias() | Transform | — | Gyro-bias state reset within the inertial-navigation state vector. One of 13 AP_NavEKF3 fusion modules, all catalogued.
17 | libraries/AP_NavEKF3/AP_NavEKF3_RngBcnFusion.cpp | 95-103 | NavEKF3_core::FuseRngBcn() | Transform | — | Range-beacon (non-GPS) position fusion — consumes AP_Beacon ranges (Table 1 #25). One of 13 AP_NavEKF3 fusion modules, all catalogued.
18 | libraries/AP_NavEKF3/AP_NavEKF3_Logging.cpp | 15-23 | NavEKF3_core::Log_Write_XKF1() | Sink | — | Logs the fused navigation state (pos/vel/attitude) to the dataflash; reads PNT state, drives no control — a logging Sink. One of 13 AP_NavEKF3 fusion modules, all catalogued.
# 14–18

## Slide 83
GROUP 1 — CORE PNT REFERENCES · CORE NAVIGATION
Table 2 — Core Navigation (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | File Path | Line(s) | Function/Class | Role | New Service Location | Notes
19 | libraries/AP_NavEKF3/AP_NavEKF3.cpp | 1846-1854 | NavEKF3::getFilterStatus() | Transform | — | EKF3 frontend: exposes the per-core nav_filter_status (position/velocity validity bits) to vehicle health logic (Group 2).
20 | libraries/AP_NavEKF2/AP_NavEKF2_core.cpp | 528-536 | NavEKF2_core::UpdateFilter() | Transform | — | [CIRCULAR] [DUPLICATED] Second-generation EKF predict/fuse step; selectable alternative to EKF3. AHRS owns NavEKF2/NavEKF3 while the EKF core reads AHRS/sensor state back through AP_DAL — AHRS↔EKF mutual reference. parallel EKF implementation to AP_NavEKF3 (extraction note).
21 | libraries/AP_NavEKF2/AP_NavEKF2_PosVelFusion.cpp | 560-568 | NavEKF2_core::FuseVelPosNED() | Transform | — | [DUPLICATED] EKF2 GPS position/velocity measurement-update; structurally mirrors EKF3 FuseVelPosNED (#8).
22 | libraries/AP_NavEKF/EKFGSF_yaw.cpp | 30-38 | EKFGSF_yaw::update() | Transform | — | Gaussian-Sum-Filter emergency yaw estimator (shared by EKF2/EKF3) providing a GPS-velocity-derived yaw used to recover the navigation solution.
23 | libraries/AC_WPNav/AC_WPNav.cpp | 245-254 | AC_WPNav::set_wp_destination_loc() | Transform | — | Waypoint navigation: converts a Location waypoint to a NEU target (get_vector_NEU_cm) relative to EKF origin.
# 19–23

## Slide 84
GROUP 1 — CORE PNT REFERENCES · CORE NAVIGATION
Table 2 — Core Navigation (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | File Path | Line(s) | Function/Class | Role | New Service Location | Notes
24 | libraries/AP_Mission/AP_Mission.cpp | 552-561 | AP_Mission::get_next_nav_cmd() | Transform | — | Mission-command storage reader + navigation-command sequencing: scans stored commands and returns the next NAV waypoint. NOT a PNT measurement Source — it sequences stored navigation targets (Transform).
25 | libraries/AP_L1_Control/AP_L1_Control.cpp | 226-234 | AP_L1_Control::update_waypoint() | Transform | AfsimL1Behavior::set_leg_ne() -> AP_L1_Control::update_waypoint(prev, next); state via AHRS shim (get_location()/groundspeed_vector()) fed by set_state_ne(); dt via set_update_dt() | Fixed-wing lateral (L1) guidance consuming the AHRS navigation position via _ahrs.get_location() (returns early if unavailable). The same method also reads AP_HAL::micros() at L214 for the dt timing coupling.
26 | libraries/AP_L1_Control/AP_L1_Control.cpp | 79-88 | AP_L1_Control::nav_roll_cd() | Transform | AfsimL1Behavior::get_roll_deg() = nav_roll_cd()/100 -> L1_GetRollDeg; get_lat_accel() -> L1_GetLatAccel | Derives demanded roll (centi-deg) from the lateral-acceleration demand and AHRS pitch.
# 24–26

## Slide 85
GROUP 1 — CORE PNT REFERENCES · CORE NAVIGATION
Table 2 — Core Navigation (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | File Path | Line(s) | Function/Class | Role | New Service Location | Notes
27 | libraries/AP_TECS/AP_TECS.cpp | 1259-1268 | AP_TECS::update_pitch_throttle() | Transform | — | Fixed-wing Total Energy Control (speed/altitude) producing pitch & throttle demands.
28 | libraries/AC_AttitudeControl/AC_AttitudeControl.cpp | 411-419 | AC_AttitudeControl::input_euler_angle_roll_pitch_yaw_cd() | Sink | — | Attitude/rate controller consuming the navigation demand; downstream of all navigation.
# 27–28

## Slide 86
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 2 — Code Snippet (5-10 lines)
Every row’s Code Snippet (5-10 lines), reproduced verbatim from the cited path:line range: one paragraph per source line, in the audit’s own order, with its indentation and its blank lines intact and nothing abbreviated.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
1 | libraries/AP_AHRS/AP_AHRS.cpp · 3600-3604 · AP_AHRS::get_location() bool AP_AHRS::get_location(Location &loc) const { loc = state.location; return state.location_ok; }
2 | libraries/AP_AHRS/AP_AHRS.h · 238-246 · AP_AHRS::groundspeed() // EKF has a better ground speed vector estimate const Vector2f &groundspeed_vector() const { return state.ground_speed_vec; } // return ground speed estimate in meters/second. Used by ground vehicles. float groundspeed(void) const { return state.ground_speed; } const Vector3f &get_accel_ef() const { return state.accel_ef; }
# 1–2

## Slide 87
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 2 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
3 | libraries/AP_AHRS/AP_AHRS.h · 269-277 · AP_AHRS::get_origin()/have_inertial_nav() // returns the inertial navigation origin in lat/lon/alt bool get_origin(Location &ret) const WARN_IF_UNUSED; bool have_inertial_nav() const; // return a ground velocity in meters/second, North/East/Down // order. Must only be called if have_inertial_nav() is true bool get_velocity_NED(Vector3f &vec) const WARN_IF_UNUSED;
4 | libraries/AP_AHRS/AP_AHRS.cpp · 1739-1748 · AP_AHRS::get_relative_position_NED_origin() bool AP_AHRS::get_relative_position_NED_origin(Vector3p &vec) const { switch (active_EKF_type()) { #if AP_AHRS_DCM_ENABLED case EKFType::DCM: return dcm.get_relative_position_NED_origin(vec); #endif #if HAL_NAVEKF2_AVAILABLE case EKFType::TWO: { Vector2p posNE;
# 3–4

## Slide 88
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 2 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
5 | libraries/AP_AHRS/AP_AHRS.cpp · 3662-3666 · AP_AHRS::get_velocity_NED() bool AP_AHRS::get_velocity_NED(Vector3f &vec) const { vec = state.velocity_NED; return state.velocity_NED_ok; }
6 | libraries/AP_NavEKF3/AP_NavEKF3_core.cpp · 627-636 · NavEKF3_core::UpdateFilter() void NavEKF3_core::UpdateFilter(bool predict) { // don't run filter updates if states have not been initialised if (!statesInitialised) { return; } fill_scratch_variables(); // update sensor selection (for affinity)
# 5–6

## Slide 89
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 2 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
7 | libraries/AP_NavEKF3/AP_NavEKF3_PosVelFusion.cpp · 502-511 · NavEKF3_core::SelectVelPosFusion() void NavEKF3_core::SelectVelPosFusion() { // Check if the magnetometer has been fused on that time step and the filter is running at faster than 200 Hz // If so, don't fuse measurements on this time step to reduce frame over-runs // Only allow one time slip to prevent high rate magnetometer data preventing fusion of other measurements if (magFusePerformed && dtIMUavg < 0.005f && !posVelFusionDelayed) { posVelFusionDelayed = true; return; } else { posVelFusionDelayed = false;
8 | libraries/AP_NavEKF3/AP_NavEKF3_PosVelFusion.cpp · 694-702 · NavEKF3_core::FuseVelPosNED() void NavEKF3_core::FuseVelPosNED() { // declare variables used to control access to arrays bool fuseData[6] {}; uint8_t stateIndex; uint8_t obsIndex; // declare variables used by state and covariance update calculations Vector6 R_OBS; // Measurement variances used for fusion
# 7–8

## Slide 90
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 2 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
9 | libraries/AP_NavEKF3/AP_NavEKF3_Measurements.cpp · 559-567 · NavEKF3_core::readGpsData() void NavEKF3_core::readGpsData() { // check for new GPS data const auto &gps = dal.gps(); // limit update rate to avoid overflowing the FIFO buffer if (gps.last_message_time_ms(selected_gps) - lastTimeGpsReceived_ms <= frontend->sensorIntervalMin_ms) { return; }
10 | libraries/AP_NavEKF3/AP_NavEKF3_Control.cpp · 232-240 · NavEKF3_core::setAidingMode() void NavEKF3_core::setAidingMode() { resetDataSource posResetSource = resetDataSource::DEFAULT; resetDataSource velResetSource = resetDataSource::DEFAULT; // Save the previous status so we can detect when it has changed PV_AidingModePrev = PV_AidingMode; setYawSource();
# 9–10

## Slide 91
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 2 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
11 | libraries/AP_NavEKF3/AP_NavEKF3_MagFusion.cpp · 227-235 · NavEKF3_core::SelectMagFusion() void NavEKF3_core::SelectMagFusion() { // clear the flag that lets other processes know that the expensive magnetometer fusion operation has been performed on that time step // used for load levelling magFusePerformed = false; // Store yaw angle when moving for use as a static reference when not moving if (!onGroundNotMoving) { if (fabsF(prevTnb[0][2]) < fabsF(prevTnb[1][2])) {
12 | libraries/AP_NavEKF3/AP_NavEKF3_AirDataFusion.cpp · 193-201 · NavEKF3_core::SelectTasFusion() void NavEKF3_core::SelectTasFusion() { // Check if the magnetometer has been fused on that time step and the filter is running at faster than 200 Hz // If so, don't fuse measurements on this time step to reduce frame over-runs // Only allow one time slip to prevent high rate magnetometer data locking out fusion of other measurements if (magFusePerformed && dtIMUavg < 0.005f && !airSpdFusionDelayed) { airSpdFusionDelayed = true; return; } else {
# 11–12

## Slide 92
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 2 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
13 | libraries/AP_NavEKF3/AP_NavEKF3_OptFlowFusion.cpp · 21-29 · NavEKF3_core::SelectFlowFusion() void NavEKF3_core::SelectFlowFusion() { // Check if the magnetometer has been fused on that time step and the filter is running at faster than 200 Hz // If so, don't fuse measurements on this time step to reduce frame over-runs // Only allow one time slip to prevent high rate magnetometer data preventing fusion of other measurements if (magFusePerformed && dtIMUavg < 0.005f && !optFlowFusionDelayed) { optFlowFusionDelayed = true; return; } else {
14 | libraries/AP_NavEKF3/AP_NavEKF3_Outputs.cpp · 326-334 · NavEKF3_core::getLLH() bool NavEKF3_core::getLLH(Location &loc) const { Location origin; if (getOriginLLH(origin)) { postype_t posD; if (getPosD_local(posD) && PV_AidingMode != AID_NONE) { // Altitude returned is an absolute altitude relative to the WGS-84 spherioid loc.set_alt_cm(origin.alt - posD*100.0, Location::AltFrame::ABSOLUTE); if (filterStatus.flags.horiz_pos_abs ¦¦ filterStatus.flags.horiz_pos_rel) {
# 13–14

## Slide 93
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 2 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
15 | libraries/AP_NavEKF3/AP_NavEKF3_VehicleStatus.cpp · 14-22 · NavEKF3_core::calcGpsGoodToAlign() void NavEKF3_core::calcGpsGoodToAlign(void) { if (inFlight && !finalInflightYawInit && assume_zero_sideslip() && !use_compass()) { // this is a special case where a plane has launched without magnetometer // is now in the air and needs to align yaw to the GPS and start navigating as soon as possible gpsGoodToAlign = true; return; }
16 | libraries/AP_NavEKF3/AP_NavEKF3_GyroBias.cpp · 6-13 · NavEKF3_core::resetGyroBias() void NavEKF3_core::resetGyroBias(void) { stateStruct.gyro_bias.zero(); zeroRows(P,10,12); zeroCols(P,10,12); P[10][10] = sq(radians(0.5f * dtIMUavg)); P[11][11] = P[10][10];
# 15–16

## Slide 94
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 2 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
17 | libraries/AP_NavEKF3/AP_NavEKF3_RngBcnFusion.cpp · 95-103 · NavEKF3_core::FuseRngBcn() void NavEKF3_core::FuseRngBcn() { // declarations ftype pn; ftype pe; ftype pd; ftype bcn_pn; ftype bcn_pe; ftype bcn_pd;
18 | libraries/AP_NavEKF3/AP_NavEKF3_Logging.cpp · 15-23 · NavEKF3_core::Log_Write_XKF1() void NavEKF3_core::Log_Write_XKF1(uint64_t time_us) const { // Write first EKF packet Vector3f euler; Vector2p posNE; postype_t posD; Vector3f velNED; Vector3f gyroBias; float posDownDeriv;
# 17–18

## Slide 95
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 2 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
19 | libraries/AP_NavEKF3/AP_NavEKF3.cpp · 1846-1854 · NavEKF3::getFilterStatus() void NavEKF3::getFilterStatus(nav_filter_status &status) const { if (core) { core[primary].getFilterStatus(status); } else { memset(&status, 0, sizeof(status)); } }
20 | libraries/AP_NavEKF2/AP_NavEKF2_core.cpp · 528-536 · NavEKF2_core::UpdateFilter() void NavEKF2_core::UpdateFilter(bool predict) { // Set the flag to indicate to the filter that the front-end has given permission for a new state prediction cycle to be started startPredictEnabled = predict; // don't run filter updates if states have not been initialised if (!statesInitialised) { return; }
# 19–20

## Slide 96
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 2 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
21 | libraries/AP_NavEKF2/AP_NavEKF2_PosVelFusion.cpp · 560-568 · NavEKF2_core::FuseVelPosNED() void NavEKF2_core::FuseVelPosNED() { // health is set bad until test passed bool velHealth = false; // boolean true if velocity measurements have passed innovation consistency check bool posHealth = false; // boolean true if position measurements have passed innovation consistency check bool hgtHealth = false; // boolean true if height measurements have passed innovation consistency check // declare variables used to check measurement errors Vector3F velInnov;
22 | libraries/AP_NavEKF/EKFGSF_yaw.cpp · 30-38 · EKFGSF_yaw::update() void EKFGSF_yaw::update(const Vector3F &delAng, const Vector3F &delVel, const ftype delAngDT, const ftype delVelDT, bool runEKF, ftype TAS) { // copy to class variables
# 21–22

## Slide 97
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 2 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
23 | libraries/AC_WPNav/AC_WPNav.cpp · 245-254 · AC_WPNav::set_wp_destination_loc() bool AC_WPNav::set_wp_destination_loc(const Location& destination) { bool is_terrain_alt; Vector3f dest_neu_cm; // convert destination location to vector if (!get_vector_NEU_cm(destination, dest_neu_cm, is_terrain_alt)) { return false; }
24 | libraries/AP_Mission/AP_Mission.cpp · 552-561 · AP_Mission::get_next_nav_cmd() bool AP_Mission::get_next_nav_cmd(uint16_t start_index, Mission_Command& cmd) { // search until the end of the mission command list for (uint16_t cmd_index = start_index; cmd_index < (unsigned)_cmd_total; cmd_index++) { // get next command if (!get_next_cmd(cmd_index, cmd, false)) { // no more commands so return failure return false; } // if found a "navigation" command then return it
# 23–24

## Slide 98
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 2 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
25 | libraries/AP_L1_Control/AP_L1_Control.cpp · 226-234 · AP_L1_Control::update_waypoint() // Calculate L1 gain required for specified damping float K_L1 = 4.0f * _L1_damping * _L1_damping; // Get current position and velocity if (_ahrs.get_location(_current_loc) == false) { // if no GPS loc available, maintain last nav/target_bearing _data_is_stale = true; return; }
26 | libraries/AP_L1_Control/AP_L1_Control.cpp · 79-88 · AP_L1_Control::nav_roll_cd() int32_t AP_L1_Control::nav_roll_cd(void) const { float ret; /* formula can be obtained through equations of balanced spiral: liftForce * cos(roll) = gravityForce * cos(pitch); liftForce * sin(roll) = gravityForce * lateralAcceleration / gravityAcceleration; // as mass = gravityForce/gravityAcceleration see issue 24319 [https://github.com/ArduPilot/ardupilot/issues/24319] Multiplier 100.0f is for converting degrees to centidegrees Made changes to avoid zero division as proposed by Andrew Tridgell: https://github.com/ArduPilot/ardupilot/pull/24331#discussion_r1267798397
# 25–26

## Slide 99
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 2 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
27 | libraries/AP_TECS/AP_TECS.cpp · 1259-1268 · AP_TECS::update_pitch_throttle() void AP_TECS::update_pitch_throttle(int32_t hgt_dem_cm, int32_t EAS_dem_cm, enum AP_FixedWing::FlightStage flight_stage, float distance_beyond_land_wp, int32_t ptchMinCO_cd, int16_t throttle_nudge, float hgt_afe, float load_factor, float pitch_trim_deg) {
28 | libraries/AC_AttitudeControl/AC_AttitudeControl.cpp · 411-419 · AC_AttitudeControl::input_euler_angle_roll_pitch_yaw_cd() void AC_AttitudeControl::input_euler_angle_roll_pitch_yaw_cd(float euler_roll_angle_cd, float euler_pitch_angle_cd, float euler_yaw_angle_cd, bool slew_yaw) { // Convert from centidegrees on public interface to radians const float euler_roll_angle_rad = cd_to_rad(euler_roll_angle_cd); const float euler_pitch_angle_rad = cd_to_rad(euler_pitch_angle_cd); const float euler_yaw_angle_rad = cd_to_rad(euler_yaw_angle_cd); input_euler_angle_roll_pitch_yaw_rad(euler_roll_angle_rad, euler_pitch_angle_rad, euler_yaw_angle_rad, slew_yaw); }
# 27–28

## Slide 100
DEPENDENCY MAP · LAYER 1 · DIRECT EDGES
Table 2a — Layer 1 dependency map
Table 2a: Layer 1 — direct callers / callees with typed dependency
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Component/Function | Directly Calls | Directly Called By | Dependency Type
1 | AP_AHRS::get_location() | returns state.location (fused by active EKF) | ArduCopter inertia.cpp; commands.cpp; GCS_MAVLink_Copter.cpp | Function call
2 | AP_AHRS::groundspeed() | returns state.ground_speed | Rover speed control; GCS reporting | Data dependency
3 | AP_AHRS::have_inertial_nav()/get_origin() | active_EKF_type(); EKF origin | Copter::ekf_has_absolute_position (system.cpp); ekf_check | Function call
4 | AP_AHRS::get_relative_position_NED_origin() | dcm/EKF2/EKF3 get_relative_position_NED_origin() | AR_PosControl::update; AP_InertialNav::update | Inheritance/Interface
5 | AP_AHRS::get_velocity_NED() | returns state.velocity_NED | Copter::crash_check; AR_PosControl | Data dependency
6 | NavEKF3_core::UpdateFilter() | fill_scratch_variables(); Select*Fusion(); CovariancePrediction() | NavEKF3::UpdateFilter() (frontend, per core) | Function call
7 | NavEKF3_core::SelectVelPosFusion() | readGpsData(); FuseVelPosNED() | NavEKF3_core::UpdateFilter() | Function call
8 | NavEKF3_core::FuseVelPosNED() | Kalman gain on NED pos/vel innovations; correct stateStruct | NavEKF3_core::SelectVelPosFusion() | Function call
# 1–8

## Slide 101
DEPENDENCY MAP · LAYER 1 · DIRECT EDGES
Table 2a — Layer 1 dependency map (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Component/Function | Directly Calls | Directly Called By | Dependency Type
9 | NavEKF3_core::readGpsData() | gps.location(); gps.velocity(); gps.status() (via AP_DAL); storedGPS.push() | NavEKF3_core::SelectVelPosFusion()/UpdateFilter() | Function call
10 | NavEKF3_core::setAidingMode() | checks gpsGoodToAlign, posTimeout; sets PV_AidingMode | NavEKF3_core::controlFilterModes() | Function call
11 | NavEKF3_core::SelectMagFusion() | FuseMagnetometer(); FuseEulerYaw() | NavEKF3_core::UpdateFilter() | Function call
12 | NavEKF3_core::SelectTasFusion() | FuseAirspeed() | NavEKF3_core::UpdateFilter() | Function call
13 | NavEKF3_core::SelectFlowFusion() | EstimateTerrainOffset(); FuseOptFlow() | NavEKF3_core::UpdateFilter() | Function call
14 | NavEKF3_core::getLLH() | outputDataNew / EKF_origin; builds Location | NavEKF3::getLLH() (frontend) -> AP_AHRS | Function call
15 | NavEKF3_core::calcGpsGoodToAlign() | reads gps metrics; sets gpsGoodToAlign | NavEKF3_core::readGpsData()/setAidingMode() | Function call
16 | NavEKF3_core::resetGyroBias() | zeroes stateStruct.gyro_bias; resets P | NavEKF3_core::InitialiseFilterBootstrap() | Function call
17 | NavEKF3_core::FuseRngBcn() | range innovations; correct NED position states | NavEKF3_core::SelectRngBcnFusion() | Function call
18 | NavEKF3_core::Log_Write_XKF1() | getEulerAngles(); getVelNED(); getLLH(); AP::logger().Write* | NavEKF3_core::Log_Write() | Function call
# 9–18

## Slide 102
DEPENDENCY MAP · LAYER 1 · DIRECT EDGES
Table 2a — Layer 1 dependency map (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Component/Function | Directly Calls | Directly Called By | Dependency Type
19 | NavEKF3::getFilterStatus() | core[].getFilterStatus() | Copter::position_ok(); ekf_check() | Function call
20 | NavEKF2_core::UpdateFilter() | Select*Fusion(); CovariancePrediction() | NavEKF2::UpdateFilter() (frontend) | Function call
21 | NavEKF2_core::FuseVelPosNED() | Kalman gain on NED pos/vel innovations | NavEKF2_core::SelectVelPosFusion() | Function call
22 | EKFGSF_yaw::update() | predict()/correct() per model; AHRS complementary filter | NavEKF3_core::runYawEstimatorPrediction() | Function call
23 | AC_WPNav::set_wp_destination_loc() | get_vector_NEU_cm(); set_wp_destination_NEU_cm() | ArduCopter mode_auto / mode_guided | Function call
24 | AP_Mission::get_next_nav_cmd() | get_next_cmd(); read_cmd_from_storage() | ArduCopter/Plane mission sequencing | Function call
25 | AP_L1_Control::update_waypoint() | _ahrs.get_location(_current_loc) | ArduPlane navigation.cpp update loop | Function call
26 | AP_L1_Control::nav_roll_cd() | _ahrs.get_pitch_rad(); _latAccDem | Plane::calc_nav_roll() (Attitude.cpp L608) | Function call
27 | AP_TECS::update_pitch_throttle() | _update_pitch(); _update_throttle_with_airspeed() | ArduPlane stabilize/auto pitch loop | Function call
28 | AC_AttitudeControl::input_euler_angle_roll_pitch_yaw_cd() | input_euler_angle_roll_pitch_yaw_rad() | ArduCopter/ArduPlane flight-mode run() | Function call
# 19–28

## Slide 103
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 2a — Layer 1 Code Snippet
Every row’s Code Snippet, reproduced verbatim from the cited path:line range: one paragraph per source line, in the audit’s own order, with its indentation and its blank lines intact and nothing abbreviated.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
1 | AP_AHRS::get_location() · Function call bool AP_AHRS::get_location(Location &loc) const { loc = state.location; return state.location_ok; }
2 | AP_AHRS::groundspeed() · Data dependency // EKF has a better ground speed vector estimate const Vector2f &groundspeed_vector() const { return state.ground_speed_vec; } // return ground speed estimate in meters/second. Used by ground vehicles. float groundspeed(void) const { return state.ground_speed; } const Vector3f &get_accel_ef() const { return state.accel_ef; }
# 1–2

## Slide 104
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 2a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
3 | AP_AHRS::have_inertial_nav()/get_origin() · Function call // returns the inertial navigation origin in lat/lon/alt bool get_origin(Location &ret) const WARN_IF_UNUSED; bool have_inertial_nav() const; // return a ground velocity in meters/second, North/East/Down // order. Must only be called if have_inertial_nav() is true bool get_velocity_NED(Vector3f &vec) const WARN_IF_UNUSED;
4 | AP_AHRS::get_relative_position_NED_origin() · Inheritance/Interface bool AP_AHRS::get_relative_position_NED_origin(Vector3p &vec) const { switch (active_EKF_type()) { #if AP_AHRS_DCM_ENABLED case EKFType::DCM: return dcm.get_relative_position_NED_origin(vec); #endif #if HAL_NAVEKF2_AVAILABLE case EKFType::TWO: { Vector2p posNE;
# 3–4

## Slide 105
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 2a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
5 | AP_AHRS::get_velocity_NED() · Data dependency bool AP_AHRS::get_velocity_NED(Vector3f &vec) const { vec = state.velocity_NED; return state.velocity_NED_ok; }
6 | NavEKF3_core::UpdateFilter() · Function call void NavEKF3_core::UpdateFilter(bool predict) { // don't run filter updates if states have not been initialised if (!statesInitialised) { return; } fill_scratch_variables(); // update sensor selection (for affinity)
# 5–6

## Slide 106
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 2a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
7 | NavEKF3_core::SelectVelPosFusion() · Function call void NavEKF3_core::SelectVelPosFusion() { // Check if the magnetometer has been fused on that time step and the filter is running at faster than 200 Hz // If so, don't fuse measurements on this time step to reduce frame over-runs // Only allow one time slip to prevent high rate magnetometer data preventing fusion of other measurements if (magFusePerformed && dtIMUavg < 0.005f && !posVelFusionDelayed) { posVelFusionDelayed = true; return; } else { posVelFusionDelayed = false;
8 | NavEKF3_core::FuseVelPosNED() · Function call void NavEKF3_core::FuseVelPosNED() { // declare variables used to control access to arrays bool fuseData[6] {}; uint8_t stateIndex; uint8_t obsIndex; // declare variables used by state and covariance update calculations Vector6 R_OBS; // Measurement variances used for fusion
# 7–8

## Slide 107
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 2a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
9 | NavEKF3_core::readGpsData() · Function call void NavEKF3_core::readGpsData() { // check for new GPS data const auto &gps = dal.gps(); // limit update rate to avoid overflowing the FIFO buffer if (gps.last_message_time_ms(selected_gps) - lastTimeGpsReceived_ms <= frontend->sensorIntervalMin_ms) { return; }
10 | NavEKF3_core::setAidingMode() · Function call void NavEKF3_core::setAidingMode() { resetDataSource posResetSource = resetDataSource::DEFAULT; resetDataSource velResetSource = resetDataSource::DEFAULT; // Save the previous status so we can detect when it has changed PV_AidingModePrev = PV_AidingMode; setYawSource();
# 9–10

## Slide 108
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 2a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
11 | NavEKF3_core::SelectMagFusion() · Function call void NavEKF3_core::SelectMagFusion() { // clear the flag that lets other processes know that the expensive magnetometer fusion operation has been performed on that time step // used for load levelling magFusePerformed = false; // Store yaw angle when moving for use as a static reference when not moving if (!onGroundNotMoving) { if (fabsF(prevTnb[0][2]) < fabsF(prevTnb[1][2])) {
12 | NavEKF3_core::SelectTasFusion() · Function call void NavEKF3_core::SelectTasFusion() { // Check if the magnetometer has been fused on that time step and the filter is running at faster than 200 Hz // If so, don't fuse measurements on this time step to reduce frame over-runs // Only allow one time slip to prevent high rate magnetometer data locking out fusion of other measurements if (magFusePerformed && dtIMUavg < 0.005f && !airSpdFusionDelayed) { airSpdFusionDelayed = true; return; } else {
# 11–12

## Slide 109
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 2a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
13 | NavEKF3_core::SelectFlowFusion() · Function call void NavEKF3_core::SelectFlowFusion() { // Check if the magnetometer has been fused on that time step and the filter is running at faster than 200 Hz // If so, don't fuse measurements on this time step to reduce frame over-runs // Only allow one time slip to prevent high rate magnetometer data preventing fusion of other measurements if (magFusePerformed && dtIMUavg < 0.005f && !optFlowFusionDelayed) { optFlowFusionDelayed = true; return; } else {
14 | NavEKF3_core::getLLH() · Function call bool NavEKF3_core::getLLH(Location &loc) const { Location origin; if (getOriginLLH(origin)) { postype_t posD; if (getPosD_local(posD) && PV_AidingMode != AID_NONE) { // Altitude returned is an absolute altitude relative to the WGS-84 spherioid loc.set_alt_cm(origin.alt - posD*100.0, Location::AltFrame::ABSOLUTE); if (filterStatus.flags.horiz_pos_abs ¦¦ filterStatus.flags.horiz_pos_rel) {
# 13–14

## Slide 110
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 2a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
15 | NavEKF3_core::calcGpsGoodToAlign() · Function call void NavEKF3_core::calcGpsGoodToAlign(void) { if (inFlight && !finalInflightYawInit && assume_zero_sideslip( ) && !use_compass()) { // this is a special case where a plane has launched without magnetometer // is now in the air and needs to align yaw to the GPS and start navigating as soon as possible gpsGoodToAlign = true; return; }
16 | NavEKF3_core::resetGyroBias() · Function call void NavEKF3_core::resetGyroBias(void) { stateStruct.gyro_bias.zero(); zeroRows(P,10,12); zeroCols(P,10,12); P[10][10] = sq(radians(0.5f * dtIMUavg)); P[11][11] = P[10][10];
# 15–16

## Slide 111
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 2a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
17 | NavEKF3_core::FuseRngBcn() · Function call void NavEKF3_core::FuseRngBcn() { // declarations ftype pn; ftype pe; ftype pd; ftype bcn_pn; ftype bcn_pe; ftype bcn_pd;
18 | NavEKF3_core::Log_Write_XKF1() · Function call void NavEKF3_core::Log_Write_XKF1(uint64_t time_us) const { // Write first EKF packet Vector3f euler; Vector2p posNE; postype_t posD; Vector3f velNED; Vector3f gyroBias; float posDownDeriv;
# 17–18

## Slide 112
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 2a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
19 | NavEKF3::getFilterStatus() · Function call void NavEKF3::getFilterStatus(nav_filter_status &status) const { if (core) { core[primary].getFilterStatus(status); } else { memset(&status, 0, sizeof(status)); } }
20 | NavEKF2_core::UpdateFilter() · Function call void NavEKF2_core::UpdateFilter(bool predict) { // Set the flag to indicate to the filter that the front-end has given permission for a new state prediction cycle to be started startPredictEnabled = predict; // don't run filter updates if states have not been initialised if (!statesInitialised) { return; }
# 19–20

## Slide 113
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 2a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
21 | NavEKF2_core::FuseVelPosNED() · Function call void NavEKF2_core::FuseVelPosNED() { // health is set bad until test passed bool velHealth = false; // boolean true if velocity measurements have passed innovation consistency check bool posHealth = false; // boolean true if position measurements have passed innovation consistency check bool hgtHealth = false; // boolean true if height measurements have passed innovation consistency check // declare variables used to check measurement errors Vector3F velInnov;
22 | EKFGSF_yaw::update() · Function call void EKFGSF_yaw::update(const Vector3F &delAng, const Vector3F &delVel, const ftype delAngDT, const ftype delVelDT, bool runEKF, ftype TAS) { // copy to class variables
# 21–22

## Slide 114
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 2a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
23 | AC_WPNav::set_wp_destination_loc() · Function call bool AC_WPNav::set_wp_destination_loc(const Location& destination) { bool is_terrain_alt; Vector3f dest_neu_cm; // convert destination location to vector if (!get_vector_NEU_cm(destination, dest_neu_cm, is_terrain_alt)) { return false; }
24 | AP_Mission::get_next_nav_cmd() · Function call bool AP_Mission::get_next_nav_cmd(uint16_t start_index, Mission_Command& cmd) { // search until the end of the mission command list for (uint16_t cmd_index = start_index; cmd_index < (unsigned)_cmd_total; cmd_index++) { // get next command if (!get_next_cmd(cmd_index, cmd, false)) { // no more commands so return failure return false; } // if found a "navigation" command then return it
# 23–24

## Slide 115
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 2a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
25 | AP_L1_Control::update_waypoint() · Function call // Calculate L1 gain required for specified damping float K_L1 = 4.0f * _L1_damping * _L1_damping; // Get current position and velocity if (_ahrs.get_location(_current_loc) == false) { // if no GPS loc available, maintain last nav/target_bearing _data_is_stale = true; return; }
26 | AP_L1_Control::nav_roll_cd() · Function call int32_t AP_L1_Control::nav_roll_cd(void) const { float ret; /* formula can be obtained through equations of balanced spiral: liftForce * cos(roll) = gravityForce * cos(pitch); liftForce * sin(roll) = gravityForce * lateralAcceleration / gravityAcceleration; // as mass = gravityForce/gravityAcceleration see issue 24319 [https://github.com/ArduPilot/ardupilot/issues/24319] Multiplier 100.0f is for converting degrees to centidegrees Made changes to avoid zero division as proposed by Andrew Tridgell: https://github.com/ArduPilot/ardupilot/pull/24331#discussion_r1267798397
# 25–26

## Slide 116
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 2a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
27 | AP_TECS::update_pitch_throttle() · Function call void AP_TECS::update_pitch_throttle(int32_t hgt_dem_cm, int32_t EAS_dem_cm, enum AP_FixedWing::FlightStage flight_stage, float distance_beyond_land_wp, int32_t ptchMinCO_cd, int16_t throttle_nudge, float hgt_afe, float load_factor, float pitch_trim_deg) {
28 | AC_AttitudeControl::input_euler_angle_roll_pitch_yaw_cd() · Function call void AC_AttitudeControl::input_euler_angle_roll_pitch_yaw_cd(float euler_roll_angle_cd, float euler_pitch_angle_cd, float euler_yaw_angle_cd, bool slew_yaw) { // Convert from centidegrees on public interface to radians const float euler_roll_angle_rad = cd_to_rad(euler_roll_angle_cd); const float euler_pitch_angle_rad = cd_to_rad(euler_pitch_angle_cd); const float euler_yaw_angle_rad = cd_to_rad(euler_yaw_angle_cd ); input_euler_angle_roll_pitch_yaw_rad(euler_roll_angle_rad, euler_pitch_angle_rad, euler_yaw_angle_rad, slew_yaw); }
# 27–28

## Slide 117
DEPENDENCY MAP · LAYER 2 · DEPTHS 3, 4
Table 2a — Layer 2 transitive chains
Table 2a: Layer 2 — full transitive chain, final consumer & hop depth
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
1 | AP_GPS (via AP_AHRS) — user example | AP_GPS → AP_AHRS::get_location() → Plane::navigate() [ArduPlane/navigation.cpp:86] → ModeAuto::navigate() [ArduPlane/mode_auto.cpp:124] | ModeAuto::navigate() [ArduPlane/mode_auto.cpp:124] | 3 | USER-SUPPLIED example (AAP 0.1.3/0.5.4). The literal example named 'ArduPlane::flight_mode_auto()', which does NOT exist in this snapshot; normalized to the real symbols Plane::navigate() and ModeAuto::navigate(). navigate() is gated on have_position (Table 5 #5).
2 | AP_AHRS::groundspeed() | AP_GPS velocity → NavEKF3 fusion → AP_AHRS::groundspeed() → Rover speed control → SRV_Channels | SRV_Channels | 4 | Ground-vehicle speed branch.
3 | AP_AHRS::have_inertial_nav() | EKF health → AP_AHRS::have_inertial_nav() → Copter::ekf_has_absolute_position → position_ok() → set_mode gate | mode transition (allow/deny) | 4 | Also observed in Group 2 (Table 5 #7).
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 1–3

## Slide 118
DEPENDENCY MAP · LAYER 2 · DEPTHS 3, 4
Table 2a — Layer 2 transitive chains (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
4 | AP_AHRS::get_relative_position_NED_origin() | EKF → AHRS NED dispatch → {AR_PosControl ¦ AP_InertialNav} → actuators | SRV_Channels / AP_Motors | 3 | Geodetic↔NED transform branch.
5 | AP_AHRS::get_velocity_NED() | EKF → AHRS → Copter::crash_check / controllers → disarm / AP_Motors | AP_Motors / disarm | 3 | Velocity consumers.
6 | NavEKF3_core::UpdateFilter() | {AP_GPS, AP_InertialSensor, AP_Baro} → NavEKF3::UpdateFilter → AP_AHRS estimate → all consumers | AP_Motors | 3 | [CIRCULAR] AHRS↔EKF; EKF reads AP_DAL.
7 | NavEKF3 PosVel fusion (Select) | readGpsData buffer → SelectVelPosFusion → FuseVelPosNED → EKF states → AP_AHRS | AP_AHRS | 4 | Core fusion scheduling.
8 | NavEKF3_core::FuseVelPosNED() | GPS NED innovations → FuseVelPosNED → stateStruct correction → getLLH → AP_AHRS::get_location() | AP_AHRS | 4 | Position/velocity measurement-update.
9 | NavEKF3_core::readGpsData() | AP_GPS::location()/velocity() → readGpsData → storedGPS buffer → SelectVelPosFusion → FuseVelPosNED | EKF state correction | 4 | Explicit GPS→EKF ingestion hop (cf. Table 1a chains).
10 | NavEKF3_core::setAidingMode() | GPS health → setAidingMode → PV_AidingMode → SelectVelPosFusion → EKF states | EKF aiding state | 4 | Nav aiding-mode control.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 4–10

## Slide 119
DEPENDENCY MAP · LAYER 2 · DEPTHS 3, 4
Table 2a — Layer 2 transitive chains (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
11 | NavEKF3_core::SelectMagFusion() | magnetometer → SelectMagFusion → FuseMagnetometer → yaw state → AP_AHRS heading | AP_AHRS | 4 | Heading component.
12 | NavEKF3_core::SelectTasFusion() | airspeed → SelectTasFusion → FuseAirspeed → wind/vel states → AP_AHRS::wind_estimate | AP_AHRS | 4 | Wind/velocity.
13 | NavEKF3_core::SelectFlowFusion() | optical flow → SelectFlowFusion → FuseOptFlow → vel/pos states → AP_AHRS | AP_AHRS | 4 | GPS-denied aiding.
14 | NavEKF3_core::getLLH() | EKF state → getLLH → NavEKF3::getLLH (frontend) → AP_AHRS::get_location() → nav consumers | AP_AHRS / consumers | 4 | EKF position output edge.
15 | NavEKF3_core::calcGpsGoodToAlign() | AP_GPS metrics → calcGpsGoodToAlign → gpsGoodToAlign → setAidingMode → EKF origin set | EKF origin / aiding | 4 | GPS quality gate.
16 | NavEKF3_core::resetGyroBias() | InitialiseFilterBootstrap → resetGyroBias → stateStruct.gyro_bias → state prediction | EKF prediction | 3 | Bias init.
17 | NavEKF3_core::FuseRngBcn() | AP_Beacon ranges → FuseRngBcn → EKF NED position correction → AP_AHRS | AP_AHRS | 3 | Non-GPS position fusion.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 11–17

## Slide 120
DEPENDENCY MAP · LAYER 2 · DEPTHS 3, 4
Table 2a — Layer 2 transitive chains (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
18 | NavEKF3_core::Log_Write_XKF1() | EKF states → Log_Write_XKF1 → AP_Logger → dataflash/SD log | dataflash log | 3 | Logging Sink branch.
19 | NavEKF3::getFilterStatus() | EKF core status bits → NavEKF3::getFilterStatus → AP_AHRS → Copter::position_ok()/ekf_check() | vehicle health logic | 3 | Status output feeds Group 2.
20 | NavEKF2_core::UpdateFilter() | {AP_GPS, INS, Baro} → NavEKF2::UpdateFilter → AP_AHRS (when EKF2 active) → consumers | AP_Motors | 3 | [CIRCULAR] [DUPLICATED] parallel EKF to EKF3.
21 | NavEKF2_core::FuseVelPosNED() | GPS NED → NavEKF2 FuseVelPosNED → EKF2 states → AP_AHRS | AP_AHRS | 3 | [DUPLICATED] mirrors EKF3 #8.
22 | EKFGSF_yaw::update() | AP_GPS velocity + IMU → EKFGSF_yaw::update → emergency yaw → EKF yaw reset → AP_AHRS | AP_AHRS | 4 | Yaw-recovery branch.
23 | AC_WPNav | AP_AHRS pos → AC_WPNav target → AC_PosControl → AC_AttitudeControl → AP_Motors | AP_Motors | 4 | Multirotor waypoint path.
24 | AP_Mission | mission storage → get_next_nav_cmd → mode_auto → AC_WPNav → controllers | AP_Motors | 4 | Mission sequencing path.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 18–24

## Slide 121
DEPENDENCY MAP · LAYER 2 · DEPTHS 3, 4
Table 2a — Layer 2 transitive chains (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
25 | AP_L1_Control::update_waypoint() | AP_AHRS pos → L1 guidance → nav_roll_cd() → Plane::calc_nav_roll → SRV_Channels | SRV_Channels | 4 | Fixed-wing lateral path.
26 | AP_L1_Control::nav_roll_cd() | L1 latAccDem → nav_roll_cd() → Plane::calc_nav_roll → SRV_Channels | SRV_Channels | 3 | Roll-demand branch.
27 | AP_TECS | airspeed/alt demand → TECS update_pitch_throttle → pitch/throttle → SRV_Channels | SRV_Channels | 3 | Energy/altitude branch.
28 | AC_AttitudeControl (Sink) | nav demand → input_euler_* → attitude_controller_run_quat → rate_controller_run → AP_Motors | AP_Motors | 4 | Inbound chain to attitude Sink.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 25–28

## Slide 122
Table 3 — Core Timing
The monotonic clock, the real-time clock and the scheduler cadence every PNT task is stamped against.

## Slide 123
GROUP 1 — CORE PNT REFERENCES · CORE TIMING
Table 3 — Core Timing
All 9 catalogued rows, with every Notes annotation, flag token and cited path:line range exactly as printed.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | File Path | Line(s) | Function/Class | Role | Notes
1 | libraries/AP_HAL/system.h | 15-20 | AP_HAL::micros()/millis()/micros64()/millis64() | Source | Monotonic time backbone (user-cited micros()/millis()). Free functions in the AP_HAL namespace backed by the board RTOS timer; the time primitive every PNT subsystem stamps against.
2 | libraries/AP_RTC/AP_RTC.h | 32-40 | AP_RTC::get_utc_usec() | Source | UTC wall-clock time in microseconds (returns false if unavailable). The absolute-time API consumed for logging and GPS-time conversion.
3 | libraries/AP_RTC/AP_RTC.cpp | 56-65 | AP_RTC::set_utc_usec() | Transform | Time-SOURCE ARBITRATION: accepts a new UTC time only if its source_type out-ranks the current rtc_source_type (GPS > GCS > HW). Selects the best clock source.
4 | libraries/AP_RTC/JitterCorrection.cpp | 50-58 | JitterCorrection::correct_offboard_timestamp_usec() | Transform | Time synchronization: maps an offboard (remote-system) timestamp onto the local clock by tracking the minimum observed link offset — rejects 'from the future' samples.
5 | libraries/AP_Scheduler/AP_Scheduler.cpp | 354-363 | AP_Scheduler::loop() | Transform | Main-loop timing core: stamps each loop with AP_HAL::micros64() and derives the measured loop time. Drives the cadence of every periodic PNT task (EKF predict/fuse, AHRS, control).
6 | libraries/AP_Scheduler/AP_Scheduler.cpp | 168-176 | AP_Scheduler::tick() | Source | Increments the loop tick counters (_tick_counter / _tick_counter32) that index task scheduling intervals.
7 | libraries/AP_Scheduler/AP_Scheduler.h | 149-155 | AP_Scheduler::get_loop_period_us() | Transform | Loop-rate→period derivation: _loop_period_us = 1000000UL / _loop_rate_hz. Couples the configured loop rate to the per-loop time budget and to controller/EKF dt.
# 1–7

## Slide 124
GROUP 1 — CORE PNT REFERENCES · CORE TIMING
Table 3 — Core Timing (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | File Path | Line(s) | Function/Class | Role | Notes
8 | libraries/AP_GPS/AP_GPS.h | 409-418 | AP_GPS::time_week_ms()/time_week() | Source | [MULTI-CATEGORY] GPS time-of-week (ms-of-week + week number) — the TIMING facet of the GPS_State that also carries Positioning (Table 1 #4/#17). Emitted separately here per the multi-category rule.
9 | libraries/AP_HAL/Scheduler.h | 13-21 | AP_HAL::Scheduler::delay()/delay_microseconds() | Source | Abstract HAL timing-service interface (pure virtual; implemented by the board backend — ChibiOS / Linux / SITL). Supplies the time-blocking primitives delay() / delay_microseconds() and the periodic-task registration register_timer_process() / register_io_process() (lines 60-64) on which the main loop is built. Distinct from the AP_Scheduler library (#5-#7) and the AP_HAL::micros()/millis() clock primitives in system.h (#1).
# 8–9

## Slide 125
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 3 — Code Snippet (5-10 lines)
Every row’s Code Snippet (5-10 lines), reproduced verbatim from the cited path:line range: one paragraph per source line, in the audit’s own order, with its indentation and its blank lines intact and nothing abbreviated.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
1 | libraries/AP_HAL/system.h · 15-20 · AP_HAL::micros()/millis()/micros64()/millis64() uint16_t micros16(); uint32_t micros(); uint32_t millis(); uint16_t millis16(); uint64_t micros64(); uint64_t millis64();
2 | libraries/AP_RTC/AP_RTC.h · 32-40 · AP_RTC::get_utc_usec() /* get clock in UTC microseconds. Returns false if it is not available. */ bool get_utc_usec(uint64_t &usec) const; // set the system time. If the time has already been set by // something better (according to source_type), this set will be // ignored. void set_utc_usec(uint64_t time_utc_usec, source_type type);
# 1–2

## Slide 126
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 3 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
3 | libraries/AP_RTC/AP_RTC.cpp · 56-65 · AP_RTC::set_utc_usec() // only allow time to be moved forward from the same sourcetype // while the vehicle is disarmed: if (hal.util->get_soft_armed()) { if (type >= rtc_source_type) { // e.g. system-time message when we've been set by the GPS return; } } else { // vehicle is disarmed; accept (e.g.) GPS time source updates if (type > rtc_source_type) {
4 | libraries/AP_RTC/JitterCorrection.cpp · 50-58 · JitterCorrection::correct_offboard_timestamp_usec() uint64_t JitterCorrection::correct_offboard_timestamp_usec(uint64_t offboard_usec, uint64_t local_usec) { int64_t diff_us = int64_t(local_usec) - int64_t(offboard_usec); if (!initialised ¦¦ diff_us < link_offset_usec) { // this message arrived from the remote system with a // timestamp that would imply the message was from the // future. We know that isn't possible, so we adjust down the
# 3–4

## Slide 127
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 3 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
5 | libraries/AP_Scheduler/AP_Scheduler.cpp · 354-363 · AP_Scheduler::loop() hal.util->persistent_data.scheduler_task = -1; _loop_sample_time_us = AP_HAL::micros64(); const uint32_t sample_time_us = uint32_t(_loop_sample_time_us); if (_loop_timer_start_us == 0) { _loop_timer_start_us = sample_time_us; _last_loop_time_s = get_loop_period_s(); } else { _last_loop_time_s = (sample_time_us - _loop_timer_start_us) * 1.0e-6;
6 | libraries/AP_Scheduler/AP_Scheduler.cpp · 168-176 · AP_Scheduler::tick() void AP_Scheduler::tick(void) { _tick_counter++; _tick_counter32++; } #if CONFIG_HAL_BOARD == HAL_BOARD_SITL /* fill stack with NaN so we can catch use of uninitialised stack
# 5–6

## Slide 128
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 3 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
7 | libraries/AP_Scheduler/AP_Scheduler.h · 149-155 · AP_Scheduler::get_loop_period_us() // get the time-allowed-per-loop in microseconds uint32_t get_loop_period_us() { if (_loop_period_us == 0) { _loop_period_us = 1000000UL / _loop_rate_hz; } return _loop_period_us; }
8 | libraries/AP_GPS/AP_GPS.h · 409-418 · AP_GPS::time_week_ms()/time_week() // GPS time of week in milliseconds uint32_t time_week_ms(uint8_t instance) const { return state[instance].time_week_ms; } uint32_t time_week_ms() const { return time_week_ms(primary_instance); } // GPS week uint16_t time_week(uint8_t instance) const {
# 7–8

## Slide 129
GROUP 1 — CORE PNT REFERENCES · VERBATIM SOURCE LINES
Table 3 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
9 | libraries/AP_HAL/Scheduler.h · 13-21 · AP_HAL::Scheduler::delay()/delay_microseconds() Scheduler() {} virtual void init() = 0; virtual void delay(uint16_t ms) = 0; /* delay for the given number of microseconds. This needs to be as accurate as possible - preferably within 100 microseconds. */ virtual void delay_microseconds(uint16_t us) = 0;
# 9

## Slide 130
DEPENDENCY MAP · LAYER 1 · DIRECT EDGES
Table 3a — Layer 1 dependency map
Table 3a: Layer 1 — direct callers / callees with typed dependency
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Component/Function | Directly Calls | Directly Called By | Dependency Type
1 | AP_HAL::micros() / millis() | board RTOS/HAL timer backend | EKF, AP_Scheduler, AP_GPS, all failsafes (ubiquitous) | Function call
2 | AP_RTC::get_utc_usec() — via AP::rtc() | AP::rtc().get_utc_usec(rtc) | AP_Scheduler::Log_Write_Performance ; AP_Logger; AP_Stats; AP_NMEA_Output | Shared global/singleton
3 | AP_RTC::set_utc_usec() (source arbitration) | reads hal.util->get_soft_armed(); compares & writes rtc_source_type | AP_GPS (GPS time); GCS SYSTEM_TIME; AP_BoardConfig (HW RTC) | Data dependency
4 | JitterCorrection::correct_offboard_timestamp_usec() | computes diff_us; updates link_offset_usec | AP_RTC; DroneCAN/MAVLink timestamp consumers | Function call
5 | AP_Scheduler::loop() | AP_HAL::micros64(); get_loop_period_s(); dispatches run-table tasks | AP_Vehicle::loop() via scheduler.loop() (AP_Vehicle.cpp:545) | Function call
6 | AP_Scheduler::tick() | increments _tick_counter / _tick_counter32 | AP_Scheduler::loop(); fast-loop | Function call
7 | AP_Scheduler::get_loop_period_us() | derives _loop_period_us from _loop_rate_hz | task budgeting; controller dt (G_Dt) | Data dependency
8 | AP_GPS::time_week_ms() / time_week() | returns state[instance].time_week_ms / time_week | NavEKF3 readGpsData (GPS time); time_epoch conversion; logging | Data dependency
# 1–8

## Slide 131
DEPENDENCY MAP · LAYER 1 · DIRECT EDGES
Table 3a — Layer 1 dependency map (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Component/Function | Directly Calls | Directly Called By | Dependency Type
9 | AP_HAL::Scheduler (abstract HAL timing / scheduling interface) | pure virtual — implemented by the board backend (ChibiOS / Linux / SITL HAL Scheduler) | AP_Scheduler via hal.scheduler->delay_microseconds (AP_Scheduler.cpp:373); register_io_process; AP_Vehicle init; all subsystems | Inheritance/Interface
# 9

## Slide 132
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 3a — Layer 1 Code Snippet
Every row’s Code Snippet, reproduced verbatim from the cited path:line range: one paragraph per source line, in the audit’s own order, with its indentation and its blank lines intact and nothing abbreviated.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
1 | AP_HAL::micros() / millis() · Function call uint16_t micros16(); uint32_t micros(); uint32_t millis(); uint16_t millis16(); uint64_t micros64(); uint64_t millis64();
2 | AP_RTC::get_utc_usec() — via AP::rtc() · Shared global/singleton void AP_Scheduler::Log_Write_Performance() { uint64_t rtc = 0; #if AP_RTC_ENABLED UNUSED_RESULT(AP::rtc().get_utc_usec(rtc)); #endif const AP_HAL::Util::PersistentData &pd = hal.util->persistent_data; struct log_Performance pkt = {
# 1–2

## Slide 133
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 3a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
3 | AP_RTC::set_utc_usec() (source arbitration) · Data dependency // only allow time to be moved forward from the same sourcetype // while the vehicle is disarmed: if (hal.util->get_soft_armed()) { if (type >= rtc_source_type) { // e.g. system-time message when we've been set by the GPS return; } } else { // vehicle is disarmed; accept (e.g.) GPS time source updates if (type > rtc_source_type) {
4 | JitterCorrection::correct_offboard_timestamp_usec() · Function call uint64_t JitterCorrection::correct_offboard_timestamp_usec(uint64_t offboard_usec, uint64_t local_usec) { int64_t diff_us = int64_t(local_usec) - int64_t(offboard_usec) ; if (!initialised ¦¦ diff_us < link_offset_usec) { // this message arrived from the remote system with a // timestamp that would imply the message was from the // future. We know that isn't possible, so we adjust down the
# 3–4

## Slide 134
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 3a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
5 | AP_Scheduler::loop() · Function call hal.util->persistent_data.scheduler_task = -1; _loop_sample_time_us = AP_HAL::micros64(); const uint32_t sample_time_us = uint32_t(_loop_sample_time_us) ; if (_loop_timer_start_us == 0) { _loop_timer_start_us = sample_time_us; _last_loop_time_s = get_loop_period_s(); } else { _last_loop_time_s = (sample_time_us - _loop_timer_start_us ) * 1.0e-6;
6 | AP_Scheduler::tick() · Function call void AP_Scheduler::tick(void) { _tick_counter++; _tick_counter32++; } #if CONFIG_HAL_BOARD == HAL_BOARD_SITL /* fill stack with NaN so we can catch use of uninitialised stack
# 5–6

## Slide 135
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 3a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
7 | AP_Scheduler::get_loop_period_us() · Data dependency // get the time-allowed-per-loop in microseconds uint32_t get_loop_period_us() { if (_loop_period_us == 0) { _loop_period_us = 1000000UL / _loop_rate_hz; } return _loop_period_us; }
8 | AP_GPS::time_week_ms() / time_week() · Data dependency // GPS time of week in milliseconds uint32_t time_week_ms(uint8_t instance) const { return state[instance].time_week_ms; } uint32_t time_week_ms() const { return time_week_ms(primary_instance); } // GPS week uint16_t time_week(uint8_t instance) const {
# 7–8

## Slide 136
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 3a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
9 | AP_HAL::Scheduler (abstract HAL timing / scheduling interface) · Inheritance/Interface // register a high priority timer task virtual void register_timer_process(AP_HAL::MemberProc) = 0; // register a low priority IO task virtual void register_io_process(AP_HAL::MemberProc) = 0;
# 9

## Slide 137
DEPENDENCY MAP · LAYER 2 · DEPTHS 3, 4
Table 3a — Layer 2 transitive chains
Table 3a: Layer 2 — full transitive chain, final consumer & hop depth
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
1 | RTOS/board hardware timer | board timer → AP_HAL::micros()/millis() → AP_Scheduler / EKF / AP_GPS timestamps → every periodic loop | all periodic PNT subsystems | 3 | Monotonic-time backbone.
2 | GPS/GCS UTC time source | time source → AP_RTC → AP::rtc().get_utc_usec() → AP_Logger / AP_Stats → log timestamps | dataflash log timestamps | 4 | Singleton consumption edge (AP::rtc()).
3 | AP_GPS time / GCS SYSTEM_TIME | time source → set_utc_usec source arbitration → rtc_source_type → system UTC clock | RTC system clock | 3 | Best-source selection.
4 | Offboard (remote) timestamp | MAVLink/DroneCAN timestamp → correct_offboard_timestamp_usec → corrected local time → EKF / sensor fusion | fused-sensor timing | 3 | Time-sync transform.
5 | AP_HAL::micros64() (loop clock) | AP_HAL::micros64() → AP_Scheduler::loop() → run-table tasks (EKF/AHRS/controllers) → AP_Motors | AP_Motors (all tasks) | 3 | Loop drives every PNT task.
6 | AP_Scheduler::loop() | loop() → tick() counters → task-table interval check → periodic task dispatch | periodic task dispatch | 3 | Cadence counter.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 1–6

## Slide 138
DEPENDENCY MAP · LAYER 2 · DEPTHS 3, 4
Table 3a — Layer 2 transitive chains (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
7 | SCHED_LOOP_RATE parameter | _loop_rate_hz → get_loop_period_us (1e6/rate) → task budget + G_Dt → AC_AttitudeControl / EKF dt | controller / EKF dt | 3 | Rate→period coupling.
8 | GPS receiver (time-of-week) | GPS receiver → GPS_State.time_week → AP_GPS::time_week() → NavEKF3 readGpsData / time_epoch_usec → UTC/log | EKF GPS-time / UTC conversion | 4 | [MULTI-CATEGORY] timing facet of GPS.
9 | board RTOS scheduler (HAL backend) | board HAL Scheduler backend → AP_HAL::Scheduler interface (delay / register_timer_process) → AP_Scheduler::loop → periodic PNT tasks (EKF / AHRS / control) | periodic PNT task execution | 3 | HAL timing interface beneath the AP_Scheduler library (#5-#7); the board backend implements the pure-virtual interface.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 7–9

## Slide 139
Table 4 — Indirect Positioning
Positioning read as a permission: health checks, fence evaluations and mode gates.

## Slide 140
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · INDIRECT POSITIONING
Table 4 — Indirect Positioning
All 10 catalogued rows, with every Notes annotation, flag token and cited path:line range exactly as printed.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# · File Path · Line(s) · Function/Class | Trigger Condition | PNT State Observed | Behavior Change Description | Notes
1 ArduCopter/system.cpp 226-234 Copter::position_ok() | Evaluated on position-mode entry and by position-dependent failsafes | failsafe.ekf flag; ekf_has_absolute_position() / ekf_has_relative_position() (EKF position validity) | Returns false when EKF failsafe is set or no EKF position estimate exists, causing callers to deny position-requiring behavior. | INDIRECT/RELATIONAL (positioning). Pure observer of EKF position health — reads no raw PNT, but gates downstream behavior.
2 ArduCopter/mode.cpp 303-310 Copter::set_mode() — requires_GPS gate | Pilot/GCS/auto requests a flight-mode change | new_flightmode->requires_GPS() && copter.position_ok() | Rejects the mode change with “requires position” when the target mode needs GPS and position_ok() is false. | INDIRECT/RELATIONAL (positioning). Central position-gate for ALL position-requiring Copter modes (per-mode requires_GPS() enumerated in the coverage register).
3 ArduCopter/fence.cpp 20-28 Copter::fence_checks_async() | 25 Hz fence rate-gate elapsed and no breach latched awaiting the main loop | fence.get_breaches() (current breach bitmask, L21); fence.check() (re-evaluates vehicle position vs fences, L25) | Latches new_breaches bitmask for the main loop and logs a breach-cleared event when the vehicle returns inside the fence. | [DUPLICATED] [FIX F1] Cited window centers on get_breaches() (L21) and check() (L25) — the actual geofence observation — not the L8-17 async/timing entry. mirrors Rover::fence_checks_async (#9). Timing rate-gate documented in Table 6.
# 1–3

## Slide 141
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · INDIRECT POSITIONING
Table 4 — Indirect Positioning (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# · File Path · Line(s) · Function/Class | Trigger Condition | PNT State Observed | Behavior Change Description | Notes
4 libraries/AC_Fence/AC_Fence.cpp 677-685 AC_Fence::check_fence_polygon() | Polygon (inclusion/exclusion) fence enabled | AP::ahrs().get_location(loc) — current vehicle Location tested against the polygon | record_breach(POLYGON) when _poly_loader.breached(loc) is true → sets the polygon breach bit. | [FIX F2] Real position-observing path (was mis-cited to L753-762 mask init). Snippet centers on the AP::ahrs().get_location() read (L680).
5 libraries/AC_Fence/AC_Fence.cpp 707-715 AC_Fence::check_fence_circle() | Circle fence enabled | AP::ahrs().get_relative_position_NE_home(home) — NE distance from home (L713) | Records a circle breach when the home distance exceeds the configured radius. | [FIX F2] Real position-observing path; snippet centers on the NE-home position read.
6 libraries/AC_Fence/AC_Fence.cpp 540-548 AC_Fence::check_fence_alt_max() | Maximum-altitude fence enabled | AP::ahrs().get_relative_position_D_home(alt) — altitude relative to home (L546) | Records an altitude breach when alt exceeds _alt_max. | [FIX F2] Real altitude-observing path; snippet centers on the D-home altitude read.
# 4–6

## Slide 142
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · INDIRECT POSITIONING
Table 4 — Indirect Positioning (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# · File Path · Line(s) · Function/Class | Trigger Condition | PNT State Observed | Behavior Change Description | Notes
7 libraries/AC_Fence/AC_Fence.cpp 837-845 AC_Fence::check() | Periodic fence check invoked from the vehicle fence_checks_async() | (aggregator) results of check_fence_alt_max() / check_fence_circle() / check_fence_polygon() position checks | Returns the bitmask of breached fence types that drives the vehicle fence failsafe action. | [FIX F2] Orchestrator dispatch (L837 circle, L842 polygon). The position reads themselves are in the dispatched checks (#4-#6).
8 ArduCopter/mode_guided_nogps.cpp 9-15 ModeGuidedNoGPS::init() | GUIDED_NOGPS entry (companion-computer angle control without GPS) | [ABSENT — by design] no position state observed; requires_GPS() returns false (ArduCopter/mode.h) | Starts angle control only and remains available when position_ok() is false — the GPS-denied fallback path. | INDIRECT/RELATIONAL (positioning). Contrast row: intentionally PNT-position-INDEPENDENT mode (documents an explicit absence of positioning dependency).
9 Rover/fence.cpp 17-25 Rover::fence_checks_async() | Rover fence rate-gate elapsed and no breach latched | fence.get_breaches() (L19); fence.check() (vehicle position vs fence, L21) | Latches new_breaches for the main loop; clears on return inside the fence. | [DUPLICATED] structurally identical to ArduCopter::fence_checks_async (#3) — copy-paste across vehicles (extraction risk).
# 7–9

## Slide 143
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · INDIRECT POSITIONING
Table 4 — Indirect Positioning (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# · File Path · Line(s) · Function/Class | Trigger Condition | PNT State Observed | Behavior Change Description | Notes
10 ArduPlane/takeoff.cpp 58-62 Plane::auto_takeoff_check() | Auto/TAKEOFF launch readiness re-evaluated each loop from Plane::set_servos() (Ardu Plane/servos.cpp:125) | gps.status() < AP_GPS:: GPS_OK_FIX_3D (GPS fix quality; gps.status() = AP_GPS::status()) | Returns false — auto-takeoff is blocked (throttle stays suppressed) until a 3D GPS fix is acquired. | [DUPLICATED] INDIRECT/RELATIONAL (positioning). User-example PNT-State-Observed accessor gps.status() (= AP_GPS::status(), libraries/AP_GPS/AP_GPS.h:293). the same gps.status() < GPS_OK_FIX_3D fix-gate recurs in ArduPlane/Plane.cpp (L420/485) and ArduPlane/is_flying.cpp (extraction risk).
# 10

## Slide 144
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · VERBATIM SOURCE LINES
Table 4 — Code Snippet (5-10 lines)
Every row’s Code Snippet (5-10 lines), reproduced verbatim from the cited path:line range: one paragraph per source line, in the audit’s own order, with its indentation and its blank lines intact and nothing abbreviated.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
1 | ArduCopter/system.cpp · 226-234 · Copter::position_ok() bool Copter::position_ok() const { // return false if ekf failsafe has triggered if (failsafe.ekf) { return false; } // check ekf position estimate return (ekf_has_absolute_position() ¦¦ ekf_has_relative_position());
# 1

## Slide 145
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · VERBATIM SOURCE LINES
Table 4 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
2 | ArduCopter/mode.cpp · 303-310 · Copter::set_mode() — requires_GPS gate if (!ignore_checks && new_flightmode->requires_GPS() && !copter.position_ok()) { mode_change_failed(new_flightmode, "requires position"); return false; }
3 | ArduCopter/fence.cpp · 20-28 · Copter::fence_checks_async() fence_breaches.last_check_ms = now; const uint8_t orig_breaches = fence.get_breaches(); bool is_landing_or_landed = flightmode->is_landing() ¦¦ ap.land_complete ¦¦ !motors->armed(); // check for new breaches; new_breaches is bitmask of fence types breached fence_breaches.new_breaches = fence.check(is_landing_or_landed); if (!fence_breaches.new_breaches && orig_breaches && fence.get_breaches() == 0) { if (!copter.ap.land_complete) {
# 2–3

## Slide 146
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · VERBATIM SOURCE LINES
Table 4 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
4 | libraries/AC_Fence/AC_Fence.cpp · 677-685 · AC_Fence::check_fence_polygon() const bool was_breached = _breached_fences & AC_FENCE_TYPE_POLYGON; Location loc; const bool have_location = AP::ahrs().get_location(loc); if (have_location && _poly_loader.breached(loc, _polygon_breach_distance)) { if (!was_breached) { record_breach(AC_FENCE_TYPE_POLYGON); return true;
5 | libraries/AC_Fence/AC_Fence.cpp · 707-715 · AC_Fence::check_fence_circle() if (!(get_enabled_fences() & AC_FENCE_TYPE_CIRCLE)) { // not enabled; no breach return false; } Vector2f home; if (AP::ahrs().get_relative_position_NE_home(home)) { // we (may) remain breached if we can't update home _home_distance = home.length();
# 4–5

## Slide 147
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · VERBATIM SOURCE LINES
Table 4 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
6 | libraries/AC_Fence/AC_Fence.cpp · 540-548 · AC_Fence::check_fence_alt_max() if (!(get_enabled_fences() & AC_FENCE_TYPE_ALT_MAX)) { // not enabled; no breach return false; } float alt; AP::ahrs().get_relative_position_D_home(alt); const float _curr_alt = -alt; // translate Down to Up
7 | libraries/AC_Fence/AC_Fence.cpp · 837-845 · AC_Fence::check() if (!(disabled_fences & AC_FENCE_TYPE_CIRCLE) && check_fence_circle()) { ret ¦= AC_FENCE_TYPE_CIRCLE; } // polygon fence check if (!(disabled_fences & AC_FENCE_TYPE_POLYGON) && check_fence_polygon()) { ret ¦= AC_FENCE_TYPE_POLYGON; }
# 6–7

## Slide 148
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · VERBATIM SOURCE LINES
Table 4 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
8 | ArduCopter/mode_guided_nogps.cpp · 9-15 · ModeGuidedNoGPS::init() // initialise guided_nogps controller bool ModeGuidedNoGPS::init(bool ignore_checks) { // start in angle control mode ModeGuided::angle_control_start(); return true; }
9 | Rover/fence.cpp · 17-25 · Rover::fence_checks_async() fence_breaches.last_check_ms = now; const uint8_t orig_breaches = fence.get_breaches(); // check for new breaches; new_breaches is bitmask of fence types breached fence_breaches.new_breaches = fence.check(); if (!fence_breaches.new_breaches && orig_breaches && fence.get_breaches() == 0) { // record clearing of breach LOGGER_WRITE_ERROR(LogErrorSubsystem::FAILSAFE_FENCE, LogErrorCode::ERROR_RESOLVED);
# 8–9

## Slide 149
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · VERBATIM SOURCE LINES
Table 4 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
10 | ArduPlane/takeoff.cpp · 58-62 · Plane::auto_takeoff_check() // Check for bad GPS if (gps.status() < AP_GPS::GPS_OK_FIX_3D) { // no auto takeoff without GPS lock return false; }
# 10

## Slide 150
DEPENDENCY MAP · LAYER 1 · DIRECT EDGES
Table 4a — Layer 1 dependency map
Table 4a: Layer 1 — direct callers / callees with typed dependency
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Component/Function | Directly Calls | Directly Called By | Dependency Type
1 | Copter::position_ok() | ekf_has_absolute_position(); ekf_has_relative_position(); reads failsafe.ekf | Copter::set_mode (mode.cpp:306); position-dependent failsafes | Function call
2 | Copter::set_mode() requires_GPS gate | new_flightmode->requires_GPS(); copter.position_ok() | GCS/RC/auto mode-change entry points | Function call
3 | Copter::fence_checks_async() | fence.get_breaches(); fence.check() | Copter IO thread (1 kHz async, 25 Hz gated) | Function call
4 | AC_Fence::check_fence_polygon() | AP::ahrs().get_location(); _poly_loader.breached() | AC_Fence::check() (L842) | Shared global/singleton
5 | AC_Fence::check_fence_circle() | AP::ahrs().get_relative_position_NE_home() | AC_Fence::check() (L837) | Shared global/singleton
6 | AC_Fence::check_fence_alt_max() | AP::ahrs().get_relative_position_D_home() | AC_Fence::check() (L821) | Shared global/singleton
7 | AC_Fence::check() | check_fence_alt_max(); check_fence_circle(); check_fence_polygon() | Copter::fence_checks_async(); Rover::fence_checks_async() | Function call
8 | ModeGuidedNoGPS::init() | ModeGuided::angle_control_start() | Copter::set_mode() | Inheritance/Interface
9 | Rover::fence_checks_async() | fence.get_breaches(); fence.check() | Rover IO thread | Function call
# 1–9

## Slide 151
DEPENDENCY MAP · LAYER 1 · DIRECT EDGES
Table 4a — Layer 1 dependency map (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Component/Function | Directly Calls | Directly Called By | Dependency Type
10 | Plane::auto_takeoff_check() | AP_GPS::status() (gps.status()); compares vs AP_GPS::GPS_OK_FIX_3D | Plane::set_servos() (ArduPlane/servos.cpp:125) | Function call
# 10

## Slide 152
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 4a — Layer 1 Code Snippet
Every row’s Code Snippet, reproduced verbatim from the cited path:line range: one paragraph per source line, in the audit’s own order, with its indentation and its blank lines intact and nothing abbreviated.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
1 | Copter::position_ok() · Function call bool Copter::position_ok() const { // return false if ekf failsafe has triggered if (failsafe.ekf) { return false; } // check ekf position estimate return (ekf_has_absolute_position() ¦¦ ekf_has_relative_position());
2 | Copter::set_mode() requires_GPS gate · Function call if (!ignore_checks && new_flightmode->requires_GPS() && !copter.position_ok()) { mode_change_failed(new_flightmode, "requires position"); return false; }
# 1–2

## Slide 153
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 4a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
3 | Copter::fence_checks_async() · Function call fence_breaches.last_check_ms = now; const uint8_t orig_breaches = fence.get_breaches(); bool is_landing_or_landed = flightmode->is_landing() ¦¦ ap.land_complete ¦¦ !motors->armed(); // check for new breaches; new_breaches is bitmask of fence types breached fence_breaches.new_breaches = fence.check(is_landing_or_landed ); if (!fence_breaches.new_breaches && orig_breaches && fence.get_breaches() == 0) { if (!copter.ap.land_complete) {
4 | AC_Fence::check_fence_polygon() · Shared global/singleton const bool was_breached = _breached_fences & AC_FENCE_TYPE_POLYGON; Location loc; const bool have_location = AP::ahrs().get_location(loc); if (have_location && _poly_loader.breached(loc, _polygon_breach_distance)) { if (!was_breached) { record_breach(AC_FENCE_TYPE_POLYGON); return true;
# 3–4

## Slide 154
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 4a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
5 | AC_Fence::check_fence_circle() · Shared global/singleton if (!(get_enabled_fences() & AC_FENCE_TYPE_CIRCLE)) { // not enabled; no breach return false; } Vector2f home; if (AP::ahrs().get_relative_position_NE_home(home)) { // we (may) remain breached if we can't update home _home_distance = home.length();
6 | AC_Fence::check_fence_alt_max() · Shared global/singleton if (!(get_enabled_fences() & AC_FENCE_TYPE_ALT_MAX)) { // not enabled; no breach return false; } float alt; AP::ahrs().get_relative_position_D_home(alt); const float _curr_alt = -alt; // translate Down to Up
# 5–6

## Slide 155
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 4a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
7 | AC_Fence::check() · Function call if (!(disabled_fences & AC_FENCE_TYPE_CIRCLE) && check_fence_circle()) { ret ¦= AC_FENCE_TYPE_CIRCLE; } // polygon fence check if (!(disabled_fences & AC_FENCE_TYPE_POLYGON) && check_fence_polygon()) { ret ¦= AC_FENCE_TYPE_POLYGON; }
8 | ModeGuidedNoGPS::init() · Inheritance/Interface // initialise guided_nogps controller bool ModeGuidedNoGPS::init(bool ignore_checks) { // start in angle control mode ModeGuided::angle_control_start(); return true; }
# 7–8

## Slide 156
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 4a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
9 | Rover::fence_checks_async() · Function call fence_breaches.last_check_ms = now; const uint8_t orig_breaches = fence.get_breaches(); // check for new breaches; new_breaches is bitmask of fence types breached fence_breaches.new_breaches = fence.check(); if (!fence_breaches.new_breaches && orig_breaches && fence.get_breaches() == 0) { // record clearing of breach LOGGER_WRITE_ERROR(LogErrorSubsystem::FAILSAFE_FENCE, LogErrorCode::ERROR_RESOLVED);
10 | Plane::auto_takeoff_check() · Function call // Check for bad GPS if (gps.status() < AP_GPS::GPS_OK_FIX_3D) { // no auto takeoff without GPS lock return false; }
# 9–10

## Slide 157
DEPENDENCY MAP · LAYER 2 · DEPTHS 2, 3, 4, 5
Table 4a — Layer 2 transitive chains
Table 4a: Layer 2 — full transitive chain, final consumer & hop depth
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
1 | EKF position health (via AP_AHRS) | AP_GPS → NavEKF3 → AP_AHRS::have_inertial_nav() → Copter::ekf_has_absolute_position() → Copter::position_ok() → set_mode gate | flight-mode entry allow/deny | 5 | Core positioning-health gate.
2 | Copter::position_ok() | position_ok() → set_mode requires_GPS gate → mode_change_failed() → mode unchanged | rejected mode change | 3 | Gate decision path.
3 | AP_AHRS vehicle position (via AC_Fence) | AP::ahrs() position → AC_Fence::check (polygon/circle/alt) → get_breaches bitmask → fence_checks_async latch → Copter::fence_check() action | Copter fence failsafe (RTL/LAND) | 4 | [DUPLICATED] mirrors Rover chain #9.
4 | AP_AHRS::get_location() | AP_AHRS::get_location() → check_fence_polygon → _poly_loader.breached() → record_breach() → _breached_fences | polygon breach bit | 4 | Polygon position test.
5 | AP_AHRS NE-home position | AP::ahrs().get_relative_position_NE_home() → check_fence_circle → distance>radius → record_breach() | circle breach bit | 3 | Circle position test.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 1–5

## Slide 158
DEPENDENCY MAP · LAYER 2 · DEPTHS 2, 3, 4, 5
Table 4a — Layer 2 transitive chains (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
6 | AP_AHRS D-home altitude | AP::ahrs().get_relative_position_D_home() → check_fence_alt_max → alt>_alt_max → record_breach() | altitude breach bit | 3 | Altitude position test.
7 | AC_Fence position checks | position checks → AC_Fence::check() aggregate → breach bitmask → vehicle fence_check() → failsafe action | vehicle fence failsafe | 4 | Aggregator path.
8 | (no PNT — GPS-independent) | ModeGuidedNoGPS::init() → angle_control_start() → AC_AttitudeControl → AP_Motors | AP_Motors | 3 | [ABSENT] no positioning hop — fallback by design.
9 | AP_AHRS vehicle position (via AC_Fence) | AP::ahrs() position → AC_Fence::check → get_breaches → Rover::fence_checks_async latch → Rover::fence_check() action | Rover fence failsafe | 4 | [DUPLICATED] structurally identical to Copter chain #3.
10 | AP_GPS::status() (GPS fix-status accessor) | AP_GPS::status() → Plane::auto_takeoff_check() [ArduPlane/takeoff.cpp:59] → Plane::set_servos() [ArduPlane/servos.cpp:125] | Plane::set_servos() (throttle suppression / launch gate) | 2 | User-example gps.status() observation gating auto-takeoff.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 6–10

## Slide 159
Table 5 — Indirect Navigation
Navigation read as a permission: estimator-variance watchdogs across the vehicle firmwares.

## Slide 160
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · INDIRECT NAVIGATION
Table 5 — Indirect Navigation
All 10 catalogued rows, with every Notes annotation, flag token and cited path:line range exactly as printed.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# · File Path · Line(s) · Function/Class | Trigger Condition | PNT State Observed | Behavior Change Description | Notes
1 ArduCopter/ekf_check.cpp 117-125 Copter::ekf_over_threshold() | 10 Hz EKF health check while the EKF has an origin | ahrs.get_variances() → velocity / position / height / magnetometer variances vs g.fs_ekf_thresh | Counts bad iterations; after EKF_CHECK_ITERATIONS_MAX (≈10) trips the EKF failsafe (LAND / AltHold). | [DUPLICATED] INDIRECT/RELATIONAL (navigation). EKF-variance watchdog replicated across ArduCopter/ekf_check.cpp, ArduPlane/ekf_check.cpp, Rover/ekf_check.cpp and ArduSub/failsafe.cpp — a 4-way copy-paste (extraction risk).
2 ArduPlane/ekf_check.cpp 56-65 Plane::ekf_check() | 10 Hz EKF health check (fixed-wing) | ekf_over_threshold() (compass & velocity variance vs fs_ekf_thresh) | Increments fail_count; two iterations before failsafe asks the EKF to reset yaw (ahrs.request_yaw_reset()); trips EKF failsafe at MAX. | [DUPLICATED] INDIRECT/RELATIONAL (navigation). EKF-variance watchdog replicated across ArduCopter/ekf_check.cpp, ArduPlane/ekf_check.cpp, Rover/ekf_check.cpp and ArduSub/failsafe.cpp — a 4-way copy-paste (extraction risk).
# 1–2

## Slide 161
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · INDIRECT NAVIGATION
Table 5 — Indirect Navigation (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# · File Path · Line(s) · Function/Class | Trigger Condition | PNT State Observed | Behavior Change Description | Notes
3 Rover/ekf_check.cpp 93-102 Rover::ekf_over_threshold() | 10 Hz EKF health check (ground vehicle) | ahrs.get_variances() → compass / velocity / position variance; ≥2 over threshold | Sets bad_variance → Rover EKF failsafe action. | [DUPLICATED] INDIRECT/RELATIONAL (navigation). EKF-variance watchdog replicated across ArduCopter/ekf_check.cpp, ArduPlane/ekf_check.cpp, Rover/ekf_check.cpp and ArduSub/failsafe.cpp — a 4-way copy-paste (extraction risk).
4 ArduSub/failsafe.cpp 112-121 Sub::failsafe_ekf_check() | Periodic EKF health check (submarine) | ahrs.get_variances() → compass_variance & vel_variance vs g.fs_ekf_thresh | Clears/sets failsafe.ekf and AP_Notify ekf_bad based on variance vs threshold; GCS warns “EKF bad”. | [DUPLICATED] INDIRECT/RELATIONAL (navigation). [FIX F13 dep-type] EKF-variance watchdog replicated across ArduCopter/ekf_check.cpp, ArduPlane/ekf_check.cpp, Rover/ekf_check.cpp and ArduSub/failsafe.cpp — a 4-way copy-paste (extraction risk).
# 3–4

## Slide 162
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · INDIRECT NAVIGATION
Table 5 — Indirect Navigation (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# · File Path · Line(s) · Function/Class | Trigger Condition | PNT State Observed | Behavior Change Description | Notes
5 ArduCopter/crash_check.cpp 65-74 Copter::crash_check() — attitude test | Disarm/crash monitor running while armed and not landed | ahrs.cos_roll() / ahrs.cos_pitch() (lean angle); attitude_control-> get_att_error_angle_deg() | Resets crash_counter (declares not-crashing) when lean angle ≤ 15° or attitude error ≤ 30°. | [FIX F3] Split row: attitude-only observation (lean L66, angle-error L73). Velocity observation is the separate row #6 (was wrongly bundled into the L64-73 citation).
6 ArduCopter/crash_check.cpp 78-84 Copter::crash_check() — velocity test | Continues after the attitude test indicates a possible crash | ahrs.get_velocity_NED(vel_ned) → NED speed magnitude (L80-81) | Resets crash_counter when speed ≥ CRASH_CHECK_SPEED_MAX (10 m/s); otherwise increments toward the 2-second crash trigger → disarm. | [FIX F3] Split row: the velocity observation cited at L78-84 (ahrs.get_velocity_NED L80-81), now accurately centered — not the L64-73 attitude range.
7 ArduPlane/GCS_MAVLink_Plane.cpp 204-212 GCS_MAVLINK_Plane::send_nav_controller_output() | GCS telemetry stream requests NAV_CONTROLLER_OUTPUT | nav_controller navigation state (target bearing, xtrack error, wp distance) — unless in MANUAL | Emits the NAV_CONTROLLER_OUTPUT MAVLink message (navigation-health reporting to the GCS). | INDIRECT/RELATIONAL (navigation). Reporting Sink for navigation state.
# 5–7

## Slide 163
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · INDIRECT NAVIGATION
Table 5 — Indirect Navigation (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# · File Path · Line(s) · Function/Class | Trigger Condition | PNT State Observed | Behavior Change Description | Notes
8 ArduPlane/Attitude.cpp 604-611 Plane::calc_nav_roll() | Fixed-wing attitude loop computing the roll demand | nav_controller->nav_roll_cd() (L1/navigation lateral roll demand) | Sets nav_roll_cd from the navigation controller, constrained to ±roll_limit_cd. | INDIRECT/RELATIONAL (navigation). Consumes navigation-controller output (user-cited calc_nav_roll).
9 ArduPlane/navigation.cpp 86-94 Plane::navigate() | 10 Hz fixed-wing navigation update | have_position flag (EKF/GPS position validity); next_WP_loc | Returns early (skips navigation) when have_position is false; otherwise computes the desired direction and distance to the next waypoint. | INDIRECT/RELATIONAL (navigation). This is the real symbol behind the user-example 'flight_mode_auto' chain (Table 2a L2 #1); gated on PNT position validity.
10 ArduPlane/navigation.cpp 304-311 Plane::calc_gndspeed_undershoot() | 10 Hz GPS/navigation update (Plane::update_GPS_10Hz, ArduPlane/Plane.cpp:490) | ahrs.have_inertial_nav() (inertial-navigation solution availability) | Ground-speed-undershoot (min-groundspeed wind/flyaway compensation) is computed only when inertial nav is available; otherwise it is skipped and left stale/zero. | INDIRECT/RELATIONAL (navigation). User-example PNT-State-Observed accessor ahrs.have_inertial_nav() (libraries/AP_AHRS/AP_AHRS.h:273); the accessor itself is catalogued in Table 2 #3.
# 8–10

## Slide 164
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · VERBATIM SOURCE LINES
Table 5 — Code Snippet (5-10 lines)
Every row’s Code Snippet (5-10 lines), reproduced verbatim from the cited path:line range: one paragraph per source line, in the audit’s own order, with its indentation and its blank lines intact and nothing abbreviated.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
1 | ArduCopter/ekf_check.cpp · 117-125 · Copter::ekf_over_threshold() float position_var, vel_var, height_var, tas_variance; Vector3f mag_variance; variances_valid = ahrs.get_variances(vel_var, position_var, height_var, mag_variance, tas_variance); if (!variances_valid) { return false; } uint32_t now_us = AP_HAL::micros();
# 1

## Slide 165
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · VERBATIM SOURCE LINES
Table 5 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
2 | ArduPlane/ekf_check.cpp · 56-65 · Plane::ekf_check() // compare compass and velocity variance vs threshold if (ekf_over_threshold()) { // if compass is not yet flagged as bad if (!ekf_check_state.bad_variance) { // increase counter ekf_check_state.fail_count++; if (ekf_check_state.fail_count == (EKF_CHECK_ITERATIONS_MAX-2)) { // we are two iterations away from declaring an EKF failsafe, ask the EKF if we can reset // yaw to resolve the issue ahrs.request_yaw_reset();
3 | Rover/ekf_check.cpp · 93-102 · Rover::ekf_over_threshold() // use EKF to get variance float position_variance, vel_variance, height_variance, tas_variance; Vector3f mag_variance; ahrs.get_variances(vel_variance, position_variance, height_variance, mag_variance, tas_variance); // return true if two of compass, velocity and position variances are over the threshold uint8_t over_thresh_count = 0; if (mag_variance.length() >= g.fs_ekf_thresh) { over_thresh_count++;
# 2–3

## Slide 166
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · VERBATIM SOURCE LINES
Table 5 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
4 | ArduSub/failsafe.cpp · 112-121 · Sub::failsafe_ekf_check() Vector3f magVar; float compass_variance; float vel_variance; ahrs.get_variances(vel_variance, posVar, hgtVar, magVar, tasVar); compass_variance = magVar.length(); if (compass_variance < g.fs_ekf_thresh && vel_variance < g.fs_ekf_thresh) { last_ekf_good_ms = AP_HAL::millis(); failsafe.ekf = false; AP_Notify::flags.ekf_bad = false;
5 | ArduCopter/crash_check.cpp · 65-74 · Copter::crash_check() — attitude test // check for lean angle over 15 degrees const float lean_angle_deg = degrees(acosf(ahrs.cos_roll()*ahrs.cos_pitch())); if (lean_angle_deg <= CRASH_CHECK_ANGLE_MIN_DEG) { crash_counter = 0; return; } // check for angle error over 30 degrees const float angle_error = attitude_control->get_att_error_angle_deg(); if (angle_error <= CRASH_CHECK_ANGLE_DEVIATION_DEG) {
# 4–5

## Slide 167
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · VERBATIM SOURCE LINES
Table 5 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
6 | ArduCopter/crash_check.cpp · 78-84 · Copter::crash_check() — velocity test // check for speed under 10m/s (if available) Vector3f vel_ned; if (ahrs.get_velocity_NED(vel_ned) && (vel_ned.length() >= CRASH_CHECK_SPEED_MAX)) { crash_counter = 0; return; }
7 | ArduPlane/GCS_MAVLink_Plane.cpp · 204-212 · GCS_MAVLINK_Plane::send_nav_controller_output() void GCS_MAVLINK_Plane::send_nav_controller_output() const { if (plane.control_mode == &plane.mode_manual) { return; } #if HAL_QUADPLANE_ENABLED const QuadPlane &quadplane = plane.quadplane; if (quadplane.show_vtol_view() && quadplane.using_wp_nav()) { const Vector3f &targets = quadplane.attitude_control->get_att_target_euler_cd();
# 6–7

## Slide 168
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · VERBATIM SOURCE LINES
Table 5 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
8 | ArduPlane/Attitude.cpp · 604-611 · Plane::calc_nav_roll() calculate a new nav_roll_cd from the navigation controller */ void Plane::calc_nav_roll() { int32_t commanded_roll = nav_controller->nav_roll_cd(); nav_roll_cd = constrain_int32(commanded_roll, -roll_limit_cd, roll_limit_cd); update_load_factor(); }
9 | ArduPlane/navigation.cpp · 86-94 · Plane::navigate() void Plane::navigate() { // do not navigate with corrupt data // --------------------------------- if (!have_position) { return; } if (next_WP_loc.lat == 0 && next_WP_loc.lng == 0) {
# 8–9

## Slide 169
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · VERBATIM SOURCE LINES
Table 5 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
10 | ArduPlane/navigation.cpp · 304-311 · Plane::calc_gndspeed_undershoot() Vector3f velNED; if (ahrs.have_inertial_nav() && ahrs.get_velocity_NED(velNED)) { const Matrix3f &rotMat = ahrs.get_rotation_body_to_ned(); Vector2f yawVect = Vector2f(rotMat.a.x,rotMat.b.x); if (!yawVect.is_zero()) { yawVect.normalize(); float gndSpdFwd = yawVect * velNED.xy(); groundspeed_undershoot_is_valid = aparm.min_groundspeed > 0;
# 10

## Slide 170
DEPENDENCY MAP · LAYER 1 · DIRECT EDGES
Table 5a — Layer 1 dependency map
Table 5a: Layer 1 — direct callers / callees with typed dependency
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Component/Function | Directly Calls | Directly Called By | Dependency Type
1 | Copter::ekf_over_threshold() | ahrs.get_variances(); variance filters; compare g.fs_ekf_thresh | Copter::ekf_check() | Function call
2 | Plane::ekf_check() | ekf_over_threshold(); ahrs.request_yaw_reset() | Plane 10 Hz scheduler | Function call
3 | Rover::ekf_over_threshold() | ahrs.get_variances(); compare g.fs_ekf_thresh | Rover::ekf_check() | Function call
4 | Sub::failsafe_ekf_check() | ahrs.get_variances(); AP_HAL::millis(); gcs().send_text() | Sub periodic scheduler | Function call
5 | Copter::crash_check() (attitude) | ahrs.cos_roll(); ahrs.cos_pitch(); attitude_control->get_att_error_angle_deg() | Copter::crash_check() | Function call
6 | Copter::crash_check() (velocity) | ahrs.get_velocity_NED(vel_ned) | Copter::crash_check() | Function call
7 | GCS_MAVLINK_Plane::send_nav_controller_output() | reads plane.control_mode; nav_controller state | GCS telemetry scheduler | Function call
8 | Plane::calc_nav_roll() | nav_controller->nav_roll_cd(); update_load_factor() | Plane fast attitude loop | Function call
# 1–8

## Slide 171
DEPENDENCY MAP · LAYER 1 · DIRECT EDGES
Table 5a — Layer 1 dependency map (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Component/Function | Directly Calls | Directly Called By | Dependency Type
9 | Plane::navigate() | reads have_position; next_WP_loc; nav_controller update | Plane 10 Hz nav loop | Data dependency
10 | Plane::calc_gndspeed_undershoot() | ahrs.have_inertial_nav(); ahrs.get_velocity_NED() | Plane::update_GPS_10Hz() (ArduPlane/Plane.cpp:490) | Function call
# 9–10

## Slide 172
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 5a — Layer 1 Code Snippet
Every row’s Code Snippet, reproduced verbatim from the cited path:line range: one paragraph per source line, in the audit’s own order, with its indentation and its blank lines intact and nothing abbreviated.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
1 | Copter::ekf_over_threshold() · Function call float position_var, vel_var, height_var, tas_variance; Vector3f mag_variance; variances_valid = ahrs.get_variances(vel_var, position_var, height_var, mag_variance, tas_variance); if (!variances_valid) { return false; } uint32_t now_us = AP_HAL::micros();
2 | Plane::ekf_check() · Function call // compare compass and velocity variance vs threshold if (ekf_over_threshold()) { // if compass is not yet flagged as bad if (!ekf_check_state.bad_variance) { // increase counter ekf_check_state.fail_count++; if (ekf_check_state.fail_count == (EKF_CHECK_ITERATIONS_MAX-2)) { // we are two iterations away from declaring an EKF failsafe, ask the EKF if we can reset // yaw to resolve the issue ahrs.request_yaw_reset();
# 1–2

## Slide 173
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 5a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
3 | Rover::ekf_over_threshold() · Function call // use EKF to get variance float position_variance, vel_variance, height_variance, tas_variance; Vector3f mag_variance; ahrs.get_variances(vel_variance, position_variance, height_variance, mag_variance, tas_variance); // return true if two of compass, velocity and position variances are over the threshold uint8_t over_thresh_count = 0; if (mag_variance.length() >= g.fs_ekf_thresh) { over_thresh_count++;
4 | Sub::failsafe_ekf_check() · Function call Vector3f magVar; float compass_variance; float vel_variance; ahrs.get_variances(vel_variance, posVar, hgtVar, magVar, tasVar); compass_variance = magVar.length(); if (compass_variance < g.fs_ekf_thresh && vel_variance < g.fs_ekf_thresh) { last_ekf_good_ms = AP_HAL::millis(); failsafe.ekf = false; AP_Notify::flags.ekf_bad = false;
# 3–4

## Slide 174
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 5a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
5 | Copter::crash_check() (attitude) · Function call // check for lean angle over 15 degrees const float lean_angle_deg = degrees(acosf(ahrs.cos_roll()*ahrs.cos_pitch())); if (lean_angle_deg <= CRASH_CHECK_ANGLE_MIN_DEG) { crash_counter = 0; return; } // check for angle error over 30 degrees const float angle_error = attitude_control->get_att_error_angle_deg(); if (angle_error <= CRASH_CHECK_ANGLE_DEVIATION_DEG) {
6 | Copter::crash_check() (velocity) · Function call // check for speed under 10m/s (if available) Vector3f vel_ned; if (ahrs.get_velocity_NED(vel_ned) && (vel_ned.length() >= CRASH_CHECK_SPEED_MAX)) { crash_counter = 0; return; }
# 5–6

## Slide 175
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 5a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
7 | GCS_MAVLINK_Plane::send_nav_controller_output() · Function call void GCS_MAVLINK_Plane::send_nav_controller_output() const { if (plane.control_mode == &plane.mode_manual) { return; } #if HAL_QUADPLANE_ENABLED const QuadPlane &quadplane = plane.quadplane; if (quadplane.show_vtol_view() && quadplane.using_wp_nav()) { const Vector3f &targets = quadplane.attitude_control->get_att_target_euler_cd();
8 | Plane::calc_nav_roll() · Function call calculate a new nav_roll_cd from the navigation controller */ void Plane::calc_nav_roll() { int32_t commanded_roll = nav_controller->nav_roll_cd(); nav_roll_cd = constrain_int32(commanded_roll, -roll_limit_cd, roll_limit_cd); update_load_factor(); }
# 7–8

## Slide 176
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 5a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
9 | Plane::navigate() · Data dependency void Plane::navigate() { // do not navigate with corrupt data // --------------------------------- if (!have_position) { return; } if (next_WP_loc.lat == 0 && next_WP_loc.lng == 0) {
10 | Plane::calc_gndspeed_undershoot() · Function call Vector3f velNED; if (ahrs.have_inertial_nav() && ahrs.get_velocity_NED(velNED)) { const Matrix3f &rotMat = ahrs.get_rotation_body_to_ned(); Vector2f yawVect = Vector2f(rotMat.a.x,rotMat.b.x); if (!yawVect.is_zero()) { yawVect.normalize(); float gndSpdFwd = yawVect * velNED.xy(); groundspeed_undershoot_is_valid = aparm.min_groundspeed > 0;
# 9–10

## Slide 177
DEPENDENCY MAP · LAYER 2 · DEPTHS 2, 3, 4, 5
Table 5a — Layer 2 transitive chains
Table 5a: Layer 2 — full transitive chain, final consumer & hop depth
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
1 | EKF variances (via AP_AHRS) | AP_GPS/EKF → ahrs.get_variances() → ekf_over_threshold() → Copter::ekf_check fail_count → failsafe_ekf_event() → LAND/AltHold | EKF failsafe action (LAND) | 5 | [DUPLICATED] EKF-variance watchdog replicated across ArduCopter/ekf_check.cpp, ArduPlane/ekf_check.cpp, Rover/ekf_check.cpp and ArduSub/failsafe.cpp — a 4-way copy-paste (extraction risk).
2 | EKF variances (Plane) | EKF variances → Plane::ekf_check → bad_variance → EKF failsafe → mode change (RTL/FBWA) | Plane EKF failsafe | 4 | [DUPLICATED] mirrors #1.
3 | EKF variances (Rover) | EKF variances → Rover::ekf_over_threshold → Rover::ekf_check → EKF failsafe action | Rover EKF failsafe | 3 | [DUPLICATED] mirrors #1.
4 | EKF variances (Sub) | EKF variances → Sub::failsafe_ekf_check → failsafe.ekf flag → GCS warn | Sub EKF failsafe flag | 3 | [DUPLICATED] mirrors #1.
5 | AP_AHRS attitude | AHRS attitude → crash_check attitude test → crash_counter → arming.disarm() | motor disarm | 3 | Attitude branch.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 1–5

## Slide 178
DEPENDENCY MAP · LAYER 2 · DEPTHS 2, 3, 4, 5
Table 5a — Layer 2 transitive chains (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
6 | AP_AHRS NED velocity | EKF velocity → ahrs.get_velocity_NED() → crash_check speed test → crash_counter → arming.disarm() | motor disarm | 4 | Velocity branch (F3 split).
7 | Navigation controller state | EKF/nav state → nav_controller → send_nav_controller_output → MAVLink → GCS | GCS NAV_CONTROLLER_OUTPUT | 4 | Reporting branch.
8 | Navigation controller roll demand | nav_controller (L1/EKF) → nav_roll_cd() → calc_nav_roll → nav_roll_cd → attitude controller → SRV_Channels | SRV_Channels | 5 | Roll-demand consumption.
9 | EKF position validity | EKF position → have_position → Plane::navigate → nav_controller->update_waypoint → calc_nav_roll → SRV_Channels | SRV_Channels | 5 | Real symbol behind user-example chain (Table 2a L2 #1).
10 | AP_AHRS::have_inertial_nav() (inertial-nav availability) | AP_AHRS::have_inertial_nav() → Plane::calc_gndspeed_undershoot() [ArduPlane/navigation.cpp:305] → Plane::update_GPS_10Hz() [ArduPlane/Plane.cpp:490] | Plane::update_GPS_10Hz() (groundspeed-undershoot nav compensation) | 2 | User-example ahrs.have_inertial_nav() observation gating nav groundspeed compensation.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 6–10

## Slide 179
Table 6 — Indirect Timing
Timing read as a permission: main-loop lockup watchdogs and the rate gates around them.

## Slide 180
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · INDIRECT TIMING
Table 6 — Indirect Timing
All 11 catalogued rows, with every Notes annotation, flag token and cited path:line range exactly as printed.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# · File Path · Line(s) · Function/Class | Trigger Condition | PNT State Observed | Behavior Change Description | Notes
1 ArduCopter/failsafe.cpp 37-45 Copter::failsafe_check() | 1 kHz timer-failsafe ISR; scheduler tick counter has not advanced since the last call | AP_HAL::micros() (tnow) and AP_Scheduler::ticks() loop counter (timing / loop-cadence state) | When ticks stall and tnow-failsafe_last_timestamp > 2,000,000 us (2 s) sets in_failsafe, drives motors->output_min(), then disarms every 1 s (CPU failsafe). | [DUPLICATED] INDIRECT/RELATIONAL (timing). Main-loop-lockup watchdog replicated 5 ways — ArduCopter/failsafe.cpp, ArduPlane/failsafe.cpp, Rover/failsafe.cpp, ArduSub/failsafe.cpp (mainloop_failsafe_check) and Blimp/failsafe.cpp — each reads AP_Scheduler::ticks() + AP_HAL::micros(); divergent thresholds/actions (extraction risk).
# 1

## Slide 181
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · INDIRECT TIMING
Table 6 — Indirect Timing (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# · File Path · Line(s) · Function/Class | Trigger Condition | PNT State Observed | Behavior Change Description | Notes
2 ArduPlane/failsafe.cpp 22-30 Plane::failsafe_check() | 1 kHz timer-failsafe ISR; scheduler tick counter unchanged (main loop stalled) | micros() (tnow) and AP_Scheduler::ticks() (ticks vs last_ticks) | After > 200,000 us (0.2 s) stall sets in_failsafe and passes RC inputs straight to servo outputs (SRV_Channels) every 20 ms instead of disarming. | [DUPLICATED] INDIRECT/RELATIONAL (timing). Main-loop-lockup watchdog replicated 5 ways — ArduCopter/failsafe.cpp, ArduPlane/failsafe.cpp, Rover/failsafe.cpp, ArduSub/failsafe.cpp (mainloop_failsafe_check) and Blimp/failsafe.cpp — each reads AP_Scheduler::ticks() + AP_HAL::micros(); divergent thresholds/actions (extraction risk). Divergent: 0.2 s trip + RC-passthrough (vs Copter 2 s + disarm).
# 2

## Slide 182
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · INDIRECT TIMING
Table 6 — Indirect Timing (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# · File Path · Line(s) · Function/Class | Trigger Condition | PNT State Observed | Behavior Change Description | Notes
3 Rover/failsafe.cpp 22-30 Rover::failsafe_check() | 1 kHz timer-failsafe ISR; scheduler tick counter unchanged | AP_HAL::micros() (tnow) and AP_Scheduler::ticks() (ticks vs last_ticks) | After > 200,000 us (0.2 s) stall calls arming.disarm(AP_Arming:: Method::CPUFAILSAFE). | [DUPLICATED] INDIRECT/RELATIONAL (timing). Main-loop-lockup watchdog replicated 5 ways — ArduCopter/failsafe.cpp, ArduPlane/failsafe.cpp, Rover/failsafe.cpp, ArduSub/failsafe.cpp (mainloop_failsafe_check) and Blimp/failsafe.cpp — each reads AP_Scheduler::ticks() + AP_HAL::micros(); divergent thresholds/actions (extraction risk).
# 3

## Slide 183
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · INDIRECT TIMING
Table 6 — Indirect Timing (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# · File Path · Line(s) · Function/Class | Trigger Condition | PNT State Observed | Behavior Change Description | Notes
4 ArduSub/failsafe.cpp 31-39 Sub::mainloop_failsafe_check() | 1 kHz timer-failsafe ISR; scheduler tick counter unchanged | AP_HAL::micros() (tnow) and AP_Scheduler::ticks() loop counter | After > 2,000,000 us (2 s) stall sets in_failsafe and drives motors.output_min(). | [DUPLICATED] INDIRECT/RELATIONAL (timing). Main-loop-lockup watchdog replicated 5 ways — ArduCopter/failsafe.cpp, ArduPlane/failsafe.cpp, Rover/failsafe.cpp, ArduSub/failsafe.cpp (mainloop_failsafe_check) and Blimp/failsafe.cpp — each reads AP_Scheduler::ticks() + AP_HAL::micros(); divergent thresholds/actions (extraction risk).
# 4

## Slide 184
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · INDIRECT TIMING
Table 6 — Indirect Timing (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# · File Path · Line(s) · Function/Class | Trigger Condition | PNT State Observed | Behavior Change Description | Notes
5 Blimp/failsafe.cpp 37-45 Blimp::failsafe_check() | 1 kHz timer-failsafe ISR; scheduler tick counter unchanged | AP_HAL::micros() (tnow) and AP_Scheduler::ticks() loop counter | After > 2,000,000 us (2 s) stall sets in_failsafe and drives motors->output_min(). | [DUPLICATED] INDIRECT/RELATIONAL (timing). Main-loop-lockup watchdog replicated 5 ways — ArduCopter/failsafe.cpp, ArduPlane/failsafe.cpp, Rover/failsafe.cpp, ArduSub/failsafe.cpp (mainloop_failsafe_check) and Blimp/failsafe.cpp — each reads AP_Scheduler::ticks() + AP_HAL::micros(); divergent thresholds/actions (extraction risk). Blimp included only because it observes scheduler timing state (AAP 0.3.2).
6 ArduCopter/ekf_check.cpp 84-88 Copter::ekf_check() — GCS warn throttle | EKF variance already flagged bad AND ≥ 30 s elapsed since the last warning | AP_HAL::millis() - ekf_check_state.last_warn_time vs EKF_CHECK_WARNING_TIME (30 s) | Rate-limits the “EKF variance” GCS_SEVERITY_CRITICAL text to at most once per 30 s; stamps last_warn_time = millis(). | [DUPLICATED] INDIRECT/RELATIONAL (timing). [MULTI-CATEGORY w/ Table 5 #1 ekf_check]. 30 s warn-throttle copied in ArduPlane/ekf_check.cpp.
# 5–6

## Slide 185
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · INDIRECT TIMING
Table 6 — Indirect Timing (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# · File Path · Line(s) · Function/Class | Trigger Condition | PNT State Observed | Behavior Change Description | Notes
7 ArduPlane/ekf_check.cpp 78-82 Plane::ekf_check() — GCS warn throttle | EKF variance already flagged bad AND ≥ 30 s elapsed since the last warning | AP_HAL::millis() - ekf_check_state.last_warn_time vs EKF_CHECK_WARNING_TIME (30 s) | Rate-limits the “EKF variance” GCS text to at most once per 30 s; stamps last_warn_time = millis(). | [DUPLICATED] INDIRECT/RELATIONAL (timing). mirrors ArduCopter/ekf_check.cpp:84-88.
8 ArduSub/failsafe.cpp 125-130 Sub::failsafe_ekf_check() — 2 s confirm hysteresis | EKF variance bad but not yet bad for a full 2 s | AP_HAL::millis() vs last_ekf_good_ms + 2000 (2 s clock-based confirmation window) | Suppresses the EKF failsafe (clears failsafe.ekf / ekf_bad and returns) until the EKF has been bad for 2 solid seconds, then trips → arming.disarm(EKFFAILSAFE). | INDIRECT/RELATIONAL (timing). [MULTI-CATEGORY w/ Table 5 #4]. Divergent hysteresis: Sub uses a clock-based 2 s window + 20 s GCS warn-throttle (L141), whereas Copter/Plane use a count-based EKF_CHECK_ITERATIONS_MAX (≈1 s) + 30 s warn-throttle.
9 ArduCopter/ekf_check.cpp 125-132 Copter::ekf_over_threshold() — dt filtering | Each ekf_over_threshold() evaluation (nominally the 10 Hz ekf_check cadence) | AP_HAL::micros() delta → dt = (now_us - last_ekf_check_us) * 1e-6 (actual inter-call interval) | Applies the measured dt to the position/velocity variance low-pass filters (pos_variance_filt / vel_variance_filt); the effective filter cutoff tracks the real scheduler call interval rather than a fixed rate. | INDIRECT/RELATIONAL (timing). [MULTI-CATEGORY w/ Table 5 #1]. EKF check-rate <-> scheduler coupling (AAP 0.5.5): filter behaviour depends on scheduler timing.
# 7–9

## Slide 186
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · INDIRECT TIMING
Table 6 — Indirect Timing (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# · File Path · Line(s) · Function/Class | Trigger Condition | PNT State Observed | Behavior Change Description | Notes
10 ArduCopter/fence.cpp 8-16 Copter::fence_checks_async() | 1 kHz async fence IO callback | AP_HAL::millis() (now) and AP_HAL::timeout_expired(fence_breaches.last_check_ms, now, 40U) (40 ms / 25 Hz gate) | Returns early until 40 ms have elapsed, throttling the geofence breach check to 25 Hz; the position-vs-fence observation itself is Table 4 #3. | [DUPLICATED] INDIRECT/RELATIONAL (timing). [MULTI-CATEGORY w/ Table 4 #3] — timing side of the same function (F1). vs Rover/fence.cpp (divergent rate).
11 Rover/fence.cpp 6-14 Rover::fence_checks_async() | 1 kHz async fence IO callback | AP_HAL::millis() (now) and AP_HAL::timeout_expired(fence_breaches.last_check_ms, now, 100U) (100 ms / 10 Hz gate) | Returns early until 100 ms have elapsed, throttling the geofence breach check to 10 Hz. | [DUPLICATED] INDIRECT/RELATIONAL (timing). [MULTI-CATEGORY w/ Table 4 #9]. vs ArduCopter/fence.cpp:8-16 — divergent rate (40U/25 Hz vs 100U/10 Hz).
# 10–11

## Slide 187
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · VERBATIM SOURCE LINES
Table 6 — Code Snippet (5-10 lines)
Every row’s Code Snippet (5-10 lines), reproduced verbatim from the cited path:line range: one paragraph per source line, in the audit’s own order, with its indentation and its blank lines intact and nothing abbreviated.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
1 | ArduCopter/failsafe.cpp · 37-45 · Copter::failsafe_check() uint32_t tnow = AP_HAL::micros(); const uint16_t ticks = scheduler.ticks(); if (ticks != failsafe_last_ticks) { // the main loop is running, all is OK failsafe_last_ticks = ticks; failsafe_last_timestamp = tnow; if (in_failsafe) { in_failsafe = false;
# 1

## Slide 188
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · VERBATIM SOURCE LINES
Table 6 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
2 | ArduPlane/failsafe.cpp · 22-30 · Plane::failsafe_check() uint32_t tnow = micros(); const uint16_t ticks = scheduler.ticks(); if (ticks != last_ticks) { // the main loop is running, all is OK last_ticks = ticks; last_timestamp = tnow; in_failsafe = false; return;
3 | Rover/failsafe.cpp · 22-30 · Rover::failsafe_check() const uint32_t tnow = AP_HAL::micros(); const uint16_t ticks = scheduler.ticks(); if (ticks != last_ticks) { // the main loop is running, all is OK last_ticks = ticks; last_timestamp = tnow; return; }
# 2–3

## Slide 189
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · VERBATIM SOURCE LINES
Table 6 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
4 | ArduSub/failsafe.cpp · 31-39 · Sub::mainloop_failsafe_check() uint32_t tnow = AP_HAL::micros(); const uint16_t ticks = scheduler.ticks(); if (ticks != failsafe_last_ticks) { // the main loop is running, all is OK failsafe_last_ticks = ticks; failsafe_last_timestamp = tnow; if (in_failsafe) { in_failsafe = false;
5 | Blimp/failsafe.cpp · 37-45 · Blimp::failsafe_check() uint32_t tnow = AP_HAL::micros(); const uint16_t ticks = scheduler.ticks(); if (ticks != failsafe_last_ticks) { // the main loop is running, all is OK failsafe_last_ticks = ticks; failsafe_last_timestamp = tnow; if (in_failsafe) { in_failsafe = false;
# 4–5

## Slide 190
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · VERBATIM SOURCE LINES
Table 6 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
6 | ArduCopter/ekf_check.cpp · 84-88 · Copter::ekf_check() — GCS warn throttle // send message to gcs if ((AP_HAL::millis() - ekf_check_state.last_warn_time) > EKF_CHECK_WARNING_TIME) { gcs().send_text(MAV_SEVERITY_CRITICAL,"EKF variance"); ekf_check_state.last_warn_time = AP_HAL::millis(); }
7 | ArduPlane/ekf_check.cpp · 78-82 · Plane::ekf_check() — GCS warn throttle // send message to gcs if ((AP_HAL::millis() - ekf_check_state.last_warn_time) > EKF_CHECK_WARNING_TIME) { gcs().send_text(MAV_SEVERITY_CRITICAL,"EKF variance"); ekf_check_state.last_warn_time = AP_HAL::millis(); }
8 | ArduSub/failsafe.cpp · 125-130 · Sub::failsafe_ekf_check() — 2 s confirm hysteresis // Bad EKF for 2 solid seconds triggers failsafe if (AP_HAL::millis() < last_ekf_good_ms + 2000) { failsafe.ekf = false; AP_Notify::flags.ekf_bad = false; return; }
# 6–8

## Slide 191
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · VERBATIM SOURCE LINES
Table 6 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
9 | ArduCopter/ekf_check.cpp · 125-132 · Copter::ekf_over_threshold() — dt filtering uint32_t now_us = AP_HAL::micros(); float dt = (now_us - last_ekf_check_us) * 1e-6f; // always update filtered values as this serves the vibration check as well position_var = pos_variance_filt.apply(position_var, dt); vel_var = vel_variance_filt.apply(vel_var, dt); last_ekf_check_us = now_us;
10 | ArduCopter/fence.cpp · 8-16 · Copter::fence_checks_async() void Copter::fence_checks_async() { const uint32_t now = AP_HAL::millis(); if (!AP_HAL::timeout_expired(fence_breaches.last_check_ms, now, 40U)) { // 25Hz update rate return; } if (fence_breaches.have_updates) {
# 9–10

## Slide 192
GROUP 2 — INDIRECT / RELATIONAL PNT REFERENCES · VERBATIM SOURCE LINES
Table 6 — Code Snippet (5-10 lines) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
# | Code Snippet (5-10 lines)
11 | Rover/fence.cpp · 6-14 · Rover::fence_checks_async() void Rover::fence_checks_async() { const uint32_t now = AP_HAL::millis(); if (!AP_HAL::timeout_expired(fence_breaches.last_check_ms, now, 100U)) { // 10Hz update rate return; } if (fence_breaches.have_updates) {
# 11

## Slide 193
DEPENDENCY MAP · LAYER 1 · DIRECT EDGES
Table 6a — Layer 1 dependency map
Table 6a: Layer 1 — direct callers / callees with typed dependency
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Component/Function | Directly Calls | Directly Called By | Dependency Type
1 | Copter::failsafe_check() | AP_HAL::micros(); AP_Scheduler::ticks(); motors->output_min(); motors->armed(false) | failsafe_check_static() <- hal.scheduler->register_timer_failsafe (1 kHz, system.cpp:87) | Function call
2 | Plane::failsafe_check() | micros(); AP_Scheduler::ticks(); rc().read_input(); SRV_Channels::set_output_scaled() | failsafe_check_static() <- hal.scheduler->register_timer_failsafe (1 kHz, system.cpp:103) | Function call
3 | Rover::failsafe_check() | AP_HAL::micros(); AP_Scheduler::ticks(); arming.disarm(CPUFAILSAFE) | failsafe_check_static() <- hal.scheduler->register_timer_failsafe (1 kHz, system.cpp:111) | Function call
4 | Sub::mainloop_failsafe_check() | AP_HAL::micros(); AP_Scheduler::ticks(); motors.output_min() | failsafe_check_static() <- hal.scheduler->register_timer_failsafe (1 kHz, system.cpp:71) | Function call
5 | Blimp::failsafe_check() | AP_HAL::micros(); AP_Scheduler::ticks(); motors->output_min() | failsafe_check_static() <- hal.scheduler->register_timer_failsafe (1 kHz, system.cpp:59) | Function call
# 1–5

## Slide 194
DEPENDENCY MAP · LAYER 1 · DIRECT EDGES
Table 6a — Layer 1 dependency map (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Component/Function | Directly Calls | Directly Called By | Dependency Type
6 | Copter::ekf_check() (warn throttle) | AP_HAL::millis(); gcs().send_text() | Copter::ekf_check() bad-variance branch | Function call
7 | Plane::ekf_check() (warn throttle) | AP_HAL::millis(); gcs().send_text() | Plane::ekf_check() bad-variance branch | Function call
8 | Sub::failsafe_ekf_check() (2 s hysteresis) | AP_HAL::millis(); compares last_ekf_good_ms + 2000 | Sub periodic scheduler | Function call
9 | Copter::ekf_over_threshold() (dt) | AP_HAL::micros(); pos_variance_filt.apply(); vel_variance_filt.apply() | Copter::ekf_check() | Function call
10 | Copter::fence_checks_async() | AP_HAL::millis(); AP_HAL::timeout_expired(.,.,40U) | 1 kHz async IO process (hal.scheduler register_io_process) | Function call
11 | Rover::fence_checks_async() | AP_HAL::millis(); AP_HAL::timeout_expired(.,.,100U) | 1 kHz async IO process (hal.scheduler register_io_process) | Function call
# 6–11

## Slide 195
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 6a — Layer 1 Code Snippet
Every row’s Code Snippet, reproduced verbatim from the cited path:line range: one paragraph per source line, in the audit’s own order, with its indentation and its blank lines intact and nothing abbreviated.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
1 | Copter::failsafe_check() · Function call uint32_t tnow = AP_HAL::micros(); const uint16_t ticks = scheduler.ticks(); if (ticks != failsafe_last_ticks) { // the main loop is running, all is OK failsafe_last_ticks = ticks; failsafe_last_timestamp = tnow; if (in_failsafe) { in_failsafe = false;
2 | Plane::failsafe_check() · Function call uint32_t tnow = micros(); const uint16_t ticks = scheduler.ticks(); if (ticks != last_ticks) { // the main loop is running, all is OK last_ticks = ticks; last_timestamp = tnow; in_failsafe = false; return;
# 1–2

## Slide 196
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 6a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
3 | Rover::failsafe_check() · Function call const uint32_t tnow = AP_HAL::micros(); const uint16_t ticks = scheduler.ticks(); if (ticks != last_ticks) { // the main loop is running, all is OK last_ticks = ticks; last_timestamp = tnow; return; }
4 | Sub::mainloop_failsafe_check() · Function call uint32_t tnow = AP_HAL::micros(); const uint16_t ticks = scheduler.ticks(); if (ticks != failsafe_last_ticks) { // the main loop is running, all is OK failsafe_last_ticks = ticks; failsafe_last_timestamp = tnow; if (in_failsafe) { in_failsafe = false;
# 3–4

## Slide 197
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 6a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
5 | Blimp::failsafe_check() · Function call uint32_t tnow = AP_HAL::micros(); const uint16_t ticks = scheduler.ticks(); if (ticks != failsafe_last_ticks) { // the main loop is running, all is OK failsafe_last_ticks = ticks; failsafe_last_timestamp = tnow; if (in_failsafe) { in_failsafe = false;
6 | Copter::ekf_check() (warn throttle) · Function call // send message to gcs if ((AP_HAL::millis() - ekf_check_state.last_warn_time) > EKF_CHECK_WARNING_TIME) { gcs().send_text(MAV_SEVERITY_CRITICAL,"EKF variance"); ekf_check_state.last_warn_time = AP_HAL::millis(); }
7 | Plane::ekf_check() (warn throttle) · Function call // send message to gcs if ((AP_HAL::millis() - ekf_check_state.last_warn_time) > EKF_CHECK_WARNING_TIME) { gcs().send_text(MAV_SEVERITY_CRITICAL,"EKF variance"); ekf_check_state.last_warn_time = AP_HAL::millis(); }
# 5–7

## Slide 198
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 6a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
8 | Sub::failsafe_ekf_check() (2 s hysteresis) · Function call // Bad EKF for 2 solid seconds triggers failsafe if (AP_HAL::millis() < last_ekf_good_ms + 2000) { failsafe.ekf = false; AP_Notify::flags.ekf_bad = false; return; }
9 | Copter::ekf_over_threshold() (dt) · Function call uint32_t now_us = AP_HAL::micros(); float dt = (now_us - last_ekf_check_us) * 1e-6f; // always update filtered values as this serves the vibration check as well position_var = pos_variance_filt.apply(position_var, dt); vel_var = vel_variance_filt.apply(vel_var, dt); last_ekf_check_us = now_us;
# 8–9

## Slide 199
DEPENDENCY MAP · LAYER 1 · VERBATIM SOURCE LINES
Table 6a — Layer 1 Code Snippet (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | Code Snippet
10 | Copter::fence_checks_async() · Function call void Copter::fence_checks_async() { const uint32_t now = AP_HAL::millis(); if (!AP_HAL::timeout_expired(fence_breaches.last_check_ms, now , 40U)) { // 25Hz update rate return; } if (fence_breaches.have_updates) {
11 | Rover::fence_checks_async() · Function call void Rover::fence_checks_async() { const uint32_t now = AP_HAL::millis(); if (!AP_HAL::timeout_expired(fence_breaches.last_check_ms, now , 100U)) { // 10Hz update rate return; } if (fence_breaches.have_updates) {
# 10–11

## Slide 200
DEPENDENCY MAP · LAYER 2 · DEPTHS 3, 4, 5
Table 6a — Layer 2 transitive chains
Table 6a: Layer 2 — full transitive chain, final consumer & hop depth
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
1 | AP_HAL::micros() + AP_Scheduler tick counter | AP_Scheduler::ticks() / AP_HAL::micros() → failsafe_check_static() [1 kHz timer-failsafe] → Copter::failsafe_check() (>2 s stall) → AP_Motors::output_min()/armed(false) | AP_Motors (motor min / disarm) | 3 | [DUPLICATED] Main-loop-lockup watchdog replicated 5 ways — ArduCopter/failsafe.cpp, ArduPlane/failsafe.cpp, Rover/failsafe.cpp, ArduSub/failsafe.cpp (mainloop_failsafe_check) and Blimp/failsafe.cpp — each reads AP_Scheduler::ticks() + AP_HAL::micros(); divergent thresholds/actions (extraction risk).
2 | AP_HAL::micros() + AP_Scheduler tick counter | AP_Scheduler::ticks() / micros() → failsafe_check_static() → Plane::failsafe_check() (>0.2 s stall) → SRV_Channels::set_output_scaled() → servos_output() | SRV_Channels (RC passthrough) | 4 | [DUPLICATED] watchdog; divergent 0.2 s trip + RC-passthrough action.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 1–2

## Slide 201
DEPENDENCY MAP · LAYER 2 · DEPTHS 3, 4, 5
Table 6a — Layer 2 transitive chains (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
3 | AP_HAL::micros() + AP_Scheduler tick counter | AP_Scheduler::ticks() / micros() → failsafe_check_static() → Rover::failsafe_check() (>0.2 s stall) → AP_Arming::disarm(CPUFAILSAFE) | AP_Arming (disarm) | 3 | [DUPLICATED] watchdog.
4 | AP_HAL::micros() + AP_Scheduler tick counter | AP_Scheduler::ticks() / micros() → failsafe_check_static() → Sub::mainloop_failsafe_check() (>2 s stall) → AP_Motors::output_min() | AP_Motors (motor min) | 3 | [DUPLICATED] watchdog.
5 | AP_HAL::micros() + AP_Scheduler tick counter | AP_Scheduler::ticks() / micros() → failsafe_check_static() → Blimp::failsafe_check() (>2 s stall) → AP_Motors::output_min() | AP_Motors (motor min) | 3 | [DUPLICATED] watchdog; Blimp observes scheduler timing state only (AAP 0.3.2).
6 | AP_HAL::millis() wall clock | AP_HAL::millis() → Copter::ekf_check() (>30 s since last_warn) → gcs().send_text(“EKF variance”) → GCS_MAVLINK | GCS_MAVLINK (telemetry text) | 3 | [DUPLICATED] 30 s warn-throttle (Copter/Plane). [MULTI-CATEGORY w/ Table 5 #1].
7 | AP_HAL::millis() wall clock | AP_HAL::millis() → Plane::ekf_check() (>30 s since last_warn) → gcs().send_text(“EKF variance”) → GCS_MAVLINK | GCS_MAVLINK (telemetry text) | 3 | [DUPLICATED] mirrors #6.
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 3–7

## Slide 202
DEPENDENCY MAP · LAYER 2 · DEPTHS 3, 4, 5
Table 6a — Layer 2 transitive chains (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Ref # | PNT Origin | Full Dependency Chain | Final Consumer | Chain Depth | Notes
8 | AP_HAL::millis() wall clock | AP_HAL::millis() → Sub::failsafe_ekf_check() (EKF bad ≥ 2 s) → failsafe.ekf = true → arming.disarm(EKFFAILSAFE) | AP_Arming (EKF failsafe disarm) | 3 | [MULTI-CATEGORY w/ Table 5 #4]. 2 s confirm + 20 s warn-throttle.
9 | AP_HAL::micros() inter-call interval | AP_HAL::micros() → dt → pos/vel_variance_filt.apply(var, dt) → ekf_over_threshold() → Copter::ekf_check() failsafe decision | Copter::ekf_check() variance decision | 4 | EKF check-rate <-> scheduler coupling (AAP 0.5.5). [MULTI-CATEGORY w/ Table 5 #1].
10 | AP_HAL::millis() wall clock | AP_HAL::millis() → AP_HAL::timeout_expired(40U) gate → Copter::fence_checks_async() → AC_Fence::check() → fence_breaches latched → main-loop fence failsafe | AC_Fence / fence failsafe | 5 | [DUPLICATED] [MULTI-CATEGORY w/ Table 4 #3]. vs Rover (40U/25 Hz).
11 | AP_HAL::millis() wall clock | AP_HAL::millis() → AP_HAL::timeout_expired(100U) gate → Rover::fence_checks_async() → AC_Fence::check() → fence_breaches latched | AC_Fence / fence failsafe | 4 | [DUPLICATED] [MULTI-CATEGORY w/ Table 4 #9]. vs Copter (100U/10 Hz).
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
# 8–11

## Slide 203
DEPENDENCY ROLL-UP · LAYER 1
Layer 1 dependency types across all 94 rows
A roll-up of the audit’s own Dependency Type column values, read cell by cell across the six Layer 1 blocks. It is not a new score, a new metric or a new finding.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Dependency Type (Layer 1) | Rows | What the value records, per the audit’s Legend
Data dependency | 10 | The component reads or writes PNT fields of a shared structure rather than calling for them.
Function call | 61 | The component obtains or hands on the PNT value through a direct call.
Inheritance/Interface | 18 | The component sits behind a base class or interface that the PNT edge is declared on.
Shared global/singleton | 5 | The component reaches the PNT value through a process-wide singleton or global.
All Layer 1 rows | 94 | One Layer 1 row for every catalogued main-table row, which is what makes the distribution exhaustive.
Every Layer 1 row carries exactly one Dependency Type value drawn from the audit’s own four-value vocabulary, so the four figures above account for all 94 rows.

## Slide 204
DEPENDENCY ROLL-UP · LAYER 2
Layer 2 chain depth, and the evidence-row reconciliation
Chain Depth is the audit’s own convention: the number of → hops explicitly listed in that chain.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Sub-table | Chain Depth values present | What the chains run through
Table 1a | 3 4 5 6 8 | Receiver backends through the shared GPS state and the estimator to the motor and servo output, the catalog’s longest chains.
Table 2a | 3 4 | The navigation hub and the estimator stack through to the guidance and mission layer.
Table 3a | 3 4 | The board hardware timer through the hardware-abstraction clock to every periodic PNT task.
Table 4a | 2 3 4 5 | Position health and fence evaluation through to mode denial and failsafe action.
Table 5a | 2 3 4 5 | Estimator-variance watchdogs through to the vehicle’s failsafe response.
Table 6a | 3 4 5 | Main-loop lockup watchdogs and their rate gates through to motor output and disarm.
94
main rows catalogued
3
layers per row
282
evidence rows in total
18
data objects behind them
94 main rows × 3 layers = 282 evidence rows, exactly the total the audit states.

## Slide 205
PNT Instance Audit
Current Location → New Service Location: the audit’s own wiring contract for the extracted service.

## Slide 206
PNT INSTANCE AUDIT · 12 MAPPING ROWS
PNT Instance Audit
Every Position, Navigation and Timing touch-point inside the wrapped controller, with the service member each one is refactored into.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Every Position / Navigation / Timing touch-point inside AP_L1_Control mapped onto the reusable AfsimL1Behavior service (the AHRS state shim, the injected-dt timing seam and the extern "C" command surface).
PNT Pillar | Behavior | Current Location(s) | Current Accessor | New Service Location
Position | Read vehicle position | AP_L1_Control.cpp:L230, L369 | `_ahrs.get_location(_current_loc)` | AHRS shim `get_location()`, fed by `set_state_ne(n, e, …)`
Navigation (velocity) | Read ground velocity vector | AP_L1_Control.cpp:L236, L375, L507 | `_ahrs.groundspeed_vector()` | AHRS shim `groundspeed_vector()`, fed by `set_velocity_EN(velE, velN)`
Navigation (attitude) | Read yaw (radians) | AP_L1_Control.cpp:L59, L61, L402, L536 | `_ahrs.get_yaw_rad()` | AHRS shim `get_yaw_rad()`, fed by `set_yaw_cd(yaw_cd)`
Navigation (attitude) | Read yaw (centideg sensor) | AP_L1_Control.cpp:L70, L72, L503, L535 | `_ahrs.yaw_sensor` | AHRS shim `yaw_sensor`, fed by `set_yaw_cd(yaw_cd)`
Navigation (attitude) | Read pitch (radians) | AP_L1_Control.cpp:L91 | `_ahrs.get_pitch_rad()` | AHRS shim `get_pitch_rad()`, fed by `set_pitch_rad(pitch_rad)`
Navigation (airspeed) | Airspeed scaling factor | AP_L1_Control.cpp:L126, L159 | `_ahrs.get_EAS2TAS()` | AHRS shim `get_EAS2TAS()` (injected or unit default)

## Slide 207
PNT INSTANCE AUDIT · 12 MAPPING ROWS
PNT Instance Audit (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
PNT Pillar | Behavior | Current Location(s) | Current Accessor | New Service Location
Timing | Control-step clock | AP_L1_Control.cpp:L214 | `AP_HAL::micros()` | `set_update_dt(dt)` injected timebase. Additive and default-off: when `set_update_dt` is never called the controller keeps its internal `AP_HAL::micros()` delta, so existing vehicle callers are unaffected.
Timing | Step delta + state store | AP_L1_Control.cpp:L215, L224 | `_last_update_waypoint_us` | Injected-`dt` path (clamp semantics preserved). Additive and default-off: existing callers keep the `_last_update_waypoint_us` `micros()` delta until `set_update_dt` is called.
Timing | Loiter/heading clock | AP_L1_Control.cpp:L448 | `AP_HAL::millis()` | Injected time for the loiter path. Additive and default-off: when unset the internal `AP_HAL::millis()` clock is used unchanged.
Navigation (math) | Bearing / NE distance | AP_L1_Control.cpp:L239, L382 / L260, L266, L274, L295, L391 | `Location::get_bearing_to` / `get_distance_NE` | Preserved unchanged inside `AP_L1_Control`
Navigation (output) | Roll command | AP_L1_Control.h:L36 | `nav_roll_cd()` | `get_roll_deg()` = `nav_roll_cd()/100` → `L1_GetRollDeg`
Navigation (output) | Lateral acceleration | AP_L1_Control.h:L37 | `lateral_acceleration()` | `get_lat_accel()` → `L1_GetLatAccel`

## Slide 208
PNT INSTANCE AUDIT · LINE-NUMBER BASIS, QUOTED
The line-number basis, reproduced unchanged
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
THE AUDIT’S OWN NOTE BENEATH THE MAPPING TABLE
“Line-number basis. The Current Location(s) line numbers below are cited as of the audited HEAD 5b67e27b0a (the pre-refactor baseline), which preserves parity with the AAP 0.6.1 instance table; they are not post-seam current-source line numbers. The extraction's single additive, default-off set_update_dt timing seam was applied to AP_L1_Control.cpp / .h after that commit and shifts only those two files' line numbers (it relocates no behavior). Because the seam is default-off, when set_update_dt is never called the controller keeps its internal AP_HAL::micros() / millis() timing path unchanged, so existing vehicle callers are unaffected.”
THE SERVICE SURFACE THE MAPPING RESOLVES TO
“For every PNT touch-point inside the wrapped L1 guidance controller it names the member of the reusable AfsimL1Behavior service that the behavior is refactored into: the AHRS state shim that supplies injected position, velocity and attitude, the injected-dt timing seam that replaces the internal hardware clock, and the extern "C" command surface that returns the roll and lateral-acceleration commands.”

## Slide 209
Coverage & Explicit-Absence Register
10 sub-registers · 109 entries · 27 checked absences

## Slide 210
COVERAGE REGISTER · NON-INFERENCE DISCIPLINE
What the register establishes
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
THE AUDIT’S OWN INTRODUCTION TO THE REGISTER
“Directory-wide token sweeps and explicit absence notations establishing exhaustiveness across libraries/, the four vehicle directories and the .gitmodules boundary edges (10 sub-registers, 109 entries, 27 checked absences).”
10
named sub-registers
109
register entries
27
checked absences
5
flag kinds in the catalog
The audit’s own footnote to the Audit-Discipline Flags table: Explicitly-documented absences catalogued in the Coverage register: 27.

## Slide 211
COVERAGE REGISTER · THE TEN SUB-REGISTERS
The ten sub-registers, in the audit’s own order
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Sub-register | Title, as catalogued
(1) | Indirect supporting-library register (AAP 0.3.1) — AC_Fence / AP_BattMonitor / AP_RCProtocol: non-PNT triggers whose failsafe action is PNT-gated, plus checked absences.
(2) | Cross-vehicle indirect safety-surface register (F16) — Rover / ArduSub failsafe, fence, and mode surfaces, each resolved to its catalogued numbered-table row.
(3) | AntennaTracker & Blimp PNT-intersection register (F18; AAP 0.3.2 — included only where they observe / consume PNT): presence sites, per-mode gating, and checked absences.
(4) | External-boundary dependency-edge register (AAP 0.4.1 — .gitmodules PNT-relevant vendored submodule boundaries): each boundary resolved to its catalogued PNT edge or publisher site, mirroring the mavlink / DroneCAN edge treatment. Non-inference discipline — every .gitmodules PNT edge is accounted for explicitly, none silently omitted.
(5) | ArduPlane vehicle-dir indirect glue register (vehicle-symmetry completeness, AAP 0.3.1 / 0.6.1): ArduPlane failsafe-action and altitude-management glue that reacts to / consumes PNT state, mirroring the catalogued ArduCopter twins.
(6) | AP_AHRS backend register (Navigation-hub completeness): the AP_AHRS frontend hub is catalogued in Table 2 / 2a; each concrete backend overrides the navigation accessors behind the hub.
(7) | Copter flight modes PNT-gating matrix — 29 files (21 PNT-relevant, 8 checked-absence). Predicate: requires_GPS().
(8) | Plane flight modes PNT-gating matrix — 26 files (20 PNT-relevant, 6 checked-absence). Predicate: does_auto_navigation().
(9) | Rover drive modes PNT-gating matrix — 14 files (11 PNT-relevant, 3 checked-absence). Predicate: requires_position().
(10) | Sub flight modes PNT-gating matrix — 12 files (7 PNT-relevant, 5 checked-absence). Predicate: requires_GPS().

## Slide 212
COVERAGE REGISTER · SUB-REGISTER (1) OF 10
Coverage sub-register (1)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Indirect supporting-library register (AAP 0.3.1) — AC_Fence / AP_BattMonitor / AP_RCProtocol: non-PNT triggers whose failsafe action is PNT-gated, plus checked absences.
Surface / File | PNT Intersection | Detail | Evidence
libraries/AC_Fence/ (AC_Fence::check + check_fence_polygon / check_fence_circle) | Catalogued ✓ | Reads vehicle position vs polygon / circle / altitude fence; position-dependent breach. Fully catalogued in the numbered tables (not an absence). | libraries/AC_Fence/AC_Fence.cpp:679-843 · Table 4 #4-#8 / Table 4a
libraries/AP_BattMonitor/ (58 source files; AP_BattMonitor::check_failsafes) | [ABSENT] checked | Directory-wide token sweep found ZERO PNT reads (no ahrs. / gps. / get_location / position_ok / get_velocity_NED). Failsafe trigger is voltage / capacity only; PNT enters at the vehicle action layer, not here. | libraries/AP_BattMonitor/AP_BattMonitor.cpp:781 (check_failsafes) · action cross-ref ArduCopter/events.cpp:99-121
libraries/AP_RCProtocol/ (RC failsafe flag) | [ABSENT] checked | Token sweep found ZERO PNT reads. Failsafe is a boolean signal-present flag (failsafe_active); no position / nav / PNT-timing observation. PNT enters at the vehicle action layer. | libraries/AP_RCProtocol/AP_RCProtocol.h:126-130 (failsafe_active) · action cross-ref ArduCopter/events.cpp:99-121
ArduCopter/events.cpp (handle_battery_failsafe / radio / GCS FS action select) | PNT-reactive ✓ | Non-PNT trigger (battery / RC / GCS) but the chosen failsafe action (RTL / SmartRTL) is gated on position_ok and degrades to LAND when position is invalid — the relational PNT site for batt / RC / GCS failsafe. | ArduCopter/events.cpp:99-121 (do_failsafe_action BATTERY_FAILSAFE) · gate Table 4 #2

## Slide 213
COVERAGE REGISTER · SUB-REGISTER (2) OF 10
Coverage sub-register (2)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Cross-vehicle indirect safety-surface register (F16) — Rover / ArduSub failsafe, fence, and mode surfaces, each resolved to its catalogued numbered-table row.
Surface / File | PNT Intersection | Detail | Evidence
Rover/failsafe.cpp (Rover::failsafe_check main-loop watchdog) | Catalogued ✓ | Main-loop-lockup watchdog reading scheduler ticks + micros; 0.2 s trip → arming.disarm(CPUFAILSAFE). Catalogued, not an absence. | Rover/failsafe.cpp:18-31 · Table 6 #3 / Table 6a #3
Rover/fence.cpp (Rover::fence_checks_async) | Catalogued ✓ | Geofence position-vs-boundary check on a 100 ms (10 Hz) timing gate; position-dependent breach. Catalogued. | Rover/fence.cpp:6-14 · Table 6 #11 / Table 6a #11
ArduSub/failsafe.cpp (Sub::failsafe_ekf_check) | Catalogued ✓ | EKF-variance health watchdog with 2 s confirm + 20 s warn hysteresis. Catalogued. | ArduSub/failsafe.cpp:100-150 · Table 5 #4 / Table 6 #8
ArduSub/failsafe.cpp (Sub::mainloop_failsafe_check) | Catalogued ✓ | Main-loop-lockup watchdog (scheduler ticks + micros; 2 s → motors.output_min). Catalogued. | ArduSub/failsafe.cpp:29-55 · Table 6 #4 / Table 6a #4
ArduSub/mode*.cpp (12 files) | Catalogued ✓ | All 12 Sub mode files enumerated with per-file requires_GPS gating and checked absences in the Sub mode-gating matrix below. | ArduSub/mode.cpp:89-90 (set_mode gate) · Sub mode-gating matrix (this appendix)

## Slide 214
COVERAGE REGISTER · SUB-REGISTER (3) OF 10
Coverage sub-register (3)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
AntennaTracker & Blimp PNT-intersection register (F18; AAP 0.3.2 — included only where they observe / consume PNT): presence sites, per-mode gating, and checked absences.
Surface / File | PNT Intersection | Detail | Evidence
AntennaTracker/tracking.cpp (Tracker::update_vehicle_pos_estimate) | PNT consumer ✓ | Reads vehicle.location and vehicle.vel and dead-reckons location_estimate (offset by vel times dt) to point the antenna. Direct PNT consumption (presence, not absence). | AntennaTracker/tracking.cpp:7-26
AntennaTracker/mode_auto.cpp + mode_guided.cpp | PNT consumer ✓ | Auto / Guided pointing modes consume the tracked vehicle position / bearing to drive pitch and yaw. PNT-reactive. | AntennaTracker/mode_auto.cpp:5-10 · consumes tracking.cpp:7-26
AntennaTracker/mode_manual.cpp + mode_scan.cpp + mode_servotest.cpp | [ABSENT] checked | Manual / Scan / Servotest drive the antenna by stick / pattern / test only; token sweep found ZERO vehicle-position reads. Checked absence. | AntennaTracker/mode_servotest.cpp (0 PNT tokens) · mode_scan.cpp / mode_manual.cpp (0)
Blimp/mode.cpp (Blimp::set_mode position gate) | Gate enforcer ✓ | Rejects PNT modes when position invalid: requires_GPS() and not blimp.position_ok(). Same gate idiom as Copter / Sub. | Blimp/mode.cpp:78-79
Blimp/mode_velocity.cpp (ModeVelocity) | Position-gated ✓ | requires_GPS()=true → needs a valid position / velocity estimate to enter. | Blimp/mode.h:181 (requires_GPS=true) · gate Blimp/mode.cpp:78-79
Blimp/mode_loiter.cpp (ModeLoiter) | Position-gated ✓ | requires_GPS()=true → position-gated. | Blimp/mode.h:226 (requires_GPS=true) · gate Blimp/mode.cpp:78-79

## Slide 215
COVERAGE REGISTER · SUB-REGISTER (3) OF 10
Coverage sub-register (3) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Surface / File | PNT Intersection | Detail | Evidence
Blimp/mode_rtl.cpp (ModeRTL) | Position-gated ✓ | requires_GPS()=true → position-gated. | Blimp/mode.h:315 (requires_GPS=true) · gate Blimp/mode.cpp:78-79
Blimp/mode_manual.cpp (ModeManual) | [ABSENT] checked | requires_GPS()=false → no position gate; manual stick control. Checked absence. | Blimp/mode.h:138 (requires_GPS=false)
Blimp/mode_land.cpp (ModeLand) | [ABSENT] checked | requires_GPS()=false → no horizontal-position gate (descent uses non-PNT references). Checked absence for horizontal PNT. | Blimp/mode.h:271 (requires_GPS=false)
Blimp/failsafe.cpp (Blimp::failsafe_check watchdog) | Catalogued ✓ | Main-loop-lockup watchdog (scheduler ticks + micros; 2 s → output_min). Catalogued. | Blimp/failsafe.cpp:37-45 · Table 6 #5 / Table 6a #5

## Slide 216
COVERAGE REGISTER · SUB-REGISTER (4) OF 10
Coverage sub-register (4)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
External-boundary dependency-edge register (AAP 0.4.1 — .gitmodules PNT-relevant vendored submodule boundaries): each boundary resolved to its catalogued PNT edge or publisher site, mirroring the mavlink / DroneCAN edge treatment. Non-inference discipline — every .gitmodules PNT edge is accounted for explicitly, none silently omitted.
Surface / File | PNT Intersection | Detail | Evidence
modules/mavlink (MAVLink message definitions) | Catalogued (edge) ✓ | GPS_INPUT ingress (AP_GPS_MAV Source backend) and NAV_CONTROLLER_OUTPUT egress (navigation-health reporting to the GCS). PNT telemetry boundary — catalogued, not an absence. | .gitmodules:7-9 · Table 1 (AP_GPS_MAV.cpp:67-75 handle_msg) · Table 5 (ArduPlane/GCS_MAVLink_Plane.cpp:204-212 send_nav_controller_output)
modules/DroneCAN/DSDL + libcanard (CAN-bus GNSS message definitions) | Catalogued (edge) ✓ | DroneCAN / UAVCAN Fix2 GNSS messages decoded into GPS_State. Positioning-source boundary — catalogued, not an absence. | .gitmodules:19-32 · Table 1 (AP_GPS_DroneCAN.cpp:388-396 handle_fix2_msg)
modules/ChibiOS (RTOS low-level clock / tick primitives) | Catalogued (edge) ✓ | Board RTOS timer backs the AP_HAL::micros() / millis() monotonic-time primitives. Timing boundary — named explicitly here as the board-timer origin of Table 3a #1. | .gitmodules:13-15 · Table 3 #1 (AP_HAL/system.h:15-20) · Table 3a #1 (RTOS / board-hardware-timer origin)

## Slide 217
COVERAGE REGISTER · SUB-REGISTER (4) OF 10
Coverage sub-register (4) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Surface / File | PNT Intersection | Detail | Evidence
modules/Micro-XRCE-DDS-Client + modules/Micro-CDR (DDS transport, AP_DDS → ROS2) | PNT publisher (edge) ✓ | AP_DDS (AP_DDS_ENABLED=1 by default) reads PNT state and publishes it over the Micro-XRCE-DDS / Micro-CDR transport to ROS2: sensor_msgs/NavSatFix from gps.location() and geographic_msgs/GeoPoseStamped from ahrs.get_location(). PNT-egress boundary — same edge treatment as mavlink / DroneCAN. | .gitmodules:34-40 · libraries/AP_DDS/AP_DDS_Client.cpp:268-270 (NavSatFix ← gps.location) · :577-584 (GeoPose ← ahrs.get_location) · AP_DDS_config.h:11 (#define AP_DDS_ENABLED 1)

## Slide 218
COVERAGE REGISTER · SUB-REGISTER (5) OF 10
Coverage sub-register (5)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
ArduPlane vehicle-dir indirect glue register (vehicle-symmetry completeness, AAP 0.3.1 / 0.6.1): ArduPlane failsafe-action and altitude-management glue that reacts to / consumes PNT state, mirroring the catalogued ArduCopter twins.
Surface / File | PNT Intersection | Detail | Evidence
ArduPlane/events.cpp (Plane::handle_battery_failsafe / failsafe_long_on_event / failsafe_short_on_event) | PNT-reactive ✓ | Non-PNT trigger (battery / radio / GCS) but the chosen failsafe action is PNT-gated: handle_battery_failsafe reads plane.have_position and plane.current_loc to choose land-sequence continuation vs RTL. Direct Plane analog of the catalogued ArduCopter/events.cpp. | ArduPlane/events.cpp:290-300 (have_position / current_loc land-sequence gate; def @265) · symmetric with ArduCopter/events.cpp:99-121 · gate ArduPlane/mode.cpp:144
ArduPlane/altitude.cpp (Plane::setup_alt_slope / check_home_alt_change) | PNT consumer (Sink) ✓ | Positioning Sink: re-reads already-catalogued PNT state — current_loc.get_distance() / line_path_proportion() (AHRS get_location, Table 2) and ahrs.get_home() — to derive the glide slope and altitude target. Consumes, does not produce, PNT. | ArduPlane/altitude.cpp:48-55 (setup_alt_slope current_loc distance) · :31-43 (check_home_alt_change ahrs.get_home) · :109 & :202 (current_loc.alt)

## Slide 219
COVERAGE REGISTER · SUB-REGISTER (6) OF 10
Coverage sub-register (6)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
AP_AHRS backend register (Navigation-hub completeness): the AP_AHRS frontend hub is catalogued in Table 2 / 2a; each concrete backend overrides the navigation accessors behind the hub.
Surface / File | PNT Intersection | Detail | Evidence
AP_AHRS_DCM (libraries/AP_AHRS/AP_AHRS_DCM.cpp) | Catalogued ✓ | Legacy DCM estimator backend; overrides get_location / groundspeed. Cited in the numbered Navigation tables alongside the hub. | libraries/AP_AHRS/AP_AHRS_DCM.cpp · Table 2 / Table 2a (AHRS hub + DCM)
AP_AHRS_External (libraries/AP_AHRS/AP_AHRS_External.cpp) | PNT backend ✓ | External-AHRS backend feeding the hub from an external INS; overrides the position accessor (get_origin). Navigation Source backend behind the AP_AHRS frontend. | libraries/AP_AHRS/AP_AHRS_External.cpp:128 (get_origin) · AP_AHRS_External.h:30 (class : public AP_AHRS_Backend)
AP_AHRS_SIM (libraries/AP_AHRS/AP_AHRS_SIM.cpp) | PNT backend ✓ | SITL simulation backend supplying simulated navigation state to the hub; overrides get_location / get_origin. Navigation Source backend behind the AP_AHRS frontend. | libraries/AP_AHRS/AP_AHRS_SIM.cpp:7 (get_location) · :194 (get_origin) · AP_AHRS_SIM.h:37 (class : public AP_AHRS_Backend)

## Slide 220
COVERAGE REGISTER · SUB-REGISTER (7) OF 10
Coverage sub-register (7)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Copter flight modes PNT-gating matrix — 29 files (21 PNT-relevant, 8 checked-absence). Predicate: requires_GPS().
Surface / File | PNT Intersection | Detail | Evidence
mode.cpp (Copter::set_mode() position gate) | Gate enforcer ✓ | new_flightmode->requires_GPS() && !copter.position_ok() rejects PNT modes when position invalid | ArduCopter/mode.cpp:303-307 · Table 4 #2
mode_acro.cpp (ModeAcro) | [ABSENT] checked | requires_GPS()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | ArduCopter/mode.h:428 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_acro_heli.cpp (ModeAcro_Heli) | [ABSENT] checked | requires_GPS()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | ArduCopter/mode.h:428 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_althold.cpp (ModeAltHold) | PNT (no horiz-GPS gate) ✓ | requires_GPS()=false, but consumes PNT here (pos_control ×9; e.g. altitude pos_control / optical-flow / optional position). | ArduCopter/mode.h:484 · use ArduCopter/mode_althold.cpp:13 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_auto.cpp (ModeAuto) | Position-gated ✓ | requires_GPS()=true (conditional: all sub-modes except NAV_ATTITUDE_TIME) — PNT position/nav required to enter; behaviour gated. | ArduCopter/mode_auto.cpp:178 · use ArduCopter/mode_auto.cpp:42 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_autorotate.cpp (ModeAutorotate) | [ABSENT] checked | requires_GPS()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | ArduCopter/mode.h:2047 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)

## Slide 221
COVERAGE REGISTER · SUB-REGISTER (7) OF 10
Coverage sub-register (7) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Surface / File | PNT Intersection | Detail | Evidence
mode_autotune.cpp (ModeAutoTune) | PNT (no horiz-GPS gate) ✓ | requires_GPS()=false, but consumes PNT here (pos_control ×5; e.g. altitude pos_control / optical-flow / optional position). | ArduCopter/mode.h:829 · use ArduCopter/mode_autotune.cpp:31 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_avoid_adsb.cpp (ModeAvoidADSB) | Position-gated ✓ | requires_GPS()=true — PNT position/nav required to enter; behaviour gated. | ArduCopter/mode.h:1888 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_brake.cpp (ModeBrake) | Position-gated ✓ | requires_GPS()=true — PNT position/nav required to enter; behaviour gated. | ArduCopter/mode.h:854 · use ArduCopter/mode_brake.cpp:13 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_circle.cpp (ModeCircle) | Position-gated ✓ | requires_GPS()=true — PNT position/nav required to enter; behaviour gated. | ArduCopter/mode.h:884 · use ArduCopter/mode_circle.cpp:16 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_drift.cpp (ModeDrift) | Position-gated ✓ | requires_GPS()=true — PNT position/nav required to enter; behaviour gated. | ArduCopter/mode.h:914 · use ArduCopter/mode_drift.cpp:54 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_flip.cpp (ModeFlip) | [ABSENT] checked | requires_GPS()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | ArduCopter/mode.h:942 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)

## Slide 222
COVERAGE REGISTER · SUB-REGISTER (7) OF 10
Coverage sub-register (7) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Surface / File | PNT Intersection | Detail | Evidence
mode_flowhold.cpp (ModeFlowHold) | PNT (no horiz-GPS gate) ✓ | requires_GPS()=false, but consumes PNT here (pos_control ×12; e.g. altitude pos_control / optical-flow / optional position). | ArduCopter/mode.h:989 · use ArduCopter/mode_flowhold.cpp:92 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_follow.cpp (ModeFollow) | Position-gated ✓ | requires_GPS()=true — PNT position/nav required to enter; behaviour gated. | ArduCopter/mode.h:1918 · use ArduCopter/mode_follow.cpp:33 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_guided.cpp (ModeGuided) | Position-gated ✓ | requires_GPS()=true — PNT position/nav required to enter; behaviour gated. | ArduCopter/mode.h:1077 · use ArduCopter/mode_guided.cpp:77 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_guided_custom.cpp (ModeGuidedCustom) | Position-gated ✓ | requires_GPS()=true — PNT position/nav required to enter; behaviour gated. | ArduCopter/mode.h:1077 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_guided_nogps.cpp (ModeGuidedNoGPS) | [ABSENT] checked | requires_GPS()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | ArduCopter/mode.h:1253 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_land.cpp (ModeLand) | PNT (no horiz-GPS gate) ✓ | requires_GPS()=false, but consumes PNT here (position_ok ×9; e.g. altitude pos_control / optical-flow / optional position). | ArduCopter/mode.h:1277 · use ArduCopter/mode_land.cpp:7 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)

## Slide 223
COVERAGE REGISTER · SUB-REGISTER (7) OF 10
Coverage sub-register (7) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Surface / File | PNT Intersection | Detail | Evidence
mode_loiter.cpp (ModeLoiter) | Position-gated ✓ | requires_GPS()=true — PNT position/nav required to enter; behaviour gated. | ArduCopter/mode.h:1323 · use ArduCopter/mode_loiter.cpp:17 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_poshold.cpp (ModePosHold) | Position-gated ✓ | requires_GPS()=true — PNT position/nav required to enter; behaviour gated. | ArduCopter/mode.h:1373 · use ArduCopter/mode_poshold.cpp:28 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_rtl.cpp (ModeRTL) | Position-gated ✓ | requires_GPS()=true — PNT position/nav required to enter; behaviour gated. | ArduCopter/mode.h:1461 · use ArduCopter/mode_rtl.cpp:21 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_smart_rtl.cpp (ModeSmartRTL) | Position-gated ✓ | requires_GPS()=true — PNT position/nav required to enter; behaviour gated. | ArduCopter/mode.h:1577 · use ArduCopter/mode_smart_rtl.cpp:16 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_sport.cpp (ModeSport) | PNT (no horiz-GPS gate) ✓ | requires_GPS()=false, but consumes PNT here (pos_control ×9; e.g. altitude pos_control / optical-flow / optional position). | ArduCopter/mode.h:1637 · use ArduCopter/mode_sport.cpp:13 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)

## Slide 224
COVERAGE REGISTER · SUB-REGISTER (7) OF 10
Coverage sub-register (7) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Surface / File | PNT Intersection | Detail | Evidence
mode_stabilize.cpp (ModeStabilize) | [ABSENT] checked | requires_GPS()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | ArduCopter/mode.h:1664 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_stabilize_heli.cpp (ModeStabilize_Heli) | [ABSENT] checked | requires_GPS()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | ArduCopter/mode.h:1664 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_systemid.cpp (ModeSystemId) | PNT (no horiz-GPS gate) ✓ | requires_GPS()=false, but consumes PNT here (pos_control ×22; e.g. altitude pos_control / optical-flow / optional position). | ArduCopter/mode.h:1712 · use ArduCopter/mode_systemid.cpp:115 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_throw.cpp (ModeThrow) | Position-gated ✓ | requires_GPS()=true — PNT position/nav required to enter; behaviour gated. | ArduCopter/mode.h:1791 · use ArduCopter/mode_throw.cpp:23 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_turtle.cpp (ModeTurtle) | [ABSENT] checked | requires_GPS()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | ArduCopter/mode.h:1849 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)
mode_zigzag.cpp (ModeZigZag) | Position-gated ✓ | requires_GPS()=true — PNT position/nav required to enter; behaviour gated. | ArduCopter/mode.h:1967 · use ArduCopter/mode_zigzag.cpp:75 · gate Table 4 #2 (ArduCopter/mode.cpp:303-307)

## Slide 225
COVERAGE REGISTER · SUB-REGISTER (8) OF 10
Coverage sub-register (8)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Plane flight modes PNT-gating matrix — 26 files (20 PNT-relevant, 6 checked-absence). Predicate: does_auto_navigation().
Surface / File | PNT Intersection | Detail | Evidence
mode.cpp (Plane::set_mode() / mode enter) | Gate enforcer ✓ | does_auto_navigation() consulted; nav modes consume EKF/AHRS nav state | ArduPlane/mode.cpp:144
mode_LoiterAltQLand.cpp (ModeLoiterAltQLand) | Position-gated ✓ | does_auto_navigation()=true — PNT position/nav required to enter; behaviour gated. | ArduPlane/mode.h:427 · use ArduPlane/mode_LoiterAltQLand.cpp:8 · gate ArduPlane/mode.cpp:144
mode_acro.cpp (ModeAcro) | [ABSENT] checked | does_auto_navigation()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | gate ArduPlane/mode.cpp:144
mode_auto.cpp (ModeAuto) | Position-gated ✓ | does_auto_navigation()=true — PNT position/nav required to enter; behaviour gated. | ArduPlane/mode_auto.cpp:137 · use ArduPlane/mode_auto.cpp:10 · gate ArduPlane/mode.cpp:144
mode_autoland.cpp (ModeAutoLand) | Position-gated ✓ | does_auto_navigation()=true — PNT position/nav required to enter; behaviour gated. | ArduPlane/mode.h:957 · use ArduPlane/mode_autoland.cpp:79 · gate ArduPlane/mode.cpp:144
mode_autotune.cpp (ModeAutoTune) | [ABSENT] checked | does_auto_navigation()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | gate ArduPlane/mode.cpp:144

## Slide 226
COVERAGE REGISTER · SUB-REGISTER (8) OF 10
Coverage sub-register (8) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Surface / File | PNT Intersection | Detail | Evidence
mode_avoidADSB.cpp (ModeAvoidADSB) | PNT (no horiz-GPS gate) ✓ | does_auto_navigation()=false, but consumes PNT here (update_loiter ×1; e.g. altitude pos_control / optical-flow / optional position). | use ArduPlane/mode_avoidADSB.cpp:19 · gate ArduPlane/mode.cpp:144
mode_circle.cpp (ModeCircle) | Position-gated ✓ | does_auto_navigation()=true — PNT position/nav required to enter; behaviour gated. | ArduPlane/mode.h:399 · use ArduPlane/mode_circle.cpp:7 · gate ArduPlane/mode.cpp:144
mode_cruise.cpp (ModeCruise) | PNT (no horiz-GPS gate) ✓ | does_auto_navigation()=false, but consumes PNT here (prev_WP_loc ×4; e.g. altitude pos_control / optical-flow / optional position). | use ArduPlane/mode_cruise.cpp:83 · gate ArduPlane/mode.cpp:144
mode_fbwa.cpp (ModeFBWA) | [ABSENT] checked | does_auto_navigation()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | gate ArduPlane/mode.cpp:144
mode_fbwb.cpp (ModeFBWB) | [ABSENT] checked | does_auto_navigation()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | gate ArduPlane/mode.cpp:144
mode_guided.cpp (ModeGuided) | Position-gated ✓ | does_auto_navigation()=true — PNT position/nav required to enter; behaviour gated. | ArduPlane/mode.h:360 · use ArduPlane/mode_guided.cpp:11 · gate ArduPlane/mode.cpp:144
mode_loiter.cpp (ModeLoiter) | Position-gated ✓ | does_auto_navigation()=true — PNT position/nav required to enter; behaviour gated. | ArduPlane/mode.h:427 · use ArduPlane/mode_loiter.cpp:7 · gate ArduPlane/mode.cpp:144

## Slide 227
COVERAGE REGISTER · SUB-REGISTER (8) OF 10
Coverage sub-register (8) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Surface / File | PNT Intersection | Detail | Evidence
mode_manual.cpp (ModeManual) | PNT (no horiz-GPS gate) ✓ | does_auto_navigation()=false, but consumes PNT here (quadplane. ×1; e.g. altitude pos_control / optical-flow / optional position). | use ArduPlane/mode_manual.cpp:26 · gate ArduPlane/mode.cpp:144
mode_qacro.cpp (ModeQAcro) | PNT (no horiz-GPS gate) ✓ | does_auto_navigation()=false, but consumes PNT here (quadplane. ×16; e.g. altitude pos_control / optical-flow / optional position). | use ArduPlane/mode_qacro.cpp:8 · gate ArduPlane/mode.cpp:144
mode_qautotune.cpp (ModeQAutotune) | PNT (no horiz-GPS gate) ✓ | does_auto_navigation()=false, but consumes PNT here (quadplane. ×4; e.g. altitude pos_control / optical-flow / optional position). | use ArduPlane/mode_qautotune.cpp:11 · gate ArduPlane/mode.cpp:144
mode_qhover.cpp (ModeQHover) | PNT (no horiz-GPS gate) ✓ | does_auto_navigation()=false, but consumes PNT here (pos_control ×13; e.g. altitude pos_control / optical-flow / optional position). | use ArduPlane/mode_qhover.cpp:9 · gate ArduPlane/mode.cpp:144
mode_qland.cpp (ModeQLand) | PNT (no horiz-GPS gate) ✓ | does_auto_navigation()=false, but consumes PNT here (quadplane. ×5; e.g. altitude pos_control / optical-flow / optional position). | use ArduPlane/mode_qland.cpp:9 · gate ArduPlane/mode.cpp:144
mode_qloiter.cpp (ModeQLoiter) | PNT (no horiz-GPS gate) ✓ | does_auto_navigation()=false, but consumes PNT here (loiter_nav ×52; e.g. altitude pos_control / optical-flow / optional position). | use ArduPlane/mode_qloiter.cpp:9 · gate ArduPlane/mode.cpp:144
mode_qrtl.cpp (ModeQRTL) | PNT (no horiz-GPS gate) ✓ | does_auto_navigation()=false, but consumes PNT here (quadplane. ×47; e.g. altitude pos_control / optical-flow / optional position). | use ArduPlane/mode_qrtl.cpp:10 · gate ArduPlane/mode.cpp:144

## Slide 228
COVERAGE REGISTER · SUB-REGISTER (8) OF 10
Coverage sub-register (8) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Surface / File | PNT Intersection | Detail | Evidence
mode_qstabilize.cpp (ModeQStabilize) | PNT (no horiz-GPS gate) ✓ | does_auto_navigation()=false, but consumes PNT here (quadplane. ×19; e.g. altitude pos_control / optical-flow / optional position). | use ArduPlane/mode_qstabilize.cpp:8 · gate ArduPlane/mode.cpp:144
mode_rtl.cpp (ModeRTL) | Position-gated ✓ | does_auto_navigation()=true — PNT position/nav required to enter; behaviour gated. | ArduPlane/mode.h:507 · use ArduPlane/mode_rtl.cpp:6 · gate ArduPlane/mode.cpp:144
mode_stabilize.cpp (ModeStabilize) | [ABSENT] checked | does_auto_navigation()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | gate ArduPlane/mode.cpp:144
mode_takeoff.cpp (ModeTakeoff) | Position-gated ✓ | does_auto_navigation()=true — PNT position/nav required to enter; behaviour gated. | ArduPlane/mode.h:909 · use ArduPlane/mode_takeoff.cpp:74 · gate ArduPlane/mode.cpp:144
mode_thermal.cpp (ModeThermal) | Position-gated ✓ | does_auto_navigation()=true — PNT position/nav required to enter; behaviour gated. | ArduPlane/mode.h:1025 · use ArduPlane/mode_thermal.cpp:16 · gate ArduPlane/mode.cpp:144
mode_training.cpp (ModeTraining) | [ABSENT] checked | does_auto_navigation()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | gate ArduPlane/mode.cpp:144

## Slide 229
COVERAGE REGISTER · SUB-REGISTER (9) OF 10
Coverage sub-register (9)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Rover drive modes PNT-gating matrix — 14 files (11 PNT-relevant, 3 checked-absence). Predicate: requires_position().
Surface / File | PNT Intersection | Detail | Evidence
mode.cpp (Mode::enter() position gate) | Gate enforcer ✓ | rover.ekf_position_ok() && requires_position()/requires_velocity() gate entry | Rover/mode.cpp:32-38
mode_acro.cpp (ModeAcro) | PNT (no horiz-GPS gate) ✓ | requires_position()=false, but consumes PNT here (wp_nav ×1; e.g. altitude pos_control / optical-flow / optional position). | Rover/mode.h:235 · use Rover/mode_acro.cpp:37 · gate Rover/mode.cpp:32-38
mode_auto.cpp (ModeAuto) | Position-gated ✓ | requires_position()=true — PNT position/nav required to enter; behaviour gated. | use Rover/mode_auto.cpp:14 · gate Rover/mode.cpp:32-38
mode_circle.cpp (ModeCircle) | Position-gated ✓ | requires_position()=true — PNT position/nav required to enter; behaviour gated. | use Rover/mode_circle.cpp:85 · gate Rover/mode.cpp:32-38
mode_dock.cpp (ModeDock) | Position-gated ✓ | requires_position()=true — PNT position/nav required to enter; behaviour gated. | use Rover/mode_dock.cpp:75 · gate Rover/mode.cpp:32-38
mode_follow.cpp (ModeFollow) | Position-gated ✓ | requires_position()=true — PNT position/nav required to enter; behaviour gated. | use Rover/mode_follow.cpp:12 · gate Rover/mode.cpp:32-38
mode_guided.cpp (ModeGuided) | Position-gated ✓ | requires_position()=true — PNT position/nav required to enter; behaviour gated. | use Rover/mode_guided.cpp:15 · gate Rover/mode.cpp:32-38
mode_hold.cpp (ModeHold) | [ABSENT] checked | requires_position()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | Rover/mode.h:630 · gate Rover/mode.cpp:32-38
mode_loiter.cpp (ModeLoiter) | Position-gated ✓ | requires_position()=true — PNT position/nav required to enter; behaviour gated. | use Rover/mode_loiter.cpp:6 · gate Rover/mode.cpp:32-38

## Slide 230
COVERAGE REGISTER · SUB-REGISTER (9) OF 10
Coverage sub-register (9) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Surface / File | PNT Intersection | Detail | Evidence
mode_manual.cpp (ModeManual) | [ABSENT] checked | requires_position()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | Rover/mode.h:681 · gate Rover/mode.cpp:32-38
mode_rtl.cpp (ModeRTL) | Position-gated ✓ | requires_position()=true — PNT position/nav required to enter; behaviour gated. | use Rover/mode_rtl.cpp:11 · gate Rover/mode.cpp:32-38
mode_simple.cpp (ModeSimple) | Position-gated ✓ | requires_position()=true — PNT position/nav required to enter; behaviour gated. | gate Rover/mode.cpp:32-38
mode_smart_rtl.cpp (ModeSmartRTL) | Position-gated ✓ | requires_position()=true — PNT position/nav required to enter; behaviour gated. | use Rover/mode_smart_rtl.cpp:17 · gate Rover/mode.cpp:32-38
mode_steering.cpp (ModeSteering) | [ABSENT] checked | requires_position()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | Rover/mode.h:785 · gate Rover/mode.cpp:32-38

## Slide 231
COVERAGE REGISTER · SUB-REGISTER (10) OF 10
Coverage sub-register (10)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Sub flight modes PNT-gating matrix — 12 files (7 PNT-relevant, 5 checked-absence). Predicate: requires_GPS().
Surface / File | PNT Intersection | Detail | Evidence
mode.cpp (Sub::set_mode() position gate) | Gate enforcer ✓ | new_flightmode->requires_GPS() && !sub.position_ok() rejects PNT modes | ArduSub/mode.cpp:89-90
mode_acro.cpp (ModeAcro) | [ABSENT] checked | requires_GPS()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | ArduSub/mode.h:155 · gate ArduSub/mode.cpp:89-90
mode_althold.cpp (ModeAlthold) | [ABSENT] checked | requires_GPS()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | ArduSub/mode.h:201 · gate ArduSub/mode.cpp:89-90
mode_auto.cpp (ModeAuto) | Position-gated ✓ | requires_GPS()=true — PNT position/nav required to enter; behaviour gated. | ArduSub/mode.h:314 · use ArduSub/mode_auto.cpp:11 · gate ArduSub/mode.cpp:89-90
mode_circle.cpp (ModeCircle) | Position-gated ✓ | requires_GPS()=true — PNT position/nav required to enter; behaviour gated. | ArduSub/mode.h:382 · use ArduSub/mode_circle.cpp:10 · gate ArduSub/mode.cpp:89-90
mode_guided.cpp (ModeGuided) | Position-gated ✓ | requires_GPS()=true — PNT position/nav required to enter; behaviour gated. | ArduSub/mode.h:260 · use ArduSub/mode_guided.cpp:34 · gate ArduSub/mode.cpp:89-90
mode_manual.cpp (ModeManual) | [ABSENT] checked | requires_GPS()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | ArduSub/mode.h:132 · gate ArduSub/mode.cpp:89-90

## Slide 232
COVERAGE REGISTER · SUB-REGISTER (10) OF 10
Coverage sub-register (10) (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Surface / File | PNT Intersection | Detail | Evidence
mode_motordetect.cpp (ModeMotordetect) | [ABSENT] checked | requires_GPS()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | ArduSub/mode.h:427 · gate ArduSub/mode.cpp:89-90
mode_poshold.cpp (ModePoshold) | Position-gated ✓ | requires_GPS()=true — PNT position/nav required to enter; behaviour gated. | ArduSub/mode.h:355 · use ArduSub/mode_poshold.cpp:13 · gate ArduSub/mode.cpp:89-90
mode_stabilize.cpp (ModeStabilize) | [ABSENT] checked | requires_GPS()=false and zero position/nav/velocity tokens — manual/attitude mode; no PNT dependence (checked absence). | ArduSub/mode.h:178 · gate ArduSub/mode.cpp:89-90
mode_surface.cpp (ModeSurface) | PNT (no horiz-GPS gate) ✓ | requires_GPS()=false, but consumes PNT here (wp_nav ×1; e.g. altitude pos_control / optical-flow / optional position). | ArduSub/mode.h:404 · use ArduSub/mode_surface.cpp:54 · gate ArduSub/mode.cpp:89-90
mode_surftrak.cpp (ModeSurftrak) | PNT (no horiz-GPS gate) ✓ | requires_GPS()=false, but consumes PNT here (pos_control ×3; e.g. altitude pos_control / optical-flow / optional position). | ArduSub/mode.h:201 · use ArduSub/mode_surftrak.cpp:91 · gate ArduSub/mode.cpp:89-90

## Slide 233
PROVENANCE · THE AUDIT’S OWN GUARANTEE
Provenance, in the audit’s own words
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
QUOTED FROM THE AUDIT’S EXECUTIVE SUMMARY
“Provenance. This Executive Summary is derived entirely from the findings already catalogued in this document — the numbered tables, the instance mapping and the registers that follow — and no new static analysis of the ArduPilot codebase was performed to produce it. Every figure above is a reconciled total of that catalog, and every cited path:line reference in this document is unchanged: none was re-derived, re-scored or re-verified for this summary.”
WHAT THAT MEANS FOR THIS DECK
This deck adds no finding, no metric and no count: every figure on every slide is a figure the audit states, and every row is the audit’s row.
No cited path:line reference was re-derived, re-scored or re-verified for this deck, and the audit’s line-number-basis notes are quoted, not reconciled.
The audit’s own flag tokens, [FIX F*] markers and AAP cross-references are transcribed exactly as printed, including where their referents lie outside the document.
The source PDF is unchanged: it was read, never rewritten, re-rendered or regenerated.

## Slide 234
COVERAGE RECONCILIATION · SOURCE-TO-DECK COVERAGE
Coverage reconciliation
Every construct in the source, the figure the audit states for it, and the slides that carry it. Read across a row to check the audit’s own figure against the slides that represent it.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Source construct | Axis | Stated by the audit | Deck coverage | Slides
Audit-Discipline Flags — taxonomy with the audit’s stated counts | Severity | 5 | 5 | 16
Flag [SHARED-STRUCT] — every token occurrence, catalog-wide | Severity | 19 | in full | 4, 16–19
Flag [DUPLICATED] — every token occurrence, catalog-wide | Severity | 36 | in full | 4, 16, 20–23
Flag [CIRCULAR] — every token occurrence, catalog-wide | Severity | 8 | in full | 4, 16, 24–25
Flag [MULTI-CATEGORY] — every token occurrence, catalog-wide | Severity | 7 | in full | 4, 16, 26–27
Flag [ABSENT] — every token occurrence, catalog-wide | Severity | 30 | in full | 4, 16, 28–30, 212, 214–215, 220–222, 224–226, 228–232
The two touch-points named in superlative risk language | Severity | 2 | 2 | 31
Table 1 — Core Positioning — every catalogued row | Group 1 | 26 | 26 | 33–37
Table 1 — Code Snippet (5-10 lines) — every cell, verbatim | Group 1 | 26 | 26 | 38–51
Where a row names a single flag token, Stated by the audit is a token-occurrence figure: it counts occurrences of that token in the audit’s text, not the rows listed on the severity axis. The corpus is the Notes of every main row and every Layer 2 chain, the Legend entry that defines the flag and, for [ABSENT], the Coverage register’s checked absences, so the Slides column locates the Legend, the flags table, the severity-axis listing and, for [ABSENT], the register.

## Slide 235
COVERAGE RECONCILIATION · SOURCE-TO-DECK COVERAGE
Coverage reconciliation (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Source construct | Axis | Stated by the audit | Deck coverage | Slides
Table 1a — Layer 1 direct edges — every typed edge | Group 1 | 26 | 26 | 52–54
Table 1a — Layer 1 Code Snippet — every cell, verbatim | Group 1 | 26 | 26 | 55–67
Table 1a — Layer 2 transitive chains — every chain | Group 1 | 26 | 26 | 68–77
Table 2 — Core Navigation — every catalogued row | Group 1 | 28 | 28 | 79–85
Table 2 — Code Snippet (5-10 lines) — every cell, verbatim | Group 1 | 28 | 28 | 86–99
Table 2a — Layer 1 direct edges — every typed edge | Group 1 | 28 | 28 | 100–102
Table 2a — Layer 1 Code Snippet — every cell, verbatim | Group 1 | 28 | 28 | 103–116
Table 2a — Layer 2 transitive chains — every chain | Group 1 | 28 | 28 | 117–121
Table 3 — Core Timing — every catalogued row | Group 1 | 9 | 9 | 123–124
Table 3 — Code Snippet (5-10 lines) — every cell, verbatim | Group 1 | 9 | 9 | 125–129
Table 3a — Layer 1 direct edges — every typed edge | Group 1 | 9 | 9 | 130–131
Table 3a — Layer 1 Code Snippet — every cell, verbatim | Group 1 | 9 | 9 | 132–136
Table 3a — Layer 2 transitive chains — every chain | Group 1 | 9 | 9 | 137–138
Table 4 — Indirect Positioning — every catalogued row | Group 2 | 10 | 10 | 140–143
Table 4 — Code Snippet (5-10 lines) — every cell, verbatim | Group 2 | 10 | 10 | 144–149
Table 4a — Layer 1 direct edges — every typed edge | Group 2 | 10 | 10 | 150–151
Table 4a — Layer 1 Code Snippet — every cell, verbatim | Group 2 | 10 | 10 | 152–156
Table 4a — Layer 2 transitive chains — every chain | Group 2 | 10 | 10 | 157–158

## Slide 236
COVERAGE RECONCILIATION · SOURCE-TO-DECK COVERAGE
Coverage reconciliation (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Source construct | Axis | Stated by the audit | Deck coverage | Slides
Table 5 — Indirect Navigation — every catalogued row | Group 2 | 10 | 10 | 160–163
Table 5 — Code Snippet (5-10 lines) — every cell, verbatim | Group 2 | 10 | 10 | 164–169
Table 5a — Layer 1 direct edges — every typed edge | Group 2 | 10 | 10 | 170–171
Table 5a — Layer 1 Code Snippet — every cell, verbatim | Group 2 | 10 | 10 | 172–176
Table 5a — Layer 2 transitive chains — every chain | Group 2 | 10 | 10 | 177–178
Table 6 — Indirect Timing — every catalogued row | Group 2 | 11 | 11 | 180–186
Table 6 — Code Snippet (5-10 lines) — every cell, verbatim | Group 2 | 11 | 11 | 187–192
Table 6a — Layer 1 direct edges — every typed edge | Group 2 | 11 | 11 | 193–194
Table 6a — Layer 1 Code Snippet — every cell, verbatim | Group 2 | 11 | 11 | 195–199
Table 6a — Layer 2 transitive chains — every chain | Group 2 | 11 | 11 | 200–202
Layer 1 Dependency Type roll-up, every Layer 1 row | Roll-up | 4 | 4 | 203
Layer 2 Chain Depth ranges, one per sub-table | Roll-up | 6 | 6 | 204
PNT Instance Audit — every mapping row | Instance audit | 12 | 12 | 206–207
Coverage sub-register (1) — every entry | Coverage register | 4 | 4 | 212
Coverage sub-register (2) — every entry | Coverage register | 5 | 5 | 213
Coverage sub-register (3) — every entry | Coverage register | 10 | 10 | 214–215
Coverage sub-register (4) — every entry | Coverage register | 4 | 4 | 216–217
Coverage sub-register (5) — every entry | Coverage register | 2 | 2 | 218

## Slide 237
COVERAGE RECONCILIATION · SOURCE-TO-DECK COVERAGE
Coverage reconciliation (continued)
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Source construct | Axis | Stated by the audit | Deck coverage | Slides
Coverage sub-register (6) — every entry | Coverage register | 3 | 3 | 219
Coverage sub-register (7) — every entry | Coverage register | 29 | 29 | 220–224
Coverage sub-register (8) — every entry | Coverage register | 26 | 26 | 225–228
Coverage sub-register (9) — every entry | Coverage register | 14 | 14 | 229–230
Coverage sub-register (10) — every entry | Coverage register | 12 | 12 | 231–232

## Slide 238
COVERAGE RECONCILIATION · TOTALS
The totals, reconciled
Each total the audit states, beside the number of rows this deck actually carries.
Source: ArduPilot_PNT_Reference_Audit.pdf · audited HEAD 5b67e27b0a · read-only static-analysis catalog · every figure as stated
Reconciled total | As the audit states it | Deck coverage
Core references (Tables 1–3) | 63 | 63
Indirect references (Tables 4–6) | 31 | 31
Total catalogued main rows | 94 | 94
Evidence rows (main + Layer 1 + Layer 2) | 282 | 282
Main-row Code Snippet (5-10 lines) cells, verbatim | 94 | 94
Layer 1 Code Snippet cells, verbatim | 94 | 94
Coverage register entries | 109 | 109
Current → new service mapping rows | 12 | 12
EVERY COLUMN OF THE SOURCE TABLES, SET ON A SLIDE
Every column of every source table is carried on these slides, Code Snippet (5-10 lines) included: each main row and each Layer 1 edge has its own cell set out verbatim, one paragraph per source line, under the File Path and Line(s) the audit prints for it. Nothing is abbreviated, summarised or left at its citation.

## Slide 239
Every finding, exactly as catalogued
Both axes are the audit’s own: its Audit-Discipline Flags for severity, its Group and pillar structure for category.
Every figure printed here is a figure the audit states; every row keeps its own number, citation and Notes text.
The source of record stays exactly as it is: ArduPilot_PNT_Reference_Audit.pdf at audited HEAD 5b67e27b0a.
Blitzy
ArduPilot PNT (Positioning, Navigation, Timing) Reference Audit · 43 pages · 94 catalogued references · 282 evidence rows